## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.1
Overview of the Internet Architecture & Performance Metrics
Network Edge, Network Core, Packet vs Circuit Switching, Delay Models, Queuing Loss & Throughput Bottlenecks
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
1.1.1 The Internet: Structural Hierarchy
M1.1 INTERNET OVERVIEW
• The Internet: Network of Networks
A vast, distributed interconnection of billions of heterogeneous computing devices (end systems / hosts) running networked software.
• Network Edge
End systems (clients, servers, mobile, IoT devices) that generate and consume application data. Connected via Access Networks (DSL, FTTH, 4G/5G, Wi-Fi 6).
• Network Core
The mesh of interconnected packet switches (routers and link-layer switches) responsible for routing and forwarding data across global ISP tiers.
• ISP Tier Hierarchy
Tier-1 ISPs (global transit providers like Lumen, AT&T), connected via IXPs (Internet Exchange Points), supplying regional and local access ISPs.
• Protocols & Standards
Network protocols define message format, ordering, transmission rules, and error handling. Governed by IETF RFCs and IEEE standards.
Key Structural Layers
→ Tier-1 ISPs: Global backbone
→ IXPs: Free/peered routing exchange
→ Regional ISPs: Connect local access
→ Access Nets: DSL, PON/Fiber, Wireless
→ End Systems: Run user applications
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
1.1.2 Switching Paradigms: Packet vs Circuit Switching
M1.1 SWITCHING COMPARISON
Packet Switching (Internet)
• Data Unit: Discrete chunks called packets (Header + Payload)
• Multiplexing: Statistical Multiplexing — resources allocated on demand
• Link Utilization: High efficiency; handles bursty internet traffic seamlessly
• Delays & Loss: Queuing delay occurs; buffers drop packets on congestion
• State Maintenance: Stateless core routers; adaptive per-packet dynamic routing
Circuit Switching (Legacy PSTN)
• Data Unit: Continuous bit stream over reserved physical channel
• Multiplexing: Fixed allocation via FDM (Frequency) or TDM (Time) slots
• Link Utilization: Low; reserved bandwidth wasted during idle/silent periods
• Delays & Loss: Zero queuing delay; calls blocked if no circuit available
• State Maintenance: Dedicated call setup and teardown state in every switch
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
1.1.3 Mathematical Delay Models in Packet Networks
M1.1 NODAL DELAY
• Total Nodal Delay ($d_{nodal}$)
Sum of 4 fundamental delay components at each intermediate router hop: $d_{nodal} = d_{proc} + d_{queue} + d_{trans} + d_{prop}$.
• Nodal Processing Delay ($d_{proc}$)
Time taken by router CPU to inspect packet header, compute bit checksums, and determine output interface (microseconds).
• Queuing Delay ($d_{queue}$)
Time packet waits inside output buffer queue before transmission. Governed by Traffic Intensity $I = (L \cdot a) / R$ ($L$ = bits, $a$ = arrival rate, $R$ = bandwidth).
• Transmission Delay ($d_{trans}$)
Time required to push all $L$ bits of the packet onto the link at rate $R$: $d_{trans} = L / R$ seconds.
• Propagation Delay ($d_{prop}$)
Time for a physical bit to travel through the physical medium over distance $d$ at speed $s \approx 2 \times 10^8$ m/s in copper/fiber: $d_{prop} = d / s$ seconds.
• Packet Loss & Throughput
When arriving traffic exceeds buffer capacity, packet drop occurs. End-to-end throughput is bottlenecked by the minimum link capacity along the transmission path.
Delay Formulas
→ d_nodal = d_proc + d_queue + d_trans + d_prop
→ d_trans = L / R (sec)
→ d_prop = d / s (sec)
→ Traffic Intensity: I = (L * a) / R
→ If I -> 1: Queuing delay -> infinity
→ Bottleneck Throughput = min(R1, R2, ...)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
1.1.4 Worked KTU Numerical: Delay & Throughput
M1.1 WORKED PROBLEM
📌 KTU Numerical Problem Statement
A 1500-byte packet is transmitted over a 100 km fiber link with transmission rate R = 10 Mbps. Propagation speed in fiber is s = 2 * 10^8 m/s. Nodal processing delay is 5 microseconds and the router queue currently holds 2 packets of 1500 bytes each. Calculate: (a) Transmission delay, (b) Propagation delay, (c) Queuing delay, (d) Total nodal delay.
📐 Governing Formulas & Principles:
• L = 1500 bytes = 1500 * 8 = 12,000 bits
• R = 10 Mbps = 10 * 10^6 bps
• d = 100 km = 10^5 m, s = 2 * 10^8 m/s
• d_trans = L / R, d_prop = d / s, d_queue = 2 * (L / R)
📝 Step-by-Step Derivation & Solution
Step 1: d_trans = 12,000 / 10^7 = 1.2 * 10^-3 s = 1.2 ms
Step 2: d_prop = 10^5 / (2 * 10^8) = 0.5 * 10^-3 s = 0.5 ms
Step 3: d_queue = 2 * 1.2 ms = 2.4 ms (2 packets ahead in queue)
Step 4: d_proc = 5 microseconds = 0.005 ms
Step 5: d_nodal = 0.005 + 2.4 + 1.2 + 0.5 = 4.105 ms
✅ FINAL ANSWER: Total Nodal Delay = 4.105 ms (Queuing delay is dominant)
💡 Exam Tip: In university exams, always convert bytes to bits (multiply by 8) before dividing by transmission rate R (bps).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 6
🎯 Exam Booster & Review: Internet Architecture & Delay Models
M1.1
📚 KTU High-Yield Questions (K2 / K3 Apply)
Q: Differentiate between packet switching and circuit switching with respect to bandwidth utilization, delays, and state maintenance. (7 Marks)
Q: Derive the four components of nodal delay in packet-switched networks with mathematical equations and units. (7 Marks)
Q: Explain statistical multiplexing and explain why traffic intensity I > 1 causes buffer overflow and packet loss. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Packet switching enables statistical multiplexing without dedicated circuits.
✔ Transmission delay (L/R) depends on bandwidth; Propagation delay (d/s) depends on distance.
✔ Queuing delay grows non-linearly as traffic intensity I = (L*a)/R approaches 1.
✔ End-to-end throughput is always throttled by the bottleneck link on the path.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET