## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.2
Protocol Layering & Network Models
Layering Principles, OSI 7-Layer Reference Model, TCP/IP 5-Layer Stack, PDU Encapsulation & Addressing Hierarchy
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
1.2.1 Principles of Layered Network Architecture
M1.2 PROTOCOL LAYERING
• Modularity & Abstraction
Dividing the massive complexity of network communication into decoupled functional layers. Each layer provides well-defined services to the layer above.
• Layer Independence
The internal implementation of a layer protocol can be completely modified or replaced without affecting adjacent layers as long as the layer interface remains unchanged.
• Encapsulation at Sender
Data moves top-down; each layer adds its own Protocol Header (and L2 adds a trailer) containing control metadata (addresses, sequence numbers, checksums).
• Decapsulation at Receiver
Data moves bottom-up; each layer processes and strips its corresponding header, passing the demultiplexed payload to the upper layer.
• Protocol Data Unit (PDU) Terminology
L5: Message (App) -> L4: Segment (TCP) / Datagram (UDP) -> L3: Packet / Datagram (IP) -> L2: Frame (Ethernet/Wi-Fi) -> L1: Raw Bit Stream.
Benefits of Layering
→ Simplifies system design
→ Standardizes interfaces
→ Enables multi-vendor hardware
→ Isolates layer troubleshooting
→ Facilitates protocol evolution
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
1.2.2 Comprehensive Architecture: OSI 7-Layer vs TCP/IP Stack
M1.2 OSI VS TCP/IP
OSI 7-Layer Model (ISO Conceptual)
• 7. Application: User applications & network services (HTTP, DNS)
• 6. Presentation: Data formatting, compression, encryption/decryption
• 5. Session: Dialog management, token coordination, checkpoints
• 4. Transport: End-to-end reliability, flow control, port addressing
• 3. Network: Logical host addressing (IP) & packet routing
• 2. Data Link: Node-to-node frame transfer & MAC error control
• 1. Physical: Unstructured bit transmission over raw copper/fiber/air
TCP/IP 5-Layer Internet Stack (Practical)
• 5. Application: Integrates OSI L7, L6, L5; protocols: HTTP, SMTP, DNS
• 4. Transport: Process-to-process multiplexing: TCP (reliable) & UDP
• 3. Network (Internet): Host-to-host delivery across networks: IPv4, IPv6, ICMP
• 2. Data Link: Hardware framing, MAC addressing: Ethernet, 802.11
• 1. Physical: Signals, voltages, optical pulses, RF frequencies
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
1.2.3 Addressing Hierarchy & PDU Encapsulation
M1.2 ADDRESSING HIERARCHY
• Application Layer Addressing
Uniform Resource Identifiers (URIs), Domain Names (FQDNs), and standardized Port Numbers.
• Transport Layer Addressing (Port Numbers)
16-bit Port Number (0 - 65,535). Well-known ports (0-1023: HTTP 80, HTTPS 443, SSH 22), Registered (1024-49151), Dynamic/Private (49152-65535).
• Network Layer Addressing (IP Addresses)
Logical 32-bit IPv4 or 128-bit IPv6 address used for global routing across subnets and autonomous systems.
• Data Link Layer Addressing (MAC Addresses)
Physical 48-bit (6-byte) EUI-48 hardware address burned into the NIC (e.g., `00:1A:2B:3C:4D:5E`). Used strictly on the local link.
• Cross-Layer Demultiplexing
L2 Frame Type field identifies L3 (IPv4 0x0800, ARP 0x0806) -> L3 Protocol field identifies L4 (TCP 6, UDP 17) -> L4 Port identifies L5 application.
Addressing Summary
→ Process ID: 16-bit Port Number
→ Host ID: 32-bit / 128-bit IP
→ NIC ID: 48-bit MAC Address
→ L2 Type 0x0800 -> IPv4
→ L3 Protocol 6 -> TCP
→ L3 Protocol 17 -> UDP
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: Protocol Layering & Network Models
M1.2
📚 KTU High-Yield Questions (K2 Understand)
Q: Compare the OSI 7-Layer model with the TCP/IP 5-Layer stack. Explain why the Presentation and Session layers are merged in TCP/IP. (8 Marks)
Q: Illustrate the step-by-step PDU encapsulation and decapsulation process across all layers with a neat labeled diagram. (7 Marks)
Q: Explain the three-level addressing hierarchy (Port, IP, MAC) and describe how demultiplexing occurs at each layer. (6 Marks)
💡 Critical Conceptual Takeaways
✔ OSI is a conceptual model; TCP/IP is the practical architecture implemented across the Internet.
✔ Headers prepend metadata: Port at L4, IP at L3, MAC and CRC FCS trailer at L2.
✔ L2 MAC changes at every router hop; L3 Source and Destination IP remain unchanged end-to-end (without NAT).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET