## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.9
Application Layer Case Study: CDNs & Video Streaming
Content Distribution Networks (CDNs), DNS Redirection, Edge Server Placement, DASH (Dynamic Adaptive Streaming over HTTP)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
1.9.1 Content Distribution Networks (CDNs)
M1.9 CDN ARCHITECTURE
• The Web Scale Problem
Serving massive video traffic (YouTube, Netflix) from a single mega data center causes single point of failure, network congestion, long-distance delay, and repeated link traversals.
• CDN Philosophy
Deploy thousands of geographically distributed server clusters (Points of Presence - PoPs) at edge ISPs across the globe. Store replicated video copies close to end users.
• Server Placement Philosophies
1. Enter Deep (Akamai): Deploy clusters inside thousands of access ISPs close to users. 2. Bring Home (Limelight): Deploy fewer large clusters at Tier-1 PoPs interconnected by private backbone.
• CDN DNS Redirection
When user requests `video.netflix.com`, authoritative DNS intercepts the request and returns a CNAME pointing to CDN domain. CDN's DNS resolver uses client IP to return the IP address of the geographically closest edge cache server.
CDN Benefits
→ Ultra-low latency to users
→ Reduces ISP transit costs
→ Absorbs DDoS attacks
→ High availability & redundancy
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
1.9.2 DASH: Dynamic Adaptive Streaming over HTTP
M1.9 DASH VIDEO
• Video Encoding & Chunks
Video is pre-encoded at multiple quality/bitrate versions (e.g., 360p 500 kbps, 720p 2 Mbps, 1080p 5 Mbps, 4K 15 Mbps) and partitioned into small chunks (2 to 10 seconds each).
• MPD (Media Presentation Description)
An XML manifest file listing the URLs and bitrates for all chunks across every quality level.
• Client-Side Dynamic Adaptation
The client player continuously monitors available download bandwidth and buffer occupancy. It dynamically requests high-quality chunks when bandwidth is ample, and gracefully steps down to lower bitrates to avoid playback stalling.
• Transport over HTTP/TCP
Streams over standard HTTP/HTTPS port 80/443, effortlessly traversing firewalls and NATs without requiring proprietary streaming server protocols.
DASH Algorithm
→ MPD Manifest: Lists chunks & bitrates
→ Client measures throughput
→ If buffer high -> Request 4K/1080p
→ If bandwidth drops -> Request 720p
→ Zero playback interruption
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: CDN & Streaming Case Study
M1.9
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain how Content Distribution Networks (CDNs) use DNS redirection to route user requests to the optimal edge server. (8 Marks)
Q: Describe the architecture and working of Dynamic Adaptive Streaming over HTTP (DASH). (7 Marks)
💡 Critical Conceptual Takeaways
✔ CDNs bring content close to users, cutting down WAN transit delays and backbone congestion.
✔ DNS CNAME redirection enables real-time dynamic traffic routing based on network conditions.
✔ DASH shifts streaming intelligence to the client, adapting video bitrate in real time.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET