## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.2
Transport Protocols & User Datagram Protocol (UDP)
UDP Segment Header Structure, 16-Bit 1's Complement Checksum with Pseudo-Header, UDP Applications & Use Cases
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
2.1.2.1 UDP Protocol Architecture & 8-Byte Header
M2.1.2 UDP ARCHITECTURE
• UDP Characteristics (RFC 768)
Connectionless, unreliable, lightweight, message-oriented transport protocol. Provides bare minimum services: process multiplexing and optional error checking.
• Why Use UDP?
1. No connection establishment delay (0-RTT), 2. No connection state at server, 3. Small header overhead (8 bytes vs TCP 20 bytes), 4. Unregulated send rate (no congestion throttling).
• UDP 8-Byte Header Format (32-bit width)
Source Port (16 bits) | Destination Port (16 bits) \n Length (16 bits, header + payload in bytes) | Checksum (16 bits).
• Message Boundary Preservation
UDP sends data in discrete datagrams. If sender writes 500 bytes twice, receiver reads 500 bytes twice (preserves message boundaries, unlike TCP byte stream).
Header Breakdown
→ Source Port: 16 bits
→ Destination Port: 16 bits
→ Length: 16 bits (Min 8 B)
→ Checksum: 16 bits
→ Total Header: Exactly 8 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
2.1.2.2 UDP 16-Bit 1's Complement Checksum Calculation
M2.1.2 CHECKSUM CALCULATION
📌 KTU Numerical Problem Statement
Compute the UDP checksum for three 16-bit words: Word 1 = 0x66B4 (0110 0110 1011 0100), Word 2 = 0x5555 (0101 0101 0101 0101), Word 3 = 0x8F0C (1000 1111 0000 1100). Show wraparound carry addition and 1's complement inversion. Also explain how the receiver verifies checksum integrity.
📐 Governing Formulas & Principles:
• Step 1: Sum 16-bit words using standard binary addition.
• Step 2: If sum produces a 17th bit (carry overflow), wrap it around and add to the least significant bit.
• Step 3: Invert all bits (1's complement) to obtain the transmitted Checksum field.
• Receiver: Sums all received words including Checksum; valid result must be 0xFFFF (all 1s).
📝 Step-by-Step Derivation & Solution
Step 1: Sum Word 1 + Word 2: 0x66B4 + 0x5555 = 0xBC09 (1011 1100 0000 1001)
Step 2: Add Word 3: 0xBC09 + 0x8F0C = 0x14B15 (1 0100 1011 0001 0101 - Carry generated!)
Step 3: Wrap carry around: 0x4B15 + 1 = 0x4B16 (0100 1011 0001 0110)
Step 4: Take 1's complement (~0x4B16): 1011 0100 1110 1001 = 0xB4E9 (Checksum transmitted)
Step 5: Receiver Verification: 0x4B16 + 0xB4E9 = 0xFFFF (1111 1111 1111 1111 -> Verified Valid!)
✅ FINAL ANSWER: Transmitted Checksum = 0xB4E9 | Receiver sum = 0xFFFF
💡 Exam Tip: Note: UDP includes an IP Pseudo-Header (Source IP, Dest IP, Protocol 17, UDP Length) in checksum calculation to detect misrouted packets.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: UDP Protocol & Checksum
M2.1.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the UDP segment header format and explain all fields. Why is UDP header size fixed at 8 bytes? (6 Marks)
Q: Explain the step-by-step procedure for computing the UDP 16-bit 1's complement checksum. What is the role of the pseudo-header? (8 Marks)
Q: Why is UDP preferred over TCP for DNS queries, SNMP, and real-time gaming? (5 Marks)
💡 Critical Conceptual Takeaways
✔ UDP header is minimal (8 bytes) with Source Port, Dest Port, Length, and Checksum.
✔ Checksum calculation wraps around carry bits and inverts result for easy receiver verification (0xFFFF).
✔ UDP avoids TCP connection overhead and latency fluctuations from retransmissions.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET