## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.3
Transmission Control Protocol (TCP) Architecture
TCP 20-Byte Header Format, 3-Way Handshake Connection Setup, 4-Way Connection Teardown (TIME_WAIT 2MSL), Sequence/ACK Mechanics
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
2.1.3.1 TCP Header Architecture (RFC 793 / 9293)
M2.1.3 TCP HEADER
• Connection-Oriented Byte Stream
TCP provides full-duplex, reliable, sequenced byte-stream transfer between communicating processes.
• Header Format (20 to 60 Bytes)
Source Port (16b) | Destination Port (16b) \n Sequence Number (32b: byte-stream offset) \n Acknowledgment Number (32b: next expected byte) \n Data Offset (4b: header length in 32-bit words) | Reserved (4b) | Flags (8b) | Window Size (16b) \n Checksum (16b) | Urgent Pointer (16b) \n Options (0 to 40 bytes: MSS, Window Scale, SACK, Timestamps).
• TCP Control Flags
SYN (Establish connection), ACK (Ack valid), FIN (Close connection), RST (Reset/abort connection), PSH (Push data immediately to app), URG (Urgent pointer active), ECE & CWR (Explicit Congestion Notification).
• Cumulative Acknowledgment
TCP Ack number $N$ indicates the receiver has successfully received all contiguous bytes up to $N-1$ and is expecting byte $N$.
TCP Control Flags
→ SYN: Connection request
→ ACK: Acknowledgment field
→ FIN: Graceful teardown
→ RST: Reset connection
→ PSH: Push buffer to app
→ URG: Out-of-band data
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
2.1.3.2 Connection Lifecycle: 3-Way Handshake vs 4-Way Teardown
M2.1.3 TCP LIFECYCLE
3-Way Handshake (Connection Setup)
• Step 1 (Client -> Server): Client sends `SYN = 1`, `Seq = x` (Initial Sequence Number $ISN_c$). Enters `SYN_SENT` state
• Step 2 (Server -> Client): Server allocates buffers, replies `SYN = 1`, `ACK = 1`, `Seq = y` ($ISN_s$), `Ack = x + 1`. Enters `SYN_RCVD`
• Step 3 (Client -> Server): Client sends `ACK = 1`, `Seq = x + 1`, `Ack = y + 1` (may piggyback initial application data). Enters `ESTABLISHED`
• SYN Flood Defense: TCP SYN Cookies prevent server memory exhaustion from bogus SYN requests
4-Way Connection Teardown (Graceful Close)
• Step 1 (Client -> Server): Client finishes sending, transmits `FIN = 1`, `Seq = u`. Enters `FIN_WAIT_1`
• Step 2 (Server -> Client): Server acknowledges with `ACK = 1`, `Ack = u + 1`. Enters `CLOSE_WAIT`; Client enters `FIN_WAIT_2`
• Step 3 (Server -> Client): Server finishes outstanding data, transmits `FIN = 1`, `Seq = v`. Enters `LAST_ACK`
• Step 4 (Client -> Server): Client replies `ACK = 1`, `Ack = v + 1`. Client enters `TIME_WAIT` for 2MSL (Maximum Segment Lifetime = 60-120s) before terminating to ensure final ACK delivery
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: TCP Connection Management
M2.1.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the complete TCP segment header format and explain all fields, especially Sequence Number, ACK Number, and Control Flags. (8 Marks)
Q: Illustrate the TCP 3-Way Handshake with sequence and acknowledgment numbers. Why is a 2-way handshake insufficient? (8 Marks)
Q: Explain the purpose of the `TIME_WAIT` state and the 2MSL timer during TCP connection termination. (5 Marks)
💡 Critical Conceptual Takeaways
✔ TCP Sequence number tracks the byte offset of transmitted data; ACK number represents the next expected byte.
✔ 3-way handshake is mandatory to synchronize Initial Sequence Numbers (ISNs) bi-directionally and verify full-duplex connectivity.
✔ `TIME_WAIT` (2MSL) guarantees that any lingering duplicate packets in the network expire before the socket is reused.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET