## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.4
TCP Flow & Congestion Control Mechanisms
Sliding Window Flow Control, Silly Window Syndrome, Congestion Window (cwnd), Slow Start, AIMD, Fast Retransmit, TCP Tahoe vs Reno
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
2.1.4.1 Flow Control & Silly Window Syndrome
M2.1.4 FLOW CONTROL
• Flow Control Goal
Matches the sender's transmission rate to the receiver's consumption rate to prevent receiver buffer overflow.
• Receive Window (`rwnd`) Mechanics
Receiver advertises remaining buffer space via `rwnd` field in TCP header. Sender ensures: $\text{LastByteSent} - \text{LastByteAcked} \le \min(\text{cwnd}, \text{rwnd})$.
• Zero-Window Probing
When receiver buffer is full (`rwnd = 0`), sender stops transmitting but periodically sends 1-byte probe segments to force receiver to return window update ACKs.
• Silly Window Syndrome (SWS)
Occurs when data is transmitted in tiny chunks (1 byte payload + 40 bytes header = 97.5% overhead).
• SWS Solutions
1. **Nagle's Algorithm (Sender-side)**: Send first small segment; buffer subsequent data until all previous data is ACKed or MSS is reached. 2. **Clark's Solution (Receiver-side)**: Receiver advertises `rwnd = 0` until buffer space is at least MSS or 50% buffer capacity.
Key Variables
→ rwnd: Receiver buffer limit
→ cwnd: Network congestion limit
→ Effective Win = min(cwnd, rwnd)
→ Nagle's: Buffers small writes
→ Clark's: Suppresses tiny rwnd
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
2.1.4.2 Congestion Control: TCP Tahoe vs TCP Reno
M2.1.4 TAHOE VS RENO
TCP Tahoe (Legacy)
• Slow Start Phase: Begins with `cwnd = 1 MSS`. Increases `cwnd` exponentially: doubles every RTT (`cwnd += 1 MSS` per ACK received)
• Congestion Avoidance: When `cwnd >= ssthresh`, transitions to AIMD: increases `cwnd` linearly by 1 MSS per RTT
• On Loss Detection (Timeout or 3 Dup ACKs): 1. `ssthresh = cwnd / 2` \n 2. Drops `cwnd = 1 MSS` (always resets to slow start)
• Performance: Severe throughput collapse upon any single packet loss
TCP Reno (Standard)
• Slow Start & Congestion Avoidance: Identical to Tahoe during normal growth
• On Timeout Loss: Severe congestion: `ssthresh = cwnd / 2`, `cwnd = 1 MSS` (resets to Slow Start)
• On 3 Duplicate ACKs (Fast Retransmit): Mild congestion: Retransmits lost segment immediately without waiting for retransmission timer to expire
• Fast Recovery Phase: Skips slow start! Sets `ssthresh = cwnd / 2`, sets `cwnd = ssthresh + 3 MSS`, continues linear AIMD growth
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
2.1.4.3 Worked KTU Numerical: TCP Congestion Window Evolution
M2.1.4 WORKED PROBLEM
📌 KTU Numerical Problem Statement
A TCP Reno connection has ssthresh = 16 MSS. Starting at RTT 1 with cwnd = 1 MSS in Slow Start: (a) Trace cwnd values up to RTT 8. (b) At RTT 8, three duplicate ACKs are received. Calculate new ssthresh and cwnd for RTT 9 and RTT 10 under Fast Recovery.
📐 Governing Formulas & Principles:
• Slow Start: cwnd doubles every RTT until ssthresh is reached.
• Congestion Avoidance (AIMD): cwnd increases by +1 MSS per RTT.
• Fast Retransmit / Fast Recovery (3 Dup ACKs): ssthresh_new = cwnd / 2, cwnd_new = ssthresh_new.
📝 Step-by-Step Derivation & Solution
Step 1: RTT 1: cwnd = 1 MSS (Slow Start)
Step 2: RTT 2: cwnd = 2 MSS | RTT 3: cwnd = 4 MSS | RTT 4: cwnd = 8 MSS | RTT 5: cwnd = 16 MSS (ssthresh reached)
Step 3: RTT 6: cwnd = 17 MSS (AIMD Linear) | RTT 7: cwnd = 18 MSS | RTT 8: cwnd = 19 MSS
Step 4: At RTT 8, 3 Dup ACKs occur: ssthresh_new = 19 / 2 = 9.5 -> 9 MSS.
Step 5: RTT 9: Under TCP Reno Fast Recovery, cwnd = 9 MSS. RTT 10: cwnd = 10 MSS (continues linear AIMD).
✅ FINAL ANSWER: RTT 8: 19 MSS -> Loss -> RTT 9: cwnd = 9 MSS, ssthresh = 9 MSS
💡 Exam Tip: If loss was caused by Timeout instead of 3 Dup ACKs, cwnd would drop to 1 MSS.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: TCP Flow & Congestion Control
M2.1.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain TCP Sliding Window flow control and how the receiver window `rwnd` prevents buffer overrun. (7 Marks)
Q: What is Silly Window Syndrome? Explain Nagle's algorithm and Clark's solution with examples. (8 Marks)
Q: Compare TCP Tahoe and TCP Reno congestion control algorithms with a neat graph plotting `cwnd` versus Transmission RTTs. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Flow control is receiver-driven (`rwnd`); Congestion control is network-driven (`cwnd`).
✔ Effective transmission window is the minimum of `cwnd` and `rwnd`.
✔ TCP Reno avoids slow start upon 3 duplicate ACKs via Fast Retransmit and Fast Recovery.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET