## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.1
Network Layer Architecture & Router Design
Data Plane (Forwarding) vs Control Plane (Routing), Datagram Networks vs Virtual Circuits, Router Fabrics & Buffer Queuing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
2.2.1.1 Network Layer: Data Plane vs Control Plane
M2.2.1 NETWORK ARCHITECTURE
• Network Layer Core Mission
Achieving end-to-end host-to-host packet delivery across multiple heterogeneous intermediate networks.
• Data Plane (Forwarding)
Local, per-router action. Takes a packet arriving on an input link interface and moves it to the appropriate output link interface in nanoseconds. Implemented in high-speed hardware ASIC/TCAM.
• Control Plane (Routing)
Network-wide logic. Determines the end-to-end global path that packets take from source to destination. Implemented in software routing algorithms (OSPF, RIP, BGP) or centralized SDN controllers.
• Service Models
Internet uses Best-Effort Service Model: no guarantees on delivery, delay, bandwidth, or ordering. Simplicity in the network core pushed intelligence to end hosts.
Plane Separation
→ Data Plane: Local forwarding (ASIC/Hardware)
→ Control Plane: Global routing (Software/OSPF)
→ Nanosecond speed in Data Plane
→ Millisecond speed in Control Plane
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
2.2.1.2 Network Models: Datagram vs Virtual Circuit
M2.2.1 DATAGRAM VS VC
Datagram Networks (Internet IP)
• Connection Setup: No connection setup phase; packets injected immediately
• Addressing: Packets carry full global 32-bit/128-bit Source and Destination IP
• Routing Path: Each packet routed independently; successive packets may follow different paths
• Router State: Stateless routers; failure of a link triggers automatic rerouting
• Complexity: Pushed to network edge end hosts
Virtual Circuit Networks (ATM / Frame Relay)
• Connection Setup: Mandatory end-to-end signaling setup before data transfer
• Addressing: Packets carry small local Virtual Circuit Identifier (VCI)
• Routing Path: All packets in a connection follow the exact same fixed virtual path
• Router State: Routers maintain per-connection state tables; link failure drops VC
• Complexity: Heavy complexity in network core switches
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Network Layer Architecture
M2.2.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Differentiate between the Data Plane and Control Plane of the Network Layer. (6 Marks)
Q: Compare Datagram networks and Virtual Circuit networks with respect to connection setup, addressing, and router state. (8 Marks)
Q: Describe the internal architecture of a modern high-speed router (Input Ports, Switching Fabric, Output Ports). (7 Marks)
💡 Critical Conceptual Takeaways
✔ Forwarding is local and hardware-based; Routing is global and software-based.
✔ Internet uses datagram packet switching with stateless routers for maximum resilience.
✔ Crossbar switching fabrics eliminate internal shared bus contention in high-speed routers.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET