## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.2
IPv4 Addressing, Subnetting, CIDR & NAT
IPv4 20-60 Byte Header, Fragmentation & Reassembly, Classless Addressing (CIDR), Subnet Design, NAT/PAT, ICMP Protocol
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
2.2.2.1 IPv4 Header Format & Fragmentation
M2.2.2 IPV4 HEADER
• IPv4 Header Structure (20 to 60 Bytes)
Version (4b: 4) | IHL (4b: Header length in 32-bit words, min 5 = 20B) | DSCP/ECN (8b: QoS) | Total Length (16b: Header + Payload, max 65535B) \n Identification (16b) | Flags (3b: Reserved, DF, MF) | Fragment Offset (13b: measured in 8-byte units) \n TTL (8b: Time-to-Live, decremented per hop) | Protocol (8b: ICMP=1, TCP=6, UDP=17) | Header Checksum (16b) \n Source IP (32b) \n Destination IP (32b) \n Options (0-40B).
• Fragmentation Fields
**Identification**: Identifies fragments belonging to same original datagram. **DF (Don't Fragment)**: If set to 1, router drops packet if larger than MTU. **MF (More Fragments)**: 1 for all fragments except the final one (0). **Fragment Offset**: Byte offset divided by 8.
• Reassembly
Occurs strictly at the final destination host before delivering to the transport layer.
Key Header Fields
→ IHL: Header words (x4 bytes)
→ Total Length: Max 65,535 B
→ TTL: Prevents routing loops
→ Protocol: 6=TCP, 17=UDP, 1=ICMP
→ Offset unit = 8 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
2.2.2.2 Worked KTU Numerical: IPv4 Fragmentation
M2.2.2 FRAGMENTATION PROBLEM
📌 KTU Numerical Problem Statement
An IPv4 datagram with Total Length = 4000 bytes (20-byte IP header + 3980 bytes payload) arrives at a router whose outgoing link has Maximum Transmission Unit MTU = 1500 bytes. Calculate the Total Length, Payload Length, MF flag, and Fragment Offset for all resulting fragments.
📐 Governing Formulas & Principles:
• MTU = 1500 bytes (Max payload per fragment = 1500 - 20 = 1480 bytes).
• 1480 is divisible by 8 (1480 / 8 = 185) -> Valid maximum payload per fragment.
• Total payload to fragment = 3980 bytes.
• Fragment Offset = Total previous payload bytes divided by 8.
📝 Step-by-Step Derivation & Solution
Step 1: Frag 1: Header = 20 B, Payload = 1480 B, Total Length = 1500 B, MF = 1, Offset = 0 / 8 = 0
Step 2: Frag 2: Header = 20 B, Payload = 1480 B, Total Length = 1500 B, MF = 1, Offset = 1480 / 8 = 185
Step 3: Remaining payload = 3980 - 1480 - 1480 = 1020 B.
Step 4: Frag 3: Header = 20 B, Payload = 1020 B, Total Length = 1040 B, MF = 0 (last fragment!), Offset = 2960 / 8 = 370
✅ FINAL ANSWER: Frag 1: Len 1500, MF=1, Off=0 | Frag 2: Len 1500, MF=1, Off=185 | Frag 3: Len 1040, MF=0, Off=370
💡 Exam Tip: Always verify that Fragment Offset values are integer multiples of 8 bytes!
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
2.2.2.3 Worked KTU Numerical: CIDR Subnetting
M2.2.2 SUBNETTING PROBLEM
📌 KTU Numerical Problem Statement
An organization is allocated the block `200.50.16.0/24`. Design 4 equal-sized subnets. For each subnet, specify: (a) Subnet Mask, (b) Network Address, (c) Usable Host Range, (d) Direct Broadcast Address, (e) Maximum usable hosts.
📐 Governing Formulas & Principles:
• Given /24 network: 8 host bits (256 addresses).
• To create 4 subnets: Need 2 subnet bits (2^2 = 4). New prefix = /24 + 2 = /26.
• Block size per subnet = 256 / 4 = 64 addresses.
• Usable hosts per subnet = 2^(32 - 26) - 2 = 64 - 2 = 62 hosts.
📝 Step-by-Step Derivation & Solution
Step 1: Subnet Mask: 255.255.255.192 (/26)
Step 2: Subnet 1: Net = 200.50.16.0/26 | Hosts = 200.50.16.1 to 200.50.16.62 | Broadcast = 200.50.16.63
Step 3: Subnet 2: Net = 200.50.16.64/26 | Hosts = 200.50.16.65 to 200.50.16.126 | Broadcast = 200.50.16.127
Step 4: Subnet 3: Net = 200.50.16.128/26 | Hosts = 200.50.16.129 to 200.50.16.190 | Broadcast = 200.50.16.191
Step 5: Subnet 4: Net = 200.50.16.192/26 | Hosts = 200.50.16.193 to 200.50.16.254 | Broadcast = 200.50.16.255
✅ FINAL ANSWER: 4 Subnets of /26 mask (255.255.255.192), each accommodating 62 usable hosts
💡 Exam Tip: First address is Network ID; Last address is Directed Broadcast; both cannot be assigned to hosts.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: IPv4, CIDR & NAT
M2.2.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the complete IPv4 header format and explain all fields with numerical significance. (8 Marks)
Q: Explain the working of Network Address Translation (NAT) and Port Address Translation (PAT) with translation table examples. (7 Marks)
Q: What is ICMP? Explain its role in error reporting (Destination Unreachable, Time Exceeded) and diagnostic tools (`ping`, `traceroute`). (6 Marks)
💡 Critical Conceptual Takeaways
✔ IPv4 fragmentation uses ID, Flags (DF, MF), and Offset in 8-byte blocks.
✔ CIDR replaces classful boundaries with arbitrary prefix lengths (/N) and Longest Prefix Matching.
✔ NAT allows private IP subnets (RFC 1918) to share a single public IP using port mapping tables.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET