## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.5
Next Generation IP: IPv6 Architecture
IPv6 128-Bit Addressing, 40-Byte Fixed Header, Extension Headers, IPv4 vs IPv6 Comparison, Transition Strategies (Dual Stack, Tunneling, NAT64)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
2.2.5.1 IPv6 Addressing & 40-Byte Fixed Header
M2.2.5 IPV6 ARCHITECTURE
• Motivation for IPv6
Exhaustion of the 32-bit IPv4 address space ($2^{32} \approx 4.3 \times 10^9$ addresses). IPv6 provides $2^{128} \approx 3.4 \times 10^{38}$ unique addresses.
• IPv6 Address Notation
8 groups of 4 hexadecimal digits separated by colons (e.g., `2001:0db8:85a3:0000:0000:8a2e:0370:7334`). Leading zeros omitted (`2001:db8:85a3::8a2e:370:7334`); `::` compresses consecutive zero blocks once.
• 40-Byte Fixed Header Format
Version (4b: 6) | Traffic Class (8b: QoS DSCP) | Flow Label (20b: identifies packet flow for non-default routing) \n Payload Length (16b: data + extension headers) | Next Header (8b: specifies upper layer or extension header) | Hop Limit (8b: decremented per hop, replaces TTL) \n Source IPv6 Address (128 bits / 16 bytes) \n Destination IPv6 Address (128 bits / 16 bytes).
• Key Structural Improvements
No header checksum (speeds up router processing), no in-network fragmentation (handled via Path MTU Discovery by end hosts), fixed 40-byte base size.
Header Breakdown
→ Fixed Header: Exactly 40 Bytes
→ Source IP: 128 bits (16 B)
→ Destination IP: 128 bits (16 B)
→ Hop Limit: Replaces TTL
→ Next Header: Chains extensions
→ Flow Label: 20-bit stream tagging
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
2.2.5.2 IPv4 vs IPv6 & Transition Strategies
M2.2.5 IPV4 VS IPV6
IPv4 vs IPv6 Header Comparison
• Address Size: IPv4: 32 bits (4 Bytes) vs IPv6: 128 bits (16 Bytes)
• Header Length: IPv4: Variable 20-60B (IHL field) vs IPv6: Fixed 40 Bytes
• Checksum: IPv4: 16-bit header checksum vs IPv6: Removed entirely
• Fragmentation: IPv4: Routers fragment packets vs IPv6: End systems only (PMTUD)
• Broadcast: IPv4: Broadcast supported vs IPv6: Replaced by Multicast & Anycast
IPv4 to IPv6 Migration Mechanisms
• Dual Stack: Nodes run both IPv4 and IPv6 protocol stacks simultaneously on all interfaces
• Tunneling (6to4 / Teredo): IPv6 datagrams encapsulated as payload inside IPv4 packets across legacy IPv4 transit networks
• Header Translation (NAT64/DNS64): Translates IPv6 packet headers directly to IPv4 headers for legacy server interoperation
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: IPv6 Architecture
M2.2.5
📚 KTU High-Yield Questions (K2 Understand)
Q: Draw the IPv6 fixed header format and explain all fields. How does it improve router forwarding performance over IPv4? (8 Marks)
Q: Compare IPv4 and IPv6 across addressing, header structure, fragmentation, and error checking. (8 Marks)
Q: Explain the three transition mechanisms from IPv4 to IPv6: Dual Stack, Tunneling, and NAT64. (7 Marks)
💡 Critical Conceptual Takeaways
✔ IPv6 fixed 40-byte header streamlines hardware ASIC forwarding.
✔ Extension headers (Hop-by-Hop, Routing, Fragment, ESP, AH) are daisy-chained via `Next Header`.
✔ Dual stack and encapsulation tunneling enable smooth evolutionary migration from IPv4.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET