## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.6
Quality of Service (QoS) & Traffic Shaping
QoS Metrics (Delay, Jitter, Loss), Traffic Policing vs Shaping, Leaky Bucket vs Token Bucket, Scheduling (FIFO, WFQ), DiffServ vs IntServ
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
2.2.6.1 Traffic Shaping: Leaky Bucket vs Token Bucket
M2.2.6 TRAFFIC SHAPING
Leaky Bucket Algorithm (Constant Output)
• Concept: A bucket with a hole at the bottom; incoming packets buffer up to bucket capacity $C$ and leak out at a strictly constant rate $\rho$
• Output Profile: Strictly constant, smooth output stream regardless of incoming burstiness
• Burst Handling: Eliminates bursts entirely; discards packets if bucket overflows
• Suitability: Constant Bit Rate (CBR) traffic like uncompressed voice
Token Bucket Algorithm (Burst-Tolerant)
• Concept: Tokens generate at rate $r$ tokens/sec up to max token capacity $b$. A packet of size $m$ bytes consumes $m$ tokens to transmit
• Output Profile: Allows short-term traffic bursts up to bucket size $b$ while enforcing average long-term rate $r$
• Burst Handling: Max burst transmission speed = link wire rate $R$ for duration $T = b / (R - r)$
• Suitability: Variable Bit Rate (VBR) video streaming and web traffic
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
2.2.6.2 Worked KTU Numerical: Token Bucket Burst Calculation
M2.2.6 TOKEN BUCKET NUMERICAL
📌 KTU Numerical Problem Statement
A token bucket has token arrival rate r = 2 MB/sec and token bucket capacity b = 16 MB. The transmission link wire rate is R = 10 MB/sec. Calculate: (a) Maximum burst duration at wire rate R, (b) Maximum total data transmitted during this burst period.
📐 Governing Formulas & Principles:
• Burst duration formula: T = b / (R - r)
• Where b = bucket size (MB), R = peak transmission rate (MB/s), r = token replenishment rate (MB/s).
• Total data transmitted during burst: D = R * T = (b * R) / (R - r).
📝 Step-by-Step Derivation & Solution
Step 1: b = 16 MB, R = 10 MB/s, r = 2 MB/s
Step 2: T = 16 / (10 - 2) = 16 / 8 = 2.0 seconds
Step 3: Total data transmitted = R * T = 10 MB/s * 2.0 s = 20 MB
Step 4: Verification: Initial tokens (16 MB) + Newly generated tokens in 2s (2 MB/s * 2s = 4 MB) = 20 MB.
✅ FINAL ANSWER: Max Burst Duration T = 2.0 seconds | Total Burst Data = 20 MB
💡 Exam Tip: After 2 seconds, the transmission rate drops strictly to the average token rate r = 2 MB/sec.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Quality of Service (QoS)
M2.2.6
📚 KTU High-Yield Questions (K3 Apply)
Q: Differentiate between Traffic Policing and Traffic Shaping with neat diagrams. (6 Marks)
Q: Compare Leaky Bucket and Token Bucket traffic shaping algorithms with equations and operating principles. (8 Marks)
Q: Explain Differentiated Services (DiffServ) architecture: Packet Classification, DSCP marking, and Per-Hop Behaviors (EF & AF). (7 Marks)
💡 Critical Conceptual Takeaways
✔ Leaky bucket produces rigid constant output; Token bucket permits regulated bursts.
✔ Weighted Fair Queuing (WFQ) guarantees minimum bandwidth shares to different service classes.
✔ DiffServ scales across WANs by classifying packets at boundary routers and using 6-bit DSCP markings.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET