## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.1
Data Link Layer Design & Framing Techniques
Node-to-Node Link Services, Character Count, Byte Stuffing (Flag/ESC), Bit Stuffing (HDLC), Physical Coding Violations
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.1.1 Data Link Layer Design & Link Abstraction
M3.1 FRAMING BASICS
• Node-to-Node Service Mission
Responsible for transferring datagrams from one node (host, router, switch) to an adjacent node over an individual physical communication link.
• Link Layer Responsibilities
1. **Framing**: Encapsulating L3 datagrams into L2 frames with header and trailer. 2. **Link Access**: MAC protocols coordinate shared medium access. 3. **Reliable Delivery**: Flow control and ARQ on error-prone wireless links. 4. **Error Detection & Correction**: Parity, Checksum, CRC, Hamming codes.
• Framing Methods Overview
1. Character Count, 2. Byte Stuffing (Character-oriented), 3. Bit Stuffing (Bit-oriented), 4. Physical Layer Coding Violations (e.g., Manchester invalid transitions).
Framing Taxonomy
→ Byte Count: Header count field
→ Byte Stuffing: Flag + ESC bytes
→ Bit Stuffing: 5 consecutive 1s rule
→ Physical Violations: Line coding
→ FCS: CRC trailer at end
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.1.2 Stuffing Techniques: Byte Stuffing vs Bit Stuffing
M3.1 STUFFING COMPARISON
Byte Stuffing (Character-Oriented Framing)
• Delimiter: Frame begins and ends with dedicated Flag Byte `FLAG` (e.g., `0x7E` in PPP)
• Escape Mechanism: If `FLAG` occurs inside payload data, sender inserts an Escape Byte `ESC` (`0x7D`) immediately before it
• ESC in Data: If `ESC` itself appears in data, sender escapes it with another `ESC` (`ESC ESC`)
• Receiver Action: Receiver strips any `ESC` byte and treats following byte as raw data
Bit Stuffing (Bit-Oriented Framing / HDLC)
• Delimiter Pattern: Frame delimited by 8-bit flag pattern `01111110` (`0x7E`) at start and end
• Sender Rule: Whenever sender encounters **5 consecutive 1s** in data stream (`11111`), it automatically stuffs a **`0` bit** immediately after it
• Receiver Rule: Whenever receiver detects 5 consecutive 1s: if 6th bit is `0`, it de-stuffs (discards) the `0`; if 6th bit is `1` and 7th is `0`, it recognizes `FLAG`
• Advantage: Completely arbitrary payload length; zero character-set dependency
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Data Link Layer Framing
M3.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the four framing methods used in the Data Link Layer with neat diagrams. (8 Marks)
Q: Given the data bit stream `01101111110111110010`, show the transmitted bit sequence after bit stuffing in HDLC. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Bit stuffing inserts a 0 after five consecutive 1s to prevent false flag detection.
✔ Byte stuffing uses escape characters (`ESC`) to preserve transparency in character protocols.
✔ Framing enables receivers to reliably locate the start and end of frames in raw bit streams.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET