## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.2
Data Link Control: Error Detection, Correction & Flow Control
Hamming Distance, 2D Parity, Internet Checksum, CRC-32 Modulo-2 Division, Hamming (7,4) Code, Stop-and-Wait, Go-Back-N, Selective Repeat
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.2.1 Block Coding & Hamming Distance Theory
M3.2 ERROR CONTROL THEORY
• Block Coding Principles
Dataword of $k$ bits encoded into Codeword of $n$ bits ($n > k$) by appending $r = n - k$ redundant parity bits.
• Hamming Distance $d(x,y)$
The number of bit positions in which two codewords $x$ and $y$ differ (computed by taking XOR and counting number of 1s).
• Minimum Hamming Distance ($d_{min}$)
The smallest Hamming distance between any pair of valid codewords in the codebook.
• Error Detection Capability
To detect up to $s$ bit errors: $d_{min} \ge s + 1$ (e.g., Simple Parity has $d_{min} = 2$, detects single-bit errors $s = 1$).
• Error Correction Capability
To correct up to $t$ bit errors: $d_{min} \ge 2t + 1$ (e.g., Single-bit error correction $t = 1$ requires $d_{min} \ge 3$).
Hamming Distance Rules
→ Detect s errors: d_min >= s + 1
→ Correct t errors: d_min >= 2t + 1
→ Simple Parity: d_min = 2
→ Hamming (7,4): d_min = 3
→ r parity bits: 2^r >= k + r + 1
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.2.2 Worked KTU Numerical: CRC Modulo-2 Polynomial Division
M3.2 CRC WORKED PROBLEM
📌 KTU Numerical Problem Statement
A data bit stream D = 10100100 is to be transmitted using CRC generator polynomial G(x) = x^4 + x^2 + 1 (binary generator G = 10101). (a) Determine the 4-bit CRC Checksum (Frame Check Sequence FCS), (b) What codeword is transmitted? (c) Show that receiver detects zero remainder in the absence of bit errors.
📐 Governing Formulas & Principles:
• Generator G(x) = x^4 + x^2 + 1 -> Degree r = 4 -> Generator bit string G = 10101 (5 bits).
• Step 1: Append r = 4 zeros to data D: D' = 10100100 0000 (12 bits).
• Step 2: Perform Modulo-2 binary division (XOR operations) of D' by G.
• Step 3: Remainder of division is the 4-bit CRC Checksum R.
📝 Step-by-Step Derivation & Solution
Step 1: Dividend: 101001000000 | Divisor: 10101
Step 2: 10100 XOR 10101 -> Remainder 00001; bring down bits -> 0001100...
Step 3: Continuing Modulo-2 XOR division yields 4-bit Remainder R = 1100.
Step 4: Transmitted Codeword T = Data + CRC = 10100100 1100 (12 bits).
Step 5: Receiver Divides T (101001001100) by G (10101) -> Remainder = 0000 (Valid / No errors!).
✅ FINAL ANSWER: CRC Checksum = 1100 | Transmitted Codeword = 101001001100
💡 Exam Tip: Modulo-2 addition and subtraction are both identical to bitwise XOR with zero carries/borrows.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
3.2.3 Worked KTU Numerical: Hamming (7,4) Single-Bit Error Correction
M3.2 HAMMING CODE WORKED
📌 KTU Numerical Problem Statement
A 4-bit dataword D = 1011 (d4=1, d3=0, d2=1, d1=1) is encoded using Hamming (7,4) code with parity bits at positions 1, 2, 4. (a) Generate 7-bit codeword. (b) If received word is R = 1011011, calculate syndrome bits (s3, s2, s1) and locate the erroneous bit position.
📐 Governing Formulas & Principles:
• Bit positions 1 to 7: p1 (pos 1), p2 (pos 2), d1 (pos 3), p4 (pos 4), d2 (pos 5), d3 (pos 6), d4 (pos 7).
• p1 checks positions with bit 1 set (1, 3, 5, 7): p1 = d1 XOR d2 XOR d4.
• p2 checks positions with bit 2 set (2, 3, 6, 7): p2 = d1 XOR d3 XOR d4.
• p4 checks positions with bit 4 set (4, 5, 6, 7): p4 = d2 XOR d3 XOR d4.
• Syndrome S = (s4 s2 s1) indicates decimal error bit position (0 = no error).
📝 Step-by-Step Derivation & Solution
Step 1: p1 = 1 XOR 1 XOR 1 = 1 | p2 = 1 XOR 0 XOR 1 = 0 | p4 = 1 XOR 0 XOR 1 = 0
Step 2: Generated Codeword: (p1, p2, d1, p4, d2, d3, d4) = (1, 0, 1, 0, 1, 0, 1) -> 1010101
Step 3: Received Word R = (r1..r7) = (1, 1, 0, 1, 1, 0, 1) (bit 2 corrupted!)
Step 4: s1 = r1 XOR r3 XOR r5 XOR r7 = 1 XOR 0 XOR 1 XOR 1 = 1
Step 5: s2 = r2 XOR r3 XOR r6 XOR r7 = 1 XOR 0 XOR 0 XOR 1 = 0
Step 6: s4 = r4 XOR r5 XOR r6 XOR r7 = 1 XOR 1 XOR 0 XOR 1 = 1 -> Syndrome = 101_2 = Pos 5 (d2 corrupted!)
✅ FINAL ANSWER: Syndrome S = 101 (Binary 5) -> Bit position 5 is inverted and corrected!
💡 Exam Tip: Hamming (7,4) code can correct any single-bit error and detect any double-bit error.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
3.2.4 Sliding Window Flow Control: Stop-and-Wait vs GBN vs Selective Repeat
M3.2 ARQ PROTOCOLS
Stop-and-Wait ARQ
• Window Size: $W_s = 1$, $W_r = 1$
• Sequence Bits: 1-bit ($m=1$, sequence numbers 0 and 1)
• Efficiency: Extremely low on high-bandwidth-delay product links: $\eta = 1 / (1 + 2a)$ where $a = t_{prop} / t_{trans}$
• Buffering: 1 frame buffer at sender and receiver
Go-Back-N (GBN) ARQ
• Window Size: $W_s = 2^m - 1$, $W_r = 1$ (Cumulative ACKs)
• On Loss: Discards all subsequent out-of-order frames; retransmits entire window from lost frame
• Sender Buffer: Buffers $W_s$ frames; receiver requires zero buffer
• Efficiency: High efficiency unless error rate is severe
Selective Repeat (SR) ARQ
• Window Size: $W_s = 2^{m-1}$, $W_r = 2^{m-1}$ (Individual ACKs)
• On Loss: Receiver buffers out-of-order frames; sender retransmits **only the lost frame**
• Buffer Needs: Both sender and receiver maintain $2^{m-1}$ buffer queues
• Efficiency: Optimal bandwidth utilization on noisy channels
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 6
🎯 Exam Booster & Review: Error Detection & Flow Control
M3.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain CRC error detection with a polynomial division example. Why is CRC implemented in hardware with LFSR shift registers? (8 Marks)
Q: Derive the maximum sender window size for Go-Back-N ($2^m - 1$) and Selective Repeat ($2^{m-1}$). Explain why exceeding these limits causes protocol failure. (8 Marks)
Q: Explain Hamming (7,4) code with syndrome error correction calculation. (7 Marks)
💡 Critical Conceptual Takeaways
✔ CRC detects all single-bit, double-bit, odd numbers of errors, and burst errors up to generator polynomial degree $r$.
✔ Go-Back-N window is $2^m - 1$ to prevent receiver from mistaking duplicate frames for new ones.
✔ Selective Repeat requires equal sender and receiver window sizes bounded at $2^{m-1}$.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET