## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.3
Multiple Access Control (MAC) Protocols
Random Access (Pure & Slotted ALOHA, CSMA, CSMA/CD, CSMA/CA), Controlled Access (Polling, Token Ring), Channelization (CDMA)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.3.1 Random Access: Pure ALOHA vs Slotted ALOHA
M3.3 ALOHA COMPARISON
Pure ALOHA (Norman Abramson, 1970)
• Transmission Rule: Transmit continuous frame whenever data is ready without sensing channel
• Vulnerable Period: $V_p = 2 \times T_{frame}$ (Collision occurs if any other node transmits within 2 frame times)
• Throughput Formula: $S = G \cdot e^{-2G}$ where $G$ = traffic load
• Maximum Efficiency: Maximum throughput $S_{max} = 1 / (2e) \approx 18.4\%$ at $G = 0.5$
• Collisions: High collision rate due to uncoordinated overlapping frames
Slotted ALOHA (Roberts, 1972)
• Transmission Rule: Time divided into discrete slots equal to $T_{frame}$. Nodes transmit strictly at slot boundaries
• Vulnerable Period: $V_p = 1 \times T_{frame}$ (Halves vulnerability interval)
• Throughput Formula: $S = G \cdot e^{-G}$
• Maximum Efficiency: Maximum throughput $S_{max} = 1 / e \approx 36.8\%$ at $G = 1.0$ (Exactly doubles Pure ALOHA!)
• Synchronization: Requires global slot synchronization across all nodes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.3.2 CSMA/CD: Carrier Sense Multiple Access with Collision Detection
M3.3 CSMA/CD PROTOCOL
• Carrier Sense (Listen Before Talk)
Node listens to channel before transmitting. 1-persistent: transmits immediately when idle; Non-persistent: waits random backoff if busy; p-persistent: transmits with probability $p$ when idle.
• Collision Detection (Listen While Talk)
Node continuously monitors voltage/energy on wire while transmitting. If signal amplitude exceeds collision threshold, collision is detected immediately!
• Jam Signal & Abort
Upon detecting collision, node aborts transmission immediately and broadcasts a 32-48 bit **Jam Signal** to ensure all other nodes detect the collision.
• Minimum Frame Size Constraint ($L_{min}$)
To ensure a sender does not finish transmitting before collision signal propagates back: $T_{frame} \ge 2 \times T_{prop} \implies \frac{L_{min}}{R} \ge 2 \cdot \frac{d}{s} \implies L_{min} = 2 \times T_{prop} \times R$.
• Binary Exponential Backoff (BEB)
After $k$-th collision ($k \le 10$), node picks random wait slot $r \in \{0, 1, 2, \dots, 2^k - 1\}$ and waits $r \times 512$ bit times. Aborts after 16 consecutive collisions.
CSMA/CD Summary
→ 1-persistent sense
→ Jam signal on collision
→ L_min = 2 * t_prop * R
→ Standard Ethernet L_min = 64 Bytes (512 bits)
→ Backoff range: [0, 2^k - 1]
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
3.3.3 Worked KTU Numerical: CSMA/CD Minimum Frame Size
M3.3 CSMA/CD NUMERICAL
📌 KTU Numerical Problem Statement
A 1 Gbps Ethernet LAN runs over a 1 km fiber link with propagation speed s = 2 * 10^8 m/s. Calculate the minimum frame size required for proper collision detection. If transmission rate is increased to 10 Gbps over the same link, what must the new minimum frame size be?
📐 Governing Formulas & Principles:
• L_min = 2 * t_prop * R
• t_prop = d / s = 1000 m / (2 * 10^8 m/s) = 5 * 10^-6 s = 5 microseconds.
• Round-trip propagation time 2 * t_prop = 10 microseconds = 10^-5 seconds.
• L_min = 2 * t_prop * R (bits).
📝 Step-by-Step Derivation & Solution
Step 1: For R = 1 Gbps = 10^9 bps:
Step 2: L_min = 10^-5 s * 10^9 bps = 10,000 bits = 10,000 / 8 = 1250 Bytes.
Step 3: For R = 10 Gbps = 10^10 bps:
Step 4: L_min = 10^-5 s * 10^10 bps = 100,000 bits = 12,500 Bytes (12.5 KB).
Step 5: Conclusion: At 10 Gbps, minimum frame size becomes unfeasibly large; hence 10 Gigabit Ethernet mandates full-duplex point-to-point links (disabling CSMA/CD entirely).
✅ FINAL ANSWER: 1 Gbps: L_min = 1250 Bytes | 10 Gbps: L_min = 12,500 Bytes
💡 Exam Tip: CSMA/CD is only applicable on half-duplex shared media; full-duplex switched Ethernet does not require CSMA/CD.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: Multiple Access Protocols
M3.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Derive the maximum channel throughput for Pure ALOHA ($18.4\%$) and Slotted ALOHA ($36.8\%$) with vulnerable period diagrams. (8 Marks)
Q: Explain the working of CSMA/CD with the Binary Exponential Backoff (BEB) algorithm and minimum frame size derivation. (8 Marks)
Q: Explain Code Division Multiple Access (CDMA) using orthogonal Walsh chip sequences with an encoding and decoding example. (7 Marks)
💡 Critical Conceptual Takeaways
✔ Slotted ALOHA doubles Pure ALOHA efficiency by eliminating partial frame collisions.
✔ Minimum frame size in CSMA/CD guarantees collision detection before transmission ends ($L_{min} = 2 \cdot t_{prop} \cdot R$).
✔ CDMA allows simultaneous transmission over the same frequency band using orthogonal chip codes.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET