## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.4
Link-Layer Addressing & Address Resolution Protocol (ARP)
48-Bit MAC Addresses (EUI-48), ARP Request (Broadcast) & ARP Reply (Unicast), ARP Cache & Timeout, Proxy ARP, Subnet Crossing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.4.1 MAC Addressing & Address Resolution Protocol (ARP)
M3.4 ARP PROTOCOL
• MAC Hardware Address (48 bits / 6 Bytes)
Burned into NIC ROM (e.g., `1A:2B:3C:4D:5E:6F`). First 24 bits = OUI (Organizationally Unique Identifier assigned by IEEE); Last 24 bits = Vendor NIC serial number.
• ARP Mission (RFC 826)
Dynamically resolves a known 32-bit IP address into its corresponding 48-bit MAC address on the local physical subnet.
• ARP Message Flow
1. **ARP Request**: Host broadcasts frame (`FF:FF:FF:FF:FF:FF`) asking: 'Who owns IP 192.168.1.5? Send your MAC to 192.168.1.2'. \n 2. **ARP Reply**: Target host unicasts reply containing its physical MAC address directly to the sender. \n 3. **ARP Table**: Sender caches the mapping in its local ARP Cache table with a TTL timer (typically 20 minutes).
• Proxy ARP & Gratuitous ARP
**Proxy ARP**: Router responds to ARP request on behalf of a remote node. **Gratuitous ARP**: Host announces its own IP/MAC to detect duplicate IP conflicts and update switch MAC tables.
ARP Key Facts
→ ARP Request: L2 Broadcast (FF:..:FF)
→ ARP Reply: L2 Unicast
→ L2 Frame Type: 0x0806 (ARP)
→ ARP Cache: Dynamic IP->MAC table
→ Gratuitous ARP: IP conflict check
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.4.2 Packet Forwarding Across Subnets (MAC & IP Rewriting)
M3.4 SUBNET ROUTING
• Scenario: Host A (Subnet 1) sends packet to Host B (Subnet 2) via Router R
Source Host A creates L3 IP packet: `Src IP = IP_A`, `Dst IP = IP_B` (IP addresses remain constant throughout end-to-end path).
• Hop 1 (Host A -> Router R)
Host A inspects routing table; determines destination `IP_B` is outside local subnet. Encapsulates IP packet into L2 frame: `Src MAC = MAC_A`, `Dst MAC = MAC_Router_Interface_1` (uses ARP to find router MAC).
• Router R Processing
Router decapsulates L2 frame, inspects L3 `Dst IP = IP_B`, consults FIB routing table, decrements TTL, recomputes IP checksum, and determines outgoing Interface 2.
• Hop 2 (Router R -> Host B)
Router encapsulates packet into a fresh L2 frame: `Src MAC = MAC_Router_Interface_2`, `Dst MAC = MAC_B` (via ARP on Subnet 2).
• Core Takeaway
**IP addresses remain unchanged end-to-end; MAC addresses change at every single router hop!**
Hop-by-Hop Headers
→ Hop 1: Src MAC_A -> Dst MAC_R1
→ Hop 2: Src MAC_R2 -> Dst MAC_B
→ End-to-End: Src IP_A -> Dst IP_B
→ L2 MAC rewritten per hop
→ L3 IP preserved end-to-end
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: MAC Addressing & ARP
M3.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the operation of Address Resolution Protocol (ARP) with request and reply frame structures. (7 Marks)
Q: Trace the step-by-step changes in Source/Destination IP and Source/Destination MAC addresses as a packet travels from Host A to Host B across an intermediate router. (8 Marks)
💡 Critical Conceptual Takeaways
✔ ARP bridges Layer 3 IP addresses to Layer 2 physical MAC addresses.
✔ ARP requests are L2 broadcasts (`FF:FF:FF:FF:FF:FF`); ARP replies are L2 unicasts.
✔ L3 IP addresses identify end hosts; L2 MAC addresses identify next-hop network interfaces.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET