## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.5V
Virtual Local Area Networks (VLANs - IEEE 802.1Q)
Broadcast Containment, Port-Based vs Tagged VLANs, IEEE 802.1Q 4-Byte Tag (VID 1-4094), Access vs Trunk Ports, Router-on-a-Stick
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.5V.1 VLAN Motivation & IEEE 802.1Q Tagged Framing
M3.5V VLAN ARCHITECTURE
• VLAN Motivation
Physically co-located hosts can be partitioned into logical broadcast domains regardless of physical switch topology. Prevents broadcast storms, enhances security, and organizes departments logically (e.g., Faculty VLAN, Student VLAN, Lab VLAN).
• Port-Based VLAN (Untagged)
Switch ports assigned static VLAN IDs. Traffic inside switch segregated by port group; frames on access links remain standard untagged Ethernet frames.
• IEEE 802.1Q Tagged Frame (4 Bytes Inserted after Source MAC)
1. **TPID (Tag Protocol Identifier - 16 bits)**: Set to `0x8100` (identifies frame as 802.1Q tagged). \n 2. **PCP (Priority Code Point - 3 bits)**: IEEE 802.1p Quality of Service priority (0 to 7). \n 3. **DEI (Drop Eligible Indicator - 1 bit)**: Set to 1 if frame can be dropped during congestion. \n 4. **VID (VLAN Identifier - 12 bits)**: Uniquely identifies VLAN number (1 to 4094; 0 and 4095 reserved).
• Access Port vs Trunk Port
**Access Port**: Connects end hosts; carries traffic for 1 untagged VLAN only. **Trunk Port**: Interconnects switches/routers; carries multiplexed tagged traffic for multiple VLANs simultaneously.
IEEE 802.1Q Tag
→ TPID: 0x8100 (16 bits)
→ PCP: 3 bits (QoS Priority)
→ DEI: 1 bit (Drop eligibility)
→ VID: 12 bits (4094 VLANs)
→ Trunking: Carries tagged frames
→ Access: Carries untagged frames
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.5V.2 Inter-VLAN Routing: Router-on-a-Stick vs Layer 3 Switch
M3.5V INTER-VLAN ROUTING
• Why Inter-VLAN Routing?
By design, hosts on different VLANs cannot communicate at Layer 2 even if plugged into the same physical switch. Inter-VLAN routing requires Layer 3 packet forwarding.
• Router-on-a-Stick (Legacy Approach)
A single physical Ethernet interface on an external router is connected to a switch Trunk port. The router interface is divided into logical **Sub-interfaces** (e.g., `eth0.10`, `eth0.20`), each configured with the default gateway IP and 802.1Q encapsulation for its respective VLAN.
• Layer 3 Switch (Modern Core Routing)
Switches with built-in hardware ASIC routing capabilities. Configured with **Switched Virtual Interfaces (SVIs)** (`interface vlan 10`, `interface vlan 20`) providing multi-gigabit wire-speed inter-VLAN routing without external router bottleneck.
Inter-VLAN Methods
→ Router-on-a-Stick: 1 Trunk link
→ Sub-interfaces: eth0.10, eth0.20
→ L3 Switch: Hardware SVI routing
→ Wire-speed routing in L3 switch
→ Isolates broadcast domains
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Virtual LANs (VLANs)
M3.5V
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the benefits of VLANs and illustrate the 4-byte IEEE 802.1Q tag header format. (7 Marks)
Q: Differentiate between Access ports and Trunk ports on an Ethernet switch. (5 Marks)
Q: Explain Inter-VLAN routing using the Router-on-a-Stick architecture with a network diagram and configuration concepts. (7 Marks)
💡 Critical Conceptual Takeaways
✔ VLANs partition a single physical switch into multiple isolated broadcast domains.
✔ IEEE 802.1Q tag inserts 4 bytes (TPID 0x8100 + 12-bit VID for 4094 VLANs).
✔ Trunk links carry tagged multiplexed frames between switches and routers.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET