## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.5
Ethernet Protocols & IEEE 802.3 Architecture
Standard Ethernet (10M), Fast Ethernet (100M), Gigabit Ethernet (1G), 10GbE, IEEE 802.3 Frame Format (64B to 1518B)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.5.1 IEEE 802.3 Ethernet Frame Format
M3.5 ETHERNET FRAME
• Preamble (7 Bytes)
7 bytes of alternating `10101010` patterns used to synchronize receiver clock circuitry.
• Start of Frame Delimiter - SFD (1 Byte)
1 byte pattern `10101011` indicating that destination MAC address begins immediately on the next bit.
• Destination MAC Address (6 Bytes)
48-bit hardware address of target NIC (or broadcast `FF:FF:FF:FF:FF:FF`).
• Source MAC Address (6 Bytes)
48-bit hardware address of sending NIC.
• Type / Length Field (2 Bytes)
If $\ge 1536$ (0x0600), specifies upper layer protocol (EtherType: IPv4 `0x0800`, ARP `0x0806`, IPv6 `0x86DD`). If $\le 1500$, specifies frame payload length.
• Payload / Data (46 to 1500 Bytes)
Carries L3 datagram. Minimum payload is 46 bytes (padded with zeros if smaller) to enforce the 64-byte minimum frame size constraint.
• Frame Check Sequence - FCS (4 Bytes)
32-bit Cyclic Redundancy Check (CRC-32) computed over Dst MAC, Src MAC, Type, and Payload.
Frame Sizes
→ Preamble + SFD: 8 Bytes
→ Header + FCS: 18 Bytes
→ Min Payload: 46 Bytes
→ Max Payload (MTU): 1500 Bytes
→ Min Frame Size: 64 Bytes
→ Max Frame Size: 1518 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.5.2 Ethernet Speed Evolution: Standard to 10GbE
M3.5 ETHERNET EVOLUTION
Standard & Fast Ethernet
• Standard (10 Mbps): 10Base5 (Thicknet coaxial), 10Base2 (Thinnet), 10Base-T (UTP Cat 3/5 with Hub/Switch). Uses Manchester line coding
• Fast Ethernet (100 Mbps): 100Base-TX (Cat 5 UTP using 4B/5B and MLT-3 coding), 100Base-FX (Fiber). Introduces Auto-Negotiation
Gigabit & 10G Ethernet
• Gigabit Ethernet (1 Gbps): 1000Base-T (Cat 5e/6 UTP using 4 pairs full-duplex with 8B/10B coding), 1000Base-SX/LX (Fiber). Introduces Carrier Extension and Packet Bursting for half-duplex
• 10 Gigabit Ethernet (10 Gbps): 10GBase-T (Cat 6a/7) and 10GBase-SR/LR. Exclusively full-duplex switched connections; eliminates CSMA/CD completely
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: IEEE 802.3 Ethernet
M3.5
📚 KTU High-Yield Questions (K2 Understand)
Q: Draw the IEEE 802.3 Ethernet frame format and explain the function of each field. Why is the minimum frame size 64 bytes and maximum 1518 bytes? (8 Marks)
Q: Compare Standard Ethernet, Fast Ethernet, Gigabit Ethernet, and 10 Gigabit Ethernet with respect to medium, coding, and transmission modes. (7 Marks)
💡 Critical Conceptual Takeaways
✔ Preamble and SFD synchronize bit timing; FCS trailer provides CRC-32 error detection.
✔ 64-byte minimum frame ensures collision detection in 10/100 Mbps CSMA/CD networks.
✔ 10GbE operates strictly in full-duplex mode over switches and fiber links.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET