## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.6
Connecting Devices & Spanning Tree Protocol (STP)
Repeaters, Hubs (L1), Bridges & Layer 2 Switches (MAC Learning), Spanning Tree Protocol (IEEE 802.1D STP), Routers & Layer 3 Switches
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.6.1 Connecting Devices Taxonomy & Collision/Broadcast Domains
M3.6 CONNECTING DEVICES
Layer 1: Repeaters & Hubs
• Operating Layer: Physical Layer (L1)
• Function: Regenerates and amplifies electrical/optical signals; broadcasts incoming bits to all ports
• Collision Domains: Single shared collision domain across all ports
• Broadcast Domains: Single broadcast domain
• Intelligence: Zero intelligence / No buffering
Layer 2: Bridges & Switches
• Operating Layer: Data Link Layer (L2)
• Function: Inspects MAC addresses; filters and forwards frames selectively using hardware MAC Learning table
• Collision Domains: Microsegmentation: **Each individual port is an isolated collision domain**
• Broadcast Domains: Single broadcast domain (unless partitioned via VLANs)
• Buffering: Store-and-forward / Cut-through
Layer 3: Routers & L3 Switches
• Operating Layer: Network Layer (L3)
• Function: Routes packets across heterogeneous networks using IP addresses
• Collision Domains: Separate collision domain per port
• Broadcast Domains: **Separates broadcast domains** (does not forward L2 broadcasts)
• Routing Table: Maintains FIB routing table
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.6.2 Spanning Tree Protocol (IEEE 802.1D STP)
M3.6 SPANNING TREE PROTOCOL
• The Layer 2 Loop Problem
Redundant links between switches provide fault tolerance, but create disastrous **Broadcast Storms**, multiple frame copies, and MAC table instability.
• STP Goal
Logically disables redundant links by placing them in Blocking state, dynamically constructing a loop-free active tree topology while keeping backup paths on standby.
• BPDU (Bridge Protocol Data Units)
Switches exchange BPDUs containing: `Bridge ID = Priority (2B) + MAC Address (6B)` (Default priority = 32768).
• 4-Step STP Algorithm
1. **Root Bridge Election**: Switch with the lowest Bridge ID becomes the Root Bridge. \n 2. **Root Port (RP) Selection**: On each non-root switch, the port with the lowest path cost to the Root Bridge is selected as RP. \n 3. **Designated Port (DP) Selection**: On each LAN segment, the port with the lowest path cost to Root becomes DP. \n 4. **Blocking State**: All remaining ports are placed in Blocking/Discarding state to break loops.
STP Algorithm Steps
→ 1. Lowest Bridge ID -> Root Bridge
→ 2. Lowest Cost to Root -> Root Port (RP)
→ 3. Lowest Cost per Link -> Designated Port (DP)
→ 4. Remaining Ports -> Blocked / Alternate
→ Convergence time: ~30-50 seconds (RSTP: < 1s)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Connecting Devices & STP
M3.6
📚 KTU High-Yield Questions (K3 Apply)
Q: Compare Repeaters, Hubs, Switches, and Routers with respect to operating layer, collision domains, and broadcast domains. (8 Marks)
Q: Explain the working of the Spanning Tree Protocol (IEEE 802.1D) with Bridge ID, Root Bridge election, Root Ports, and Blocking ports. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Hubs extend collision domains; Switches isolate collision domains; Routers isolate broadcast domains.
✔ Transparent switches dynamically populate MAC tables by inspecting source MACs of arriving frames.
✔ STP prevents broadcast storms by breaking physical switching loops into a single logical tree.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET