## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.7
Wireless LANs: IEEE 802.11 (Wi-Fi) Architecture
BSS, AP, ESS, Distribution System, Hidden/Exposed Terminal Problems, CSMA/CA with RTS/CTS, SIFS/PIFS/DIFS, 802.11 Frame (4 Addresses)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.7.1 IEEE 802.11 Architecture & Terminal Problems
M3.7 WIRELESS ARCHITECTURE
• Basic Service Set (BSS)
The fundamental building block consisting of wireless stations and a central Access Point (AP) in Infrastructure mode (or peer-to-peer in Ad-hoc / IBSS mode).
• Extended Service Set (ESS)
Multiple BSSs interconnected via a wired Distribution System (DS) sharing a common SSID, enabling seamless roaming across campus.
• Hidden Terminal Problem
Nodes A and C cannot hear each other due to distance or physical obstacles, but both are in range of AP B. If A and C transmit simultaneously, their frames collide at B!
• Exposed Terminal Problem
Node B is transmitting to A. Node C wants to transmit to D (away from A). C senses B transmitting and unnecessarily defers, wasting channel capacity.
• Solution: CSMA/CA with RTS/CTS Handshake
Sender transmits short **RTS (Request to Send)** frame (20B). AP replies with **CTS (Clear to Send)** broadcast (14B) containing Network Allocation Vector (NAV) reservation time, silencing hidden terminals.
802.11 Topology
→ BSS: AP + Associated Stations
→ ESS: Multiple BSSs + Wired DS
→ Hidden Terminal: Collisions at AP
→ RTS/CTS: Virtual carrier sensing
→ NAV: Channel reservation timer
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.7.2 CSMA/CA Protocol Timing Intervals & 4-Address Frame
M3.7 CSMA/CA TIMING
• Inter-Frame Space (IFS) Hierarchy
1. **SIFS (Short IFS)**: Highest priority; used for immediate ACKs, CTS, and fragmented frames. \n 2. **PIFS (PCF IFS)**: Medium priority; used in polling mode. \n 3. **DIFS (DCF IFS)**: Standard priority; minimum wait time before station can contend for channel.
• Contention Window (CW) & Backoff
Station waits DIFS; if idle, selects random backoff slot in $[0, CW]$. Counts down while channel is idle; freezes counter during busy periods.
• IEEE 802.11 4-Address Frame Format
Frame Control (2B) | Duration/ID (2B) | Address 1 (6B: Receiver MAC) | Address 2 (6B: Transmitter MAC) | Address 3 (6B: Original Source or Final Dest MAC) | Sequence Control (2B) | Address 4 (6B: Used strictly when bridging across WDS wireless distribution links) | Payload (0-2312B) | FCS (4B).
Timing Hierarchy
→ SIFS < PIFS < DIFS < EIFS
→ SIFS: ACKs & CTS (Highest priority)
→ DIFS: Standard data contention
→ Addr 1: Immediate Receiver
→ Addr 2: Immediate Transmitter
→ Addr 3: Original Source / Dest
→ Addr 4: WDS Wireless Bridge
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: IEEE 802.11 Wireless LANs
M3.7
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the Hidden Terminal and Exposed Terminal problems in Wireless LANs. How does CSMA/CA with RTS/CTS resolve them? (8 Marks)
Q: Explain the timing relationships between SIFS, PIFS, and DIFS in IEEE 802.11 CSMA/CA with a neat timing diagram. (7 Marks)
Q: Explain the four MAC address fields in the IEEE 802.11 frame format. When is Address 4 used? (6 Marks)
💡 Critical Conceptual Takeaways
✔ Wireless radios cannot detect collisions while transmitting; hence Wi-Fi uses collision avoidance (CSMA/CA).
✔ RTS and CTS frames carry NAV reservation timers to silence hidden nodes.
✔ Address 4 is populated only when frames are bridged between two wireless APs in WDS mode.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET