## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.8
Mobile IP Architecture & Protocols
Mobile Node (MN), Home Agent (HA), Foreign Agent (FA), Home Address (HoA), Care-of Address (CoA), Tunneling & Triangle Routing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.8.1 Mobile IP Architecture & Entities (RFC 5944)
M3.8 MOBILE IP BASICS
• The Mobility Challenge
Standard IP routing uses destination IP prefixes. If a mobile laptop moves to a new subnet, changing its IP address terminates all active TCP connections! Mobile IP allows a host to retain its permanent IP transparently.
• Mobile IP Entities
1. **Mobile Node (MN)**: The roaming host. \n 2. **Home Network & Home Agent (HA)**: The home subnet and the router acting on behalf of MN when away. \n 3. **Foreign Network & Foreign Agent (FA)**: The visited subnet router assisting MN. \n 4. **Correspondent Node (CN)**: The peer host communicating with MN.
• Dual-Address Mechanism
1. **Home Address (HoA)**: Permanent IP address assigned in home subnet (used for active TCP sessions). \n 2. **Care-of Address (CoA)**: Temporary IP address associated with visited foreign network.
Core Entities
→ MN: Mobile Node
→ HA: Home Agent router
→ FA: Foreign Agent router
→ HoA: Permanent IP address
→ CoA: Temporary visited IP
→ CN: Correspondent Node
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
3.8.2 Operational Phases: Registration, Tunneling & Triangle Routing
M3.8 MOBILE IP PHASES
• Phase 1: Agent Discovery
Foreign Agents broadcast periodic Agent Advertisements (ICMP extension); MN detects it has moved and obtains a CoA.
• Phase 2: Registration
MN sends Registration Request to FA -> FA forwards to Home Agent (HA) -> HA updates binding table (`HoA -> CoA`) and sends Registration Reply.
• Phase 3: Data Transfer (IP-in-IP Encapsulation Tunneling)
CN sends packet to `HoA` -> Routed to Home Network -> Home Agent intercepts packet via Proxy ARP -> HA encapsulates packet inside a new IP header (`Src IP = HA`, `Dst IP = CoA`) -> Transmits through IP tunnel to FA -> FA decapsulates and delivers to MN.
• Reverse Path & Triangle Routing Problem
MN sends directly to CN via standard IP routing. However, traffic from CN travels through HA -> FA -> MN (inefficient Triangle Routing). Solution: Route Optimization allows CN to cache MN's CoA and tunnel directly.
Tunneling Flow
→ CN -> Home Agent (HoA)
→ HA intercepts (Proxy ARP)
→ HA tunnels to FA (IP-in-IP)
→ FA decapsulates -> MN
→ MN replies directly to CN
→ Triangle Routing fixed via CoA cache
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Mobile IP Architecture
M3.8
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the architecture and entities of Mobile IP (MN, HA, FA, HoA, CoA) with a neat diagram. (8 Marks)
Q: Explain the three operational phases of Mobile IP: Agent Discovery, Registration, and Encapsulation Tunneling. (8 Marks)
Q: What is the Triangle Routing problem in Mobile IP, and how does Route Optimization solve it? (6 Marks)
💡 Critical Conceptual Takeaways
✔ Mobile IP preserves TCP connection survivability during subnet roaming.
✔ Home Agent intercepts packets using Proxy ARP and encapsulates them via IP-in-IP tunneling to the Care-of Address.
✔ Triangle routing introduces latency by routing all forward traffic through the Home Agent.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET