## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.9
Linux Network Programming: Raw Sockets & PF_PACKET
Data Link Provider Interface (DLPI), BSD Packet Filter (BPF), Linux PF_PACKET / AF_PACKET (SOCK_RAW, ETH_P_ALL), Promiscuous Sniffer
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
3.9.1 Hands-On: Packet Sniffing with Linux `PF_PACKET`
M3.9 LINUX RAW SOCKETS
// Linux Socket & Protocol Implementation
#include <sys/socket.h> #include <netinet/ether.h> #include <net/if.h> #include <sys/ioctl.h> int main() { // 1. Create Raw Packet Socket to capture all Ethernet frames int raw_sock = socket(AF_PACKET, SOCK_RAW, htons(ETH_P_ALL)); // 2. Enable Promiscuous Mode on network interface eth0 struct ifreq ifr; strcpy(ifr.ifr_name, "eth0"); ioctl(raw_sock, SIOCGIFFLAGS, &ifr); ifr.ifr_flags |= IFF_PROMISC; ioctl(raw_sock, SIOCSIFFLAGS, &ifr); // 3. Capture and Dissect Raw Ethernet Frame unsigned char buffer[2048]; while (1) { int len = recvfrom(raw_sock, buffer, sizeof(buffer), 0, NULL, NULL); struct ether_header *eth = (struct ether_header *)buffer; printf("Src MAC: %s -> Dst MAC: %s | Protocol: 0x%04X\n", ether_ntoa((struct ether_addr *)eth->ether_shost), ether_ntoa((struct ether_addr *)eth->ether_dhost), ntohs(eth->ether_type)); } }
⚙️ System Call & Execution Workflow
• `AF_PACKET` / `PF_PACKET`: Linux-specific socket domain allowing direct interaction with Layer 2 device drivers, bypassing the standard kernel TCP/IP protocol stack entirely.
• `SOCK_RAW` vs `SOCK_DGRAM`: `SOCK_RAW` provides raw Ethernet frames including L2 header and trailer; `SOCK_DGRAM` provides frames with L2 header stripped.
• Protocol Filter `ETH_P_ALL`: Captures all incoming and outgoing frames (IPv4, ARP, IPv6, STP, VLAN).
• Promiscuous Mode (`IFF_PROMISC`): Instructs the NIC hardware to disable MAC address filtering and deliver all overheard frames on the physical wire to the OS.
💡 Hands-on Insight: Used by network diagnostic tools like Wireshark, tcpdump, and custom IDS packet analysis engines.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
🎯 Exam Booster & Review: Linux Raw Sockets
M3.9
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the difference between standard Berkeley sockets (`AF_INET`) and Linux packet sockets (`AF_PACKET`). (6 Marks)
Q: Write a C program using `PF_PACKET` and `SOCK_RAW` to capture Ethernet frames and extract Source and Destination MAC addresses. (8 Marks)
💡 Critical Conceptual Takeaways
✔ `AF_PACKET` gives direct access to Layer 2 raw Ethernet frames.
✔ Promiscuous mode captures all frames on the shared link regardless of destination MAC.
✔ `ETH_P_ALL` captures all Layer 3 protocol payloads.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET