## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.1
Network Management Architecture & SNMP Protocol
Managing Entities (Managers), Managed Devices (Agents), MIB, SNMP Protocol Operations, SNMPv1 vs SNMPv2c vs SNMPv3 (USM & VACM)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
4.1.1 Network Management Framework & SNMP Operations
M4.1 SNMP FRAMEWORK
• Network Management Architecture
Consists of 4 pillars: 1. **Managing Entity (Manager / NMS)**: Centralized workstation running management software. 2. **Managed Devices**: Routers, switches, servers, hosts containing management data. 3. **Management Agent**: Software daemon running inside managed device. 4. **Management Information Base (MIB)**: Virtual database of manageable object variables.
• SNMP Protocol (Simple Network Management Protocol - RFC 3411)
Operates over UDP port 161 (Manager to Agent queries) and UDP port 162 (Agent to Manager asynchronous Traps).
• Core SNMP Protocol Operations
1. **GetRequest**: Manager fetches value of 1 or more MIB variables from Agent. \n 2. **GetNextRequest**: Manager fetches the lexicographically next MIB variable (used for MIB tree walking and table traversal). \n 3. **GetBulkRequest (v2c/v3)**: Fetches large blocks of table rows in a single packet. \n 4. **SetRequest**: Manager sets/modifies configuration value on Agent device. \n 5. **Response**: Agent returns requested data values or error status. \n 6. **Trap / InformRequest**: Unsolicited alert sent by Agent to Manager upon an event (e.g., link failure, reboot). `InformRequest` requires Manager ACK.
SNMP Ports & PDUs
→ UDP Port 161: Agent listener
→ UDP Port 162: Manager Trap listener
→ GetRequest: Read variable
→ SetRequest: Write configuration
→ GetNext: Sequential MIB walk
→ GetBulk: Fast table download
→ Trap: Asynchronous alert
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
4.1.2 SNMP Version Evolution: SNMPv1 vs SNMPv2c vs SNMPv3
M4.1 SNMP EVOLUTION
SNMPv1 & SNMPv2c
• Security Model: Plaintext Community Strings (`public` for read-only, `private` for read-write). Vulnerable to packet sniffing
• Operations (v1): Get, GetNext, Set, Response, Trap
• Enhancements (v2c): Adds `GetBulkRequest` for fast table fetching and 64-bit high-capacity counters (`Counter64`), but retains plaintext community security
• Suitability: Isolated, trusted internal LANs only
SNMPv3 (Cryptographically Secure)
• Security Model: User-Based Security Model (USM) + View-Based Access Control Model (VACM)
• Authentication: Message digest authentication via HMAC-MD5 or HMAC-SHA (verifies origin and prevents tampering)
• Confidentiality: Payload encryption via DES or AES-128 / AES-256 (prevents eavesdropping)
• Message Freshness: Timestamps and boot counters prevent Replay attacks
• Enterprise Standard: Mandatory standard for secure network management
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Network Management & SNMP
M4.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the four components of the Network Management architecture (Manager, Agent, MIB, SNMP) with a neat diagram. (7 Marks)
Q: Describe the various SNMP protocol operations (GetRequest, GetNextRequest, GetBulkRequest, SetRequest, Trap, InformRequest). (8 Marks)
Q: Compare SNMPv1, SNMPv2c, and SNMPv3 with focus on the User-Based Security Model (USM) in SNMPv3. (7 Marks)
💡 Critical Conceptual Takeaways
✔ SNMP uses UDP port 161 for synchronous polling and port 162 for asynchronous event Traps.
✔ SNMPv2c introduced `GetBulk` and 64-bit counters; SNMPv3 added cryptographic authentication and AES encryption.
✔ `InformRequest` provides reliable delivery of trap notifications with manager acknowledgments.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET