## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.3
Data and Signals: Theoretical Channel Capacity
Analog vs Digital Signals, Bandwidth, Transmission Impairments (Attenuation, Noise), Signal-to-Noise Ratio (SNR), Nyquist Rate vs Shannon Capacity
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
4.3.1 Signals, Bandwidth & Transmission Impairments
M4.3 DATA & SIGNALS
• Analog vs Digital Signals
Analog signals have infinitely many continuous values over time (e.g., sine wave $s(t) = A \sin(2\pi f t + \phi)$). Digital signals have discrete discrete levels (e.g., 0V and 5V pulses representing bits 0 and 1).
• Bandwidth ($B$)
The range of frequencies contained in a composite signal: $B = f_{max} - f_{min}$ Hertz (Hz).
• Transmission Impairments
1. **Attenuation**: Loss of signal energy over distance (measured in decibels $dB = 10 \log_{10} (P_2 / P_1)$). Corrected via amplifiers/repeaters. \n 2. **Distortion**: Different frequency components travel at different speeds, altering composite waveform shape. \n 3. **Noise**: Unwanted external energy added to signal (Thermal noise $N_0 = kTB$, Induced noise, Crosstalk, Impulse noise).
• Signal-to-Noise Ratio (SNR)
Ratio of signal power to noise power: $SNR = \frac{P_{signal}}{P_{noise}}$. In decibels: $SNR_{dB} = 10 \log_{10} (SNR)$ (e.g., $SNR = 1000 \implies SNR_{dB} = 30$ dB).
Key Formulas
→ Bandwidth: B = f_max - f_min (Hz)
→ Decibels: dB = 10 * log10(P2 / P1)
→ SNR = P_signal / P_noise
→ SNR_dB = 10 * log10(SNR)
→ SNR = 10^(SNR_dB / 10)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
4.3.2 Channel Capacity Limits: Nyquist vs Shannon
M4.3 NYQUIST VS SHANNON
Nyquist Bit Rate (Noiseless Channel)
• Formulated By: Harry Nyquist (1928)
• Channel Condition: Assumes theoretical **noiseless** channel with bandwidth $B$ Hz and $L$ discrete signaling levels
• Formula: $C = 2 \times B \times \log_2 (L)$ bps
• Implication: Data rate can be increased indefinitely by increasing the number of signal levels $L$, but is constrained by noise in practice
Shannon Capacity (Noisy Channel)
• Formulated By: Claude Shannon (1948)
• Channel Condition: Assumes real-world channel contaminated with Thermal White Noise (Gaussian Noise)
• Formula: $C = B \times \log_2 (1 + SNR)$ bps
• Implication: Defines the absolute physical upper bound on error-free channel capacity regardless of how many signal levels $L$ are used
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
4.3.3 Worked KTU Numerical: Nyquist & Shannon Capacity
M4.3 CAPACITY NUMERICAL
📌 KTU Numerical Problem Statement
A telephone line has bandwidth B = 3000 Hz and Signal-to-Noise ratio SNR_dB = 31.62 dB (SNR approx 1452). (a) Calculate the theoretical maximum Shannon channel capacity. (b) To achieve this capacity on a noiseless line with B = 3000 Hz, how many signal levels L are required by Nyquist formula?
📐 Governing Formulas & Principles:
• Shannon Capacity: C = B * log2(1 + SNR) bps
• Given SNR_dB = 31.62 dB -> SNR = 10^(31.62 / 10) = 10^3.162 = 1452.1
• Nyquist Bit Rate: C = 2 * B * log2(L) bps -> log2(L) = C / (2 * B) -> L = 2^(C / 2B).
📝 Step-by-Step Derivation & Solution
Step 1: 1 + SNR = 1 + 1452.1 = 1453.1
Step 2: log2(1453.1) = log10(1453.1) / log10(2) = 3.1623 / 0.30103 = 10.505 bits
Step 3: Shannon Capacity C = 3000 Hz * 10.505 = 31,515 bps (approx 31.5 kbps).
Step 4: Equating to Nyquist: 31,515 = 2 * 3000 * log2(L) = 6000 * log2(L)
Step 5: log2(L) = 31,515 / 6000 = 5.2525 -> L = 2^5.2525 = 38.12 -> L = 38 signal levels.
✅ FINAL ANSWER: Shannon Capacity C = 31.5 kbps | Required Nyquist signal levels L = 38
💡 Exam Tip: Shannon determines the upper capacity limit; Nyquist tells us how many signal levels L are required to realize it.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: Channel Capacity & Signals
M4.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the three transmission impairments: Attenuation, Distortion, and Noise with diagrams and formulas. (7 Marks)
Q: State and derive the Nyquist Bit Rate formula for noiseless channels and Shannon Capacity theorem for noisy channels. (8 Marks)
Q: A channel has bandwidth B = 4 kHz. Calculate Shannon capacity if SNR_dB = 20 dB. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Nyquist bit rate ($2B \log_2 L$) applies to ideal noiseless channels.
✔ Shannon capacity ($B \log_2(1+SNR)$) establishes the fundamental thermodynamic limit of noisy channels.
✔ Decibels convert logarithmic power ratios into simple additive terms.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET