## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.4
Digital Transmission & Line Coding Schemes
Line Coding Criteria (DC, Sync, Baseline Wander), Unipolar, Polar (NRZ, RZ, Manchester, Diff Manchester), Bipolar (AMI), Block Coding (4B/5B), PCM & DM
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
4.4.1 Line Coding Design Criteria & Characteristics
M4.4 LINE CODING CRITERIA
• Line Coding Definition
The process of converting a sequence of digital bits (1s and 0s) into a discrete electrical/optical signal waveform for baseband transmission.
• Key Line Coding Design Criteria
1. **Signal Level vs Data Level**: Number of voltage states ($L$) vs bit values. \n 2. **DC Component**: Frequencies around 0 Hz create heat, cannot pass through transformers/capacitors, and waste transmitter power. Desirable = Zero DC. \n 3. **Self-Synchronization**: Signal transitions (edges) must allow receiver clock to synchronize timing, especially during long strings of consecutive 0s or 1s. \n 4. **Baseline Wander**: Running average of signal voltage must remain constant to maintain accurate decision slicing threshold. \n 5. **Error Detection**: Built-in coding violations indicate physical link errors.
• Pulse Code Modulation (PCM)
Digitizes analog signals in 3 steps: 1. **Sampling** (Nyquist Rate $f_s \ge 2 f_{max}$), 2. **Quantization** (approximates sample amplitudes to discrete levels; introduces Quantization Error), 3. **Encoding** (maps quantized levels into $n$-bit binary codewords: Bit Rate $= n \times f_s$).
Line Coding Goals
→ Eliminate DC components
→ Provide self-synchronization
→ Prevent baseline wander
→ Minimize bandwidth needs
→ PCM: Sample -> Quantize -> Encode
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
4.4.2 Major Line Coding Schemes Comparison
M4.4 SCHEMES COMPARISON
Unipolar & Polar NRZ
• Unipolar NRZ: Bit 1 = Positive voltage $+V$, Bit 0 = Zero 0V. Severe DC component; no synchronization on long 0s/1s
• Polar NRZ-L (Level): Bit 1 = Negative $-V$, Bit 0 = Positive $+V$. Sensitive to polarity inversion
• Polar NRZ-I (Invert): Bit 1 = Transition at start of bit interval; Bit 0 = No transition. Immune to polarity inversion, but fails on consecutive 0s
Biphase: Manchester & Differential Manchester
• Manchester (IEEE 802.3): Mid-bit transition: Bit 1 = High-to-Low transition; Bit 0 = Low-to-High transition. Perfect clock synchronization and Zero DC component, but doubles bandwidth requirement ($2 \times$ baud rate)
• Differential Manchester (Token Ring): Always transitions in the middle for clocking. Bit 0 = Transition at start of bit interval; Bit 1 = No transition at start. Highly robust against wire twists
Bipolar AMI & Multilevel
• Bipolar AMI: Bit 0 = Zero 0V; Bit 1 = Alternating positive $+V$ and negative $-V$. Zero DC component, low bandwidth, but loses sync on long 0s (solved via B8ZS/HDB3 scrambling)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Digital Transmission & Line Coding
M4.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the line coding waveforms for the bit stream `10110001` using: (a) Unipolar NRZ, (b) NRZ-L, (c) NRZ-I, (d) Manchester, (e) Differential Manchester, (f) Bipolar AMI. (9 Marks)
Q: Explain the working of Pulse Code Modulation (PCM) with Sampling Theorem ($f_s \ge 2f_{max}$), Quantization, and Encoding. (8 Marks)
Q: What is the DC component problem and baseline wander in digital transmission? (5 Marks)
💡 Critical Conceptual Takeaways
✔ Manchester coding guarantees a transition in every single bit cell for foolproof clock synchronization.
✔ Differential Manchester transitions at the start for bit 0, and has no start transition for bit 1.
✔ PCM digitizes voice signals at 8000 samples/sec $\times$ 8 bits/sample = 64 kbps (standard DS0 channel).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET