## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.5
Analog Transmission & Bandwidth Utilization (Multiplexing)
Digital-to-Analog Modulation (ASK, FSK, PSK, QAM), Multiplexing Techniques (FDM, WDM, Synchronous vs Statistical TDM), Spread Spectrum (FHSS, DSSS)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
4.5.1 Digital Modulation Schemes: ASK vs FSK vs PSK vs QAM
M4.5 MODULATION SCHEMES
ASK, FSK & PSK
• ASK (Amplitude Shift Keying / BASK): Bit 1 = High amplitude carrier $A_1 \cos(2\pi f_c t)$; Bit 0 = Low amplitude $A_2$ (or 0 in OOK). Susceptible to noise
• FSK (Frequency Shift Keying / BFSK): Bit 1 = Frequency $f_1$; Bit 0 = Frequency $f_2$. Robust against amplitude noise; requires higher bandwidth
• PSK (Phase Shift Keying / BPSK & QPSK): BPSK: Bit 1 = $0^\circ$ phase, Bit 0 = $180^\circ$ phase. QPSK: 2 bits per baud ($00, 01, 10, 11$) using 4 orthogonal phases ($45^\circ, 135^\circ, 225^\circ, 315^\circ$)
QAM (Quadrature Amplitude Modulation)
• Concept: Combines Amplitude Modulation (ASK) and Phase Modulation (PSK) simultaneously to maximize spectral efficiency
• 16-QAM & 64-QAM: 16-QAM encodes 4 bits/symbol ($2^4 = 16$ constellation points); 64-QAM encodes 6 bits/symbol; 256-QAM encodes 8 bits/symbol
• Constellation Diagrams: Visualizes constellation constellation points in In-Phase ($I$) and Quadrature ($Q$) 2D plane
• Applications: Wi-Fi (802.11ac/ax), 4G/5G LTE, Cable modems (DOCSIS)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
4.5.2 Multiplexing: FDM vs WDM vs Synchronous TDM vs Statistical TDM
M4.5 MULTIPLEXING TAXONOMY
Frequency & Optical Multiplexing
• FDM (Frequency-Division Multiplexing): Divides total analog bandwidth into distinct frequency channels separated by **Guard Bands** (e.g., FM radio, cable TV)
• WDM (Wavelength-Division Multiplexing): Optical analog of FDM. Combines multiple laser light beams of different wavelengths (e.g., 1550 nm, 1310 nm) onto a single optical fiber using diffraction prisms. DWDM handles 80+ channels
Time-Division Multiplexing (TDM)
• Synchronous TDM: Time divided into fixed recurring frames containing dedicated slots allocated round-robin to each input line. Slot wasted if an input line is idle
• Statistical TDM (Asynchronous): Dynamically allocates time slots **on demand** only to active lines transmitting data. Eliminates idle slot waste by adding channel address headers to each slot
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Analog Transmission & Multiplexing
M4.5
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain Quadrature Amplitude Modulation (QAM) and draw the constellation diagrams for 4-QAM and 16-QAM. (8 Marks)
Q: Compare Synchronous TDM and Statistical TDM with framing and slot allocation diagrams. (7 Marks)
Q: Explain Spread Spectrum techniques: Frequency Hopping Spread Spectrum (FHSS) vs Direct Sequence Spread Spectrum (DSSS). (7 Marks)
💡 Critical Conceptual Takeaways
✔ QAM modulates both amplitude and phase to pack multiple bits into a single baud symbol.
✔ FDM shares bandwidth in frequency; TDM shares bandwidth in time slots.
✔ Statistical TDM dynamically allocates slots on demand, achieving much higher link utilization than Synchronous TDM.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET