## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.6
Physical Transmission Media
Guided Media (Twisted Pair UTP/STP, Coaxial Cable, Fiber Optics SMF/MMF), Unguided Wireless (Radio Waves, Microwaves, Infrared)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
4.6.1 Guided Media: Twisted Pair vs Coaxial vs Optical Fiber
M4.6 GUIDED MEDIA
Twisted-Pair & Coaxial Cable
• Twisted-Pair (UTP / STP): Two insulated copper wires twisted together to cancel electromagnetic interference (crosstalk). Cat 5e (100 MHz, 1 Gbps), Cat 6 (250 MHz, 10 Gbps up to 55m), Cat 6a (500 MHz, 10 Gbps 100m). Terminated with RJ-45 connectors
• Coaxial Cable: Central copper core surrounded by dielectric insulator, metallic braided shield, and outer jacket. 10Base5 (Thicknet, 500m), 10Base2 (Thinnet, 185m), RG-59 (Cable TV). Terminated with BNC connectors
Optical Fiber (Total Internal Reflection)
• Physics Principle: Light pulses propagate via Total Internal Reflection inside glass core (refractive index $n_1$) surrounded by cladding ($n_2 < n_1$) when incident angle exceeds critical angle
• Multimode Step-Index: Multiple light rays reflect abruptly at core-cladding boundary; causes modal dispersion (short distances)
• Multimode Graded-Index: Core refractive index decreases gradually outward; light rays curve smoothly, reducing modal dispersion
• Single-Mode Fiber (SMF): Ultra-narrow core (8-10 $\mu$m); single light ray propagates straight; zero modal dispersion; enables 100+ km long-haul backbone links
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 3
4.6.2 Unguided Media: Wireless Electromagnetic Spectrum
M4.6 UNGUIDED WIRELESS
• Radio Waves (3 kHz to 1 GHz)
Omnidirectional radiation pattern (transmitting antenna broadcasts signals in all directions). Penetrates physical walls effortlessly. Subject to multi-path interference. Used in AM/FM radio and cordless phones.
• Microwaves (1 GHz to 300 GHz)
Unidirectional, Line-of-Sight propagation. Focused beam using parabolic dish or horn antennas. Cannot penetrate solid obstacles (walls, hills). Used in cellular networks, satellite communications, and GPS.
• Infrared Waves (300 GHz to 400 THz)
High-frequency, short-range line-of-sight communication. Completely blocked by walls and solid obstacles (ensures indoor security without room-to-room interference). Used in TV remote controls and IrDA devices.
Wireless Spectrum
→ Radio: Omnidirectional (Wall penetration)
→ Microwaves: Line-of-sight (Dish antenna)
→ Infrared: Short range (Blocked by walls)
→ Satellite: Geosynchronous (36,000 km)
→ Fiber: Total Internal Reflection
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
🎯 Exam Booster & Review: Transmission Media
M4.6
📚 KTU High-Yield Questions (K2 Understand)
Q: Compare Step-Index Multimode, Graded-Index Multimode, and Single-Mode optical fibers with refractive index profiles and light propagation paths. (8 Marks)
Q: Compare Twisted-Pair Cable, Coaxial Cable, and Optical Fiber across bandwidth, attenuation, EMI immunity, and cost. (7 Marks)
Q: Differentiate between Radio waves, Microwaves, and Infrared wireless media. (6 Marks)
💡 Critical Conceptual Takeaways
✔ Optical fibers provide immense bandwidth, zero EMI susceptibility, and ultra-low attenuation.
✔ Single-mode fiber eliminates modal dispersion for high-speed long-distance backbones.
✔ Microwaves require line-of-sight parabolic antennas; Infrared is safely contained by room walls.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET