## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 MASTER • MODULE 2 MASTER DECK
Transport & Network Layer Architecture
Complete Lecture Slides for KTU PCCST501 Computer Networks | Topics M2.1.1 through M2.3
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.1
Transport Layer Services & Multiplexing Principles
Process-to-Process Communication, Port Addressing, Connectionless vs Connection-Oriented Demultiplexing (2-Tuple vs 4-Tuple)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 3
2.1.1.1 Transport Layer Core Responsibilities
M2.1.1 TRANSPORT SERVICES
• Process-to-Process Logical Delivery
While the Network Layer delivers packets host-to-host between IP addresses, the Transport Layer extends this to deliver messages process-to-process between application sockets.
• Port Addressing & Socket Binding
Processes are identified via 16-bit Port Numbers (0 to 65,535). Sockets bind an IP address and Port number together as an end-to-end communication endpoint.
• Transport Layer Responsibilities
1. Multiplexing & Demultiplexing, 2. Reliability (Loss detection, ACKs, retransmissions), 3. Flow Control (Preventing receiver buffer overflow), 4. Congestion Control (Preventing network core collapse).
• Transport Limitations
Transport protocols cannot provide hard real-time delay bounds or guaranteed bandwidth on standard best-effort IP networks.
Key Port Numbers
→ Port 80: HTTP
→ Port 443: HTTPS
→ Port 22: SSH
→ Port 53: DNS
→ Port 25: SMTP
→ Port 21: FTP Control
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
2.1.1.2 Demultiplexing: Connectionless (UDP) vs Connection-Oriented (TCP)
M2.1.1 DEMULTIPLEXING
UDP Demultiplexing (2-Tuple)
• Identifier Tuple: Identified strictly by: `(Destination IP, Destination Port)`
• Behavior: Two UDP datagrams arriving from different source IP/ports targeted at same Dest Port are delivered to the exact same socket
• State: Completely stateless; no connection handshake or per-peer buffers
• Speed: Zero connection establishment latency
TCP Demultiplexing (4-Tuple)
• Identifier Tuple: Identified by 4-tuple: `(Source IP, Source Port, Destination IP, Destination Port)`
• Behavior: Server listening socket (`listen()`) forks/spawns a distinct connected socket (`accept()`) for each unique client 4-tuple
• State: Full connection state, sequence tracking, and dedicated receive buffers per connection
• Scalability: Enables concurrent multi-client web/database servers
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: Transport Layer Services
M2.1.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Differentiate between host-to-host delivery and process-to-process delivery with a neat diagram. (6 Marks)
Q: Explain how multiplexing and demultiplexing work in UDP and TCP. Why does TCP require a 4-tuple while UDP needs only a 2-tuple? (8 Marks)
💡 Critical Conceptual Takeaways
✔ Network layer provides host-to-host IP delivery; Transport layer provides process-to-process port delivery.
✔ UDP demux uses Destination Port only; TCP demux uses Source IP, Source Port, Dest IP, Dest Port.
✔ TCP creates separate connected sockets for every distinct client connection.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 6
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.2
Transport Protocols & User Datagram Protocol (UDP)
UDP Segment Header Structure, 16-Bit 1's Complement Checksum with Pseudo-Header, UDP Applications & Use Cases
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 7
2.1.2.1 UDP Protocol Architecture & 8-Byte Header
M2.1.2 UDP ARCHITECTURE
• UDP Characteristics (RFC 768)
Connectionless, unreliable, lightweight, message-oriented transport protocol. Provides bare minimum services: process multiplexing and optional error checking.
• Why Use UDP?
1. No connection establishment delay (0-RTT), 2. No connection state at server, 3. Small header overhead (8 bytes vs TCP 20 bytes), 4. Unregulated send rate (no congestion throttling).
• UDP 8-Byte Header Format (32-bit width)
Source Port (16 bits) | Destination Port (16 bits) \n Length (16 bits, header + payload in bytes) | Checksum (16 bits).
• Message Boundary Preservation
UDP sends data in discrete datagrams. If sender writes 500 bytes twice, receiver reads 500 bytes twice (preserves message boundaries, unlike TCP byte stream).
Header Breakdown
→ Source Port: 16 bits
→ Destination Port: 16 bits
→ Length: 16 bits (Min 8 B)
→ Checksum: 16 bits
→ Total Header: Exactly 8 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 8
2.1.2.2 UDP 16-Bit 1's Complement Checksum Calculation
M2.1.2 CHECKSUM CALCULATION
📌 KTU Numerical Problem Statement
Compute the UDP checksum for three 16-bit words: Word 1 = 0x66B4 (0110 0110 1011 0100), Word 2 = 0x5555 (0101 0101 0101 0101), Word 3 = 0x8F0C (1000 1111 0000 1100). Show wraparound carry addition and 1's complement inversion. Also explain how the receiver verifies checksum integrity.
📐 Governing Formulas & Principles:
• Step 1: Sum 16-bit words using standard binary addition.
• Step 2: If sum produces a 17th bit (carry overflow), wrap it around and add to the least significant bit.
• Step 3: Invert all bits (1's complement) to obtain the transmitted Checksum field.
• Receiver: Sums all received words including Checksum; valid result must be 0xFFFF (all 1s).
📝 Step-by-Step Derivation & Solution
Step 1: Sum Word 1 + Word 2: 0x66B4 + 0x5555 = 0xBC09 (1011 1100 0000 1001)
Step 2: Add Word 3: 0xBC09 + 0x8F0C = 0x14B15 (1 0100 1011 0001 0101 - Carry generated!)
Step 3: Wrap carry around: 0x4B15 + 1 = 0x4B16 (0100 1011 0001 0110)
Step 4: Take 1's complement (~0x4B16): 1011 0100 1110 1001 = 0xB4E9 (Checksum transmitted)
Step 5: Receiver Verification: 0x4B16 + 0xB4E9 = 0xFFFF (1111 1111 1111 1111 -> Verified Valid!)
✅ FINAL ANSWER: Transmitted Checksum = 0xB4E9 | Receiver sum = 0xFFFF
💡 Exam Tip: Note: UDP includes an IP Pseudo-Header (Source IP, Dest IP, Protocol 17, UDP Length) in checksum calculation to detect misrouted packets.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 9
🎯 Exam Booster & Review: UDP Protocol & Checksum
M2.1.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the UDP segment header format and explain all fields. Why is UDP header size fixed at 8 bytes? (6 Marks)
Q: Explain the step-by-step procedure for computing the UDP 16-bit 1's complement checksum. What is the role of the pseudo-header? (8 Marks)
Q: Why is UDP preferred over TCP for DNS queries, SNMP, and real-time gaming? (5 Marks)
💡 Critical Conceptual Takeaways
✔ UDP header is minimal (8 bytes) with Source Port, Dest Port, Length, and Checksum.
✔ Checksum calculation wraps around carry bits and inverts result for easy receiver verification (0xFFFF).
✔ UDP avoids TCP connection overhead and latency fluctuations from retransmissions.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 10
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.3
Transmission Control Protocol (TCP) Architecture
TCP 20-Byte Header Format, 3-Way Handshake Connection Setup, 4-Way Connection Teardown (TIME_WAIT 2MSL), Sequence/ACK Mechanics
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 11
2.1.3.1 TCP Header Architecture (RFC 793 / 9293)
M2.1.3 TCP HEADER
• Connection-Oriented Byte Stream
TCP provides full-duplex, reliable, sequenced byte-stream transfer between communicating processes.
• Header Format (20 to 60 Bytes)
Source Port (16b) | Destination Port (16b) \n Sequence Number (32b: byte-stream offset) \n Acknowledgment Number (32b: next expected byte) \n Data Offset (4b: header length in 32-bit words) | Reserved (4b) | Flags (8b) | Window Size (16b) \n Checksum (16b) | Urgent Pointer (16b) \n Options (0 to 40 bytes: MSS, Window Scale, SACK, Timestamps).
• TCP Control Flags
SYN (Establish connection), ACK (Ack valid), FIN (Close connection), RST (Reset/abort connection), PSH (Push data immediately to app), URG (Urgent pointer active), ECE & CWR (Explicit Congestion Notification).
• Cumulative Acknowledgment
TCP Ack number $N$ indicates the receiver has successfully received all contiguous bytes up to $N-1$ and is expecting byte $N$.
TCP Control Flags
→ SYN: Connection request
→ ACK: Acknowledgment field
→ FIN: Graceful teardown
→ RST: Reset connection
→ PSH: Push buffer to app
→ URG: Out-of-band data
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 12
2.1.3.2 Connection Lifecycle: 3-Way Handshake vs 4-Way Teardown
M2.1.3 TCP LIFECYCLE
3-Way Handshake (Connection Setup)
• Step 1 (Client -> Server): Client sends `SYN = 1`, `Seq = x` (Initial Sequence Number $ISN_c$). Enters `SYN_SENT` state
• Step 2 (Server -> Client): Server allocates buffers, replies `SYN = 1`, `ACK = 1`, `Seq = y` ($ISN_s$), `Ack = x + 1`. Enters `SYN_RCVD`
• Step 3 (Client -> Server): Client sends `ACK = 1`, `Seq = x + 1`, `Ack = y + 1` (may piggyback initial application data). Enters `ESTABLISHED`
• SYN Flood Defense: TCP SYN Cookies prevent server memory exhaustion from bogus SYN requests
4-Way Connection Teardown (Graceful Close)
• Step 1 (Client -> Server): Client finishes sending, transmits `FIN = 1`, `Seq = u`. Enters `FIN_WAIT_1`
• Step 2 (Server -> Client): Server acknowledges with `ACK = 1`, `Ack = u + 1`. Enters `CLOSE_WAIT`; Client enters `FIN_WAIT_2`
• Step 3 (Server -> Client): Server finishes outstanding data, transmits `FIN = 1`, `Seq = v`. Enters `LAST_ACK`
• Step 4 (Client -> Server): Client replies `ACK = 1`, `Ack = v + 1`. Client enters `TIME_WAIT` for 2MSL (Maximum Segment Lifetime = 60-120s) before terminating to ensure final ACK delivery
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 13
🎯 Exam Booster & Review: TCP Connection Management
M2.1.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the complete TCP segment header format and explain all fields, especially Sequence Number, ACK Number, and Control Flags. (8 Marks)
Q: Illustrate the TCP 3-Way Handshake with sequence and acknowledgment numbers. Why is a 2-way handshake insufficient? (8 Marks)
Q: Explain the purpose of the `TIME_WAIT` state and the 2MSL timer during TCP connection termination. (5 Marks)
💡 Critical Conceptual Takeaways
✔ TCP Sequence number tracks the byte offset of transmitted data; ACK number represents the next expected byte.
✔ 3-way handshake is mandatory to synchronize Initial Sequence Numbers (ISNs) bi-directionally and verify full-duplex connectivity.
✔ `TIME_WAIT` (2MSL) guarantees that any lingering duplicate packets in the network expire before the socket is reused.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 14
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.4
TCP Flow & Congestion Control Mechanisms
Sliding Window Flow Control, Silly Window Syndrome, Congestion Window (cwnd), Slow Start, AIMD, Fast Retransmit, TCP Tahoe vs Reno
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 15
2.1.4.1 Flow Control & Silly Window Syndrome
M2.1.4 FLOW CONTROL
• Flow Control Goal
Matches the sender's transmission rate to the receiver's consumption rate to prevent receiver buffer overflow.
• Receive Window (`rwnd`) Mechanics
Receiver advertises remaining buffer space via `rwnd` field in TCP header. Sender ensures: $\text{LastByteSent} - \text{LastByteAcked} \le \min(\text{cwnd}, \text{rwnd})$.
• Zero-Window Probing
When receiver buffer is full (`rwnd = 0`), sender stops transmitting but periodically sends 1-byte probe segments to force receiver to return window update ACKs.
• Silly Window Syndrome (SWS)
Occurs when data is transmitted in tiny chunks (1 byte payload + 40 bytes header = 97.5% overhead).
• SWS Solutions
1. **Nagle's Algorithm (Sender-side)**: Send first small segment; buffer subsequent data until all previous data is ACKed or MSS is reached. 2. **Clark's Solution (Receiver-side)**: Receiver advertises `rwnd = 0` until buffer space is at least MSS or 50% buffer capacity.
Key Variables
→ rwnd: Receiver buffer limit
→ cwnd: Network congestion limit
→ Effective Win = min(cwnd, rwnd)
→ Nagle's: Buffers small writes
→ Clark's: Suppresses tiny rwnd
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 16
2.1.4.2 Congestion Control: TCP Tahoe vs TCP Reno
M2.1.4 TAHOE VS RENO
TCP Tahoe (Legacy)
• Slow Start Phase: Begins with `cwnd = 1 MSS`. Increases `cwnd` exponentially: doubles every RTT (`cwnd += 1 MSS` per ACK received)
• Congestion Avoidance: When `cwnd >= ssthresh`, transitions to AIMD: increases `cwnd` linearly by 1 MSS per RTT
• On Loss Detection (Timeout or 3 Dup ACKs): 1. `ssthresh = cwnd / 2` \n 2. Drops `cwnd = 1 MSS` (always resets to slow start)
• Performance: Severe throughput collapse upon any single packet loss
TCP Reno (Standard)
• Slow Start & Congestion Avoidance: Identical to Tahoe during normal growth
• On Timeout Loss: Severe congestion: `ssthresh = cwnd / 2`, `cwnd = 1 MSS` (resets to Slow Start)
• On 3 Duplicate ACKs (Fast Retransmit): Mild congestion: Retransmits lost segment immediately without waiting for retransmission timer to expire
• Fast Recovery Phase: Skips slow start! Sets `ssthresh = cwnd / 2`, sets `cwnd = ssthresh + 3 MSS`, continues linear AIMD growth
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 17
2.1.4.3 Worked KTU Numerical: TCP Congestion Window Evolution
M2.1.4 WORKED PROBLEM
📌 KTU Numerical Problem Statement
A TCP Reno connection has ssthresh = 16 MSS. Starting at RTT 1 with cwnd = 1 MSS in Slow Start: (a) Trace cwnd values up to RTT 8. (b) At RTT 8, three duplicate ACKs are received. Calculate new ssthresh and cwnd for RTT 9 and RTT 10 under Fast Recovery.
📐 Governing Formulas & Principles:
• Slow Start: cwnd doubles every RTT until ssthresh is reached.
• Congestion Avoidance (AIMD): cwnd increases by +1 MSS per RTT.
• Fast Retransmit / Fast Recovery (3 Dup ACKs): ssthresh_new = cwnd / 2, cwnd_new = ssthresh_new.
📝 Step-by-Step Derivation & Solution
Step 1: RTT 1: cwnd = 1 MSS (Slow Start)
Step 2: RTT 2: cwnd = 2 MSS | RTT 3: cwnd = 4 MSS | RTT 4: cwnd = 8 MSS | RTT 5: cwnd = 16 MSS (ssthresh reached)
Step 3: RTT 6: cwnd = 17 MSS (AIMD Linear) | RTT 7: cwnd = 18 MSS | RTT 8: cwnd = 19 MSS
Step 4: At RTT 8, 3 Dup ACKs occur: ssthresh_new = 19 / 2 = 9.5 -> 9 MSS.
Step 5: RTT 9: Under TCP Reno Fast Recovery, cwnd = 9 MSS. RTT 10: cwnd = 10 MSS (continues linear AIMD).
✅ FINAL ANSWER: RTT 8: 19 MSS -> Loss -> RTT 9: cwnd = 9 MSS, ssthresh = 9 MSS
💡 Exam Tip: If loss was caused by Timeout instead of 3 Dup ACKs, cwnd would drop to 1 MSS.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 18
🎯 Exam Booster & Review: TCP Flow & Congestion Control
M2.1.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain TCP Sliding Window flow control and how the receiver window `rwnd` prevents buffer overrun. (7 Marks)
Q: What is Silly Window Syndrome? Explain Nagle's algorithm and Clark's solution with examples. (8 Marks)
Q: Compare TCP Tahoe and TCP Reno congestion control algorithms with a neat graph plotting `cwnd` versus Transmission RTTs. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Flow control is receiver-driven (`rwnd`); Congestion control is network-driven (`cwnd`).
✔ Effective transmission window is the minimum of `cwnd` and `rwnd`.
✔ TCP Reno avoids slow start upon 3 duplicate ACKs via Fast Retransmit and Fast Recovery.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 19
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.5
Berkeley Socket API & I/O Multiplexing
Socket System Calls Lifecycle (TCP & UDP), I/O Multiplexing with select() and poll(), fd_set Macros, Non-Blocking Sockets
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 20
2.1.5.1 Berkeley Socket API System Call Lifecycle
M2.1.5 SOCKET API
• Socket Abstraction
A socket is a kernel endpoint for network I/O represented as an integer file descriptor in Linux (`int sockfd`).
• TCP Server Lifecycle
1. `socket(AF_INET, SOCK_STREAM, 0)` -> Creates endpoint \n 2. `bind(sockfd, &addr, sizeof)` -> Associates socket with IP/Port \n 3. `listen(sockfd, backlog)` -> Sets passive listening mode and backlog queue \n 4. `accept(sockfd, &client_addr, &len)` -> Blocks until client connects, returns new connected descriptor \n 5. `read()` / `write()` or `recv()` / `send()` -> Data exchange \n 6. `close(sockfd)` -> Tears down connection.
• TCP Client Lifecycle
1. `socket()` -> 2. `connect(sockfd, &server_addr, sizeof)` (initiates 3-way handshake) -> 3. `write()` / `read()` -> 4. `close()`.
• UDP Sockets
Connectionless: Server calls `socket()` -> `bind()` -> `recvfrom()` -> `sendto()`. Client calls `socket()` -> `sendto()` -> `recvfrom()` without `listen()` or `accept()`.
Key System Calls
→ socket(): Create fd
→ bind(): Bind IP & Port
→ listen(): Passive queue
→ accept(): Return client fd
→ connect(): 3-way handshake
→ sendto()/recvfrom(): UDP
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 21
2.1.5.2 I/O Multiplexing: `select()` System Call
M2.1.5 IO MULTIPLEXING
// Linux Socket & Protocol Implementation
#include <sys/select.h> int max_fd = listen_fd; fd_set read_fds; while (1) { FD_ZERO(&read_fds); FD_SET(listen_fd, &read_fds); // Add active client descriptors for (int i = 0; i < max_clients; i++) { if (client_fds[i] > 0) FD_SET(client_fds[i], &read_fds); if (client_fds[i] > max_fd) max_fd = client_fds[i]; } // Block until at least one descriptor is ready for read int activity = select(max_fd + 1, &read_fds, NULL, NULL, NULL); if (FD_ISSET(listen_fd, &read_fds)) { int new_fd = accept(listen_fd, ...); // Add new_fd to client list } }
⚙️ System Call & Execution Workflow
• Why I/O Multiplexing?: Allows a single-threaded server process to monitor multiple socket descriptors simultaneously without blocking on any single slow client.
• `fd_set` Bitmask Macros: `FD_ZERO(&set)` clears mask, `FD_SET(fd, &set)` adds fd, `FD_CLR(fd, &set)` removes fd, `FD_ISSET(fd, &set)` tests readiness.
• `select()` Parameters: `int select(int nfds, fd_set *readfds, fd_set *writefds, fd_set *exceptfds, struct timeval *timeout)`. `nfds` is `max_fd + 1`.
• `poll()` vs `select()`: `poll()` uses array of `struct pollfd` (no `FD_SETSIZE` 1024 descriptor limit and separate input/output events).
💡 Hands-on Insight: Single-threaded I/O multiplexing handles hundreds of concurrent connections with minimal memory overhead compared to multi-threading.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 22
🎯 Exam Booster & Review: Socket API & select()
M2.1.5
📚 KTU High-Yield Questions (K3 Apply)
Q: Write the sequence of Berkeley socket system calls executed on both server and client for TCP connection establishment and data transfer. (8 Marks)
Q: Explain the working of I/O multiplexing using the `select()` system call with code structure and `fd_set` macros. (8 Marks)
Q: Differentiate between blocking, non-blocking, and I/O multiplexed socket architectures. (6 Marks)
💡 Critical Conceptual Takeaways
✔ `listen()` creates a passive socket queue; `accept()` extracts the next connection from the queue.
✔ `select()` monitors multiple file descriptors simultaneously, unblocking as soon as any fd is ready.
✔ `poll()` and `epoll()` overcome the 1024 file descriptor limitation of traditional `select()`.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 23
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.1
Network Layer Architecture & Router Design
Data Plane (Forwarding) vs Control Plane (Routing), Datagram Networks vs Virtual Circuits, Router Fabrics & Buffer Queuing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 24
2.2.1.1 Network Layer: Data Plane vs Control Plane
M2.2.1 NETWORK ARCHITECTURE
• Network Layer Core Mission
Achieving end-to-end host-to-host packet delivery across multiple heterogeneous intermediate networks.
• Data Plane (Forwarding)
Local, per-router action. Takes a packet arriving on an input link interface and moves it to the appropriate output link interface in nanoseconds. Implemented in high-speed hardware ASIC/TCAM.
• Control Plane (Routing)
Network-wide logic. Determines the end-to-end global path that packets take from source to destination. Implemented in software routing algorithms (OSPF, RIP, BGP) or centralized SDN controllers.
• Service Models
Internet uses Best-Effort Service Model: no guarantees on delivery, delay, bandwidth, or ordering. Simplicity in the network core pushed intelligence to end hosts.
Plane Separation
→ Data Plane: Local forwarding (ASIC/Hardware)
→ Control Plane: Global routing (Software/OSPF)
→ Nanosecond speed in Data Plane
→ Millisecond speed in Control Plane
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 25
2.2.1.2 Network Models: Datagram vs Virtual Circuit
M2.2.1 DATAGRAM VS VC
Datagram Networks (Internet IP)
• Connection Setup: No connection setup phase; packets injected immediately
• Addressing: Packets carry full global 32-bit/128-bit Source and Destination IP
• Routing Path: Each packet routed independently; successive packets may follow different paths
• Router State: Stateless routers; failure of a link triggers automatic rerouting
• Complexity: Pushed to network edge end hosts
Virtual Circuit Networks (ATM / Frame Relay)
• Connection Setup: Mandatory end-to-end signaling setup before data transfer
• Addressing: Packets carry small local Virtual Circuit Identifier (VCI)
• Routing Path: All packets in a connection follow the exact same fixed virtual path
• Router State: Routers maintain per-connection state tables; link failure drops VC
• Complexity: Heavy complexity in network core switches
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 26
🎯 Exam Booster & Review: Network Layer Architecture
M2.2.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Differentiate between the Data Plane and Control Plane of the Network Layer. (6 Marks)
Q: Compare Datagram networks and Virtual Circuit networks with respect to connection setup, addressing, and router state. (8 Marks)
Q: Describe the internal architecture of a modern high-speed router (Input Ports, Switching Fabric, Output Ports). (7 Marks)
💡 Critical Conceptual Takeaways
✔ Forwarding is local and hardware-based; Routing is global and software-based.
✔ Internet uses datagram packet switching with stateless routers for maximum resilience.
✔ Crossbar switching fabrics eliminate internal shared bus contention in high-speed routers.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 27
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.2
IPv4 Addressing, Subnetting, CIDR & NAT
IPv4 20-60 Byte Header, Fragmentation & Reassembly, Classless Addressing (CIDR), Subnet Design, NAT/PAT, ICMP Protocol
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 28
2.2.2.1 IPv4 Header Format & Fragmentation
M2.2.2 IPV4 HEADER
• IPv4 Header Structure (20 to 60 Bytes)
Version (4b: 4) | IHL (4b: Header length in 32-bit words, min 5 = 20B) | DSCP/ECN (8b: QoS) | Total Length (16b: Header + Payload, max 65535B) \n Identification (16b) | Flags (3b: Reserved, DF, MF) | Fragment Offset (13b: measured in 8-byte units) \n TTL (8b: Time-to-Live, decremented per hop) | Protocol (8b: ICMP=1, TCP=6, UDP=17) | Header Checksum (16b) \n Source IP (32b) \n Destination IP (32b) \n Options (0-40B).
• Fragmentation Fields
**Identification**: Identifies fragments belonging to same original datagram. **DF (Don't Fragment)**: If set to 1, router drops packet if larger than MTU. **MF (More Fragments)**: 1 for all fragments except the final one (0). **Fragment Offset**: Byte offset divided by 8.
• Reassembly
Occurs strictly at the final destination host before delivering to the transport layer.
Key Header Fields
→ IHL: Header words (x4 bytes)
→ Total Length: Max 65,535 B
→ TTL: Prevents routing loops
→ Protocol: 6=TCP, 17=UDP, 1=ICMP
→ Offset unit = 8 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 29
2.2.2.2 Worked KTU Numerical: IPv4 Fragmentation
M2.2.2 FRAGMENTATION PROBLEM
📌 KTU Numerical Problem Statement
An IPv4 datagram with Total Length = 4000 bytes (20-byte IP header + 3980 bytes payload) arrives at a router whose outgoing link has Maximum Transmission Unit MTU = 1500 bytes. Calculate the Total Length, Payload Length, MF flag, and Fragment Offset for all resulting fragments.
📐 Governing Formulas & Principles:
• MTU = 1500 bytes (Max payload per fragment = 1500 - 20 = 1480 bytes).
• 1480 is divisible by 8 (1480 / 8 = 185) -> Valid maximum payload per fragment.
• Total payload to fragment = 3980 bytes.
• Fragment Offset = Total previous payload bytes divided by 8.
📝 Step-by-Step Derivation & Solution
Step 1: Frag 1: Header = 20 B, Payload = 1480 B, Total Length = 1500 B, MF = 1, Offset = 0 / 8 = 0
Step 2: Frag 2: Header = 20 B, Payload = 1480 B, Total Length = 1500 B, MF = 1, Offset = 1480 / 8 = 185
Step 3: Remaining payload = 3980 - 1480 - 1480 = 1020 B.
Step 4: Frag 3: Header = 20 B, Payload = 1020 B, Total Length = 1040 B, MF = 0 (last fragment!), Offset = 2960 / 8 = 370
✅ FINAL ANSWER: Frag 1: Len 1500, MF=1, Off=0 | Frag 2: Len 1500, MF=1, Off=185 | Frag 3: Len 1040, MF=0, Off=370
💡 Exam Tip: Always verify that Fragment Offset values are integer multiples of 8 bytes!
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 30
2.2.2.3 Worked KTU Numerical: CIDR Subnetting
M2.2.2 SUBNETTING PROBLEM
📌 KTU Numerical Problem Statement
An organization is allocated the block `200.50.16.0/24`. Design 4 equal-sized subnets. For each subnet, specify: (a) Subnet Mask, (b) Network Address, (c) Usable Host Range, (d) Direct Broadcast Address, (e) Maximum usable hosts.
📐 Governing Formulas & Principles:
• Given /24 network: 8 host bits (256 addresses).
• To create 4 subnets: Need 2 subnet bits (2^2 = 4). New prefix = /24 + 2 = /26.
• Block size per subnet = 256 / 4 = 64 addresses.
• Usable hosts per subnet = 2^(32 - 26) - 2 = 64 - 2 = 62 hosts.
📝 Step-by-Step Derivation & Solution
Step 1: Subnet Mask: 255.255.255.192 (/26)
Step 2: Subnet 1: Net = 200.50.16.0/26 | Hosts = 200.50.16.1 to 200.50.16.62 | Broadcast = 200.50.16.63
Step 3: Subnet 2: Net = 200.50.16.64/26 | Hosts = 200.50.16.65 to 200.50.16.126 | Broadcast = 200.50.16.127
Step 4: Subnet 3: Net = 200.50.16.128/26 | Hosts = 200.50.16.129 to 200.50.16.190 | Broadcast = 200.50.16.191
Step 5: Subnet 4: Net = 200.50.16.192/26 | Hosts = 200.50.16.193 to 200.50.16.254 | Broadcast = 200.50.16.255
✅ FINAL ANSWER: 4 Subnets of /26 mask (255.255.255.192), each accommodating 62 usable hosts
💡 Exam Tip: First address is Network ID; Last address is Directed Broadcast; both cannot be assigned to hosts.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 31
🎯 Exam Booster & Review: IPv4, CIDR & NAT
M2.2.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the complete IPv4 header format and explain all fields with numerical significance. (8 Marks)
Q: Explain the working of Network Address Translation (NAT) and Port Address Translation (PAT) with translation table examples. (7 Marks)
Q: What is ICMP? Explain its role in error reporting (Destination Unreachable, Time Exceeded) and diagnostic tools (`ping`, `traceroute`). (6 Marks)
💡 Critical Conceptual Takeaways
✔ IPv4 fragmentation uses ID, Flags (DF, MF), and Offset in 8-byte blocks.
✔ CIDR replaces classful boundaries with arbitrary prefix lengths (/N) and Longest Prefix Matching.
✔ NAT allows private IP subnets (RFC 1918) to share a single public IP using port mapping tables.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 32
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.3
Unicast Routing Protocols & Algorithms
Link-State Routing & Dijkstra's Algorithm, Distance-Vector & Bellman-Ford, Count-to-Infinity, RIP, OSPF & BGP-4
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 33
2.2.3.1 Link-State (LS) vs Distance-Vector (DV) Algorithms
M2.2.3 LS VS DV ROUTING
Link-State (LS) Routing (e.g., OSPF)
• Global Topology Knowledge: Every router floods link-state advertisements (LSAs); all nodes possess full network topology graph
• Algorithm: Dijkstra's Shortest Path Algorithm run locally on each router
• Convergence Speed: Ultra-fast convergence; zero routing loops
• Message Overhead: $O(N \cdot E)$ messages flooded periodically
• Complexity: $O(V^2)$ or $O(E \log V)$ computation per router
Distance-Vector (DV) Routing (e.g., RIP)
• Local Knowledge Only: Routers only know cost to immediate direct neighbors; exchange vectors periodically
• Algorithm: Distributed Bellman-Ford equation: $d_x(y) = \min_v \{c(x,v) + d_v(y)\}$
• Convergence Speed: Slow convergence; susceptible to Count-to-Infinity problem
• Mitigation: Split Horizon and Poisoned Reverse rules
• Simplicity: Lightweight computation; suitable for small networks
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 34
2.2.3.2 Internet Routing Protocols: RIP vs OSPF vs BGP-4
M2.2.3 PROTOCOL COMPARISON
• RIP (Routing Information Protocol - RFC 2453)
Intra-AS Distance Vector protocol. Uses Hop Count metric (max 15 hops; 16 = infinity). Updates broadcast every 30s over UDP port 520.
• OSPF (Open Shortest Path First - RFC 2328)
Intra-AS Link State protocol. Uses link cost based on inverse bandwidth. Hierarchical design with Area 0 (Backbone Area) and non-backbone areas. Runs directly over IP protocol 89. Supports authenticated LSA flooding and ECMP (Equal-Cost Multi-Path).
• BGP-4 (Border Gateway Protocol - RFC 4271)
Inter-AS Path Vector protocol glueing the global Internet together. Operates over reliable TCP port 179. Advertises AS-PATH attributes to prevent loops and enforces policy-based business routing between Autonomous Systems (eBGP and iBGP).
Protocol Matrix
→ RIP: DV, Hop count (Max 15), UDP 520
→ OSPF: LS, Dijkstra, IP 89, Areas
→ BGP: Path Vector, AS-PATH, TCP 179
→ Intra-AS: RIP, OSPF
→ Inter-AS: BGP-4
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 35
🎯 Exam Booster & Review: Unicast Routing Protocols
M2.2.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain Dijkstra's shortest path algorithm with a step-by-step table derivation for a 5-node network graph. (9 Marks)
Q: What is the Count-to-Infinity problem in Distance Vector routing? Explain how Split Horizon and Poisoned Reverse mitigate it. (8 Marks)
Q: Compare RIP, OSPF, and BGP-4 with respect to routing algorithm, metric, transport protocol, and scalability. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Dijkstra computes shortest path trees using complete topological knowledge.
✔ Distance vector iterates Bellman-Ford equations among adjacent neighbors.
✔ OSPF structures networks into areas with Area 0 backbone to scale within large enterprises.
✔ BGP-4 implements policy routing and loop prevention across Autonomous Systems using AS-PATH.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 36
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.4
Multicast Routing Protocols & IGMP
Multicast Addressing (Class D), IGMP Host-Router Membership, Source-Based Trees vs Group-Shared Trees, RPF, PIM-DM vs PIM-SM
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 37
2.2.4.1 Multicast Fundamentals & IGMP Protocol
M2.2.4 MULTICAST BASICS
• Multicast Concept
Delivering a single stream of datagrams from one or more sources to a specific group of interested receivers simultaneously without duplicate packet transmission on shared links.
• Multicast Addressing
IPv4 Class D range `224.0.0.0` to `239.255.255.255`. Special groups: `224.0.0.1` (All systems on subnet), `224.0.0.2` (All routers).
• IGMP (Internet Group Management Protocol - RFC 3376)
Operates locally between end hosts and their attached first-hop multicast router. Hosts send IGMP Membership Reports; router sends periodic Membership Queries.
• Multicast Routing Trees
1. **Source-Based Tree (Shortest Path Tree)**: Builds a separate tree rooted at each sender source (used in DVMRP, PIM-DM). 2. **Group-Shared Tree (Core-Based Tree)**: All sources transmit to a shared Rendezvous Point (RP) / Core router (used in PIM-SM).
• Reverse Path Forwarding (RPF)
Loop-prevention rule: Router accepts a multicast packet only if it arrived on the interface that is the shortest path back to the sender source.
Key Mechanisms
→ Class D: 224.0.0.0/4
→ IGMP: Local group membership
→ Source Tree: Optimal delay per source
→ Shared Tree: Minimal router state
→ RPF: Prevents multicast loops
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 38
2.2.4.2 PIM Protocols: Dense Mode (PIM-DM) vs Sparse Mode (PIM-SM)
M2.2.4 PIM DENSE VS SPARSE
PIM Dense Mode (PIM-DM / Flood & Prune)
• Assumed Environment: Receivers densely populated across almost every subnet
• Tree Construction: Source-Based Shortest Path Trees
• Mechanics: 1. **Flood**: Broadcasts multicast traffic everywhere \n 2. **Prune**: Routers with no interested members send Prune messages back upstream \n 3. **Graft**: New receivers send Graft to re-attach
• Overhead: High periodic flooding overhead
PIM Sparse Mode (PIM-SM / Explicit Join)
• Assumed Environment: Receivers sparsely distributed across wide area WAN
• Tree Construction: Group-Shared Tree rooted at Rendezvous Point (RP)
• Mechanics: 1. Receivers send explicit `IGMP Join` -> Router sends `PIM Join` towards RP \n 2. Sources register with RP \n 3. Traffic flows down shared tree
• Overhead: Zero flooding; highly scalable for enterprise IPTV
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 39
🎯 Exam Booster & Review: Multicast Routing
M2.2.4
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the role of IGMP in managing multicast group memberships on local subnets. (6 Marks)
Q: Compare Source-Based Trees and Group-Shared Trees in multicast routing. (7 Marks)
Q: Explain the working of PIM-DM (Flood and Prune) versus PIM-SM (Rendezvous Point and Explicit Joins). (8 Marks)
💡 Critical Conceptual Takeaways
✔ IGMP connects local hosts to their edge multicast router.
✔ Source-based trees minimize latency per sender; Shared trees minimize router state.
✔ RPF algorithm discards packets that do not arrive on the shortest return path to the source.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 40
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.5
Next Generation IP: IPv6 Architecture
IPv6 128-Bit Addressing, 40-Byte Fixed Header, Extension Headers, IPv4 vs IPv6 Comparison, Transition Strategies (Dual Stack, Tunneling, NAT64)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 41
2.2.5.1 IPv6 Addressing & 40-Byte Fixed Header
M2.2.5 IPV6 ARCHITECTURE
• Motivation for IPv6
Exhaustion of the 32-bit IPv4 address space ($2^{32} \approx 4.3 \times 10^9$ addresses). IPv6 provides $2^{128} \approx 3.4 \times 10^{38}$ unique addresses.
• IPv6 Address Notation
8 groups of 4 hexadecimal digits separated by colons (e.g., `2001:0db8:85a3:0000:0000:8a2e:0370:7334`). Leading zeros omitted (`2001:db8:85a3::8a2e:370:7334`); `::` compresses consecutive zero blocks once.
• 40-Byte Fixed Header Format
Version (4b: 6) | Traffic Class (8b: QoS DSCP) | Flow Label (20b: identifies packet flow for non-default routing) \n Payload Length (16b: data + extension headers) | Next Header (8b: specifies upper layer or extension header) | Hop Limit (8b: decremented per hop, replaces TTL) \n Source IPv6 Address (128 bits / 16 bytes) \n Destination IPv6 Address (128 bits / 16 bytes).
• Key Structural Improvements
No header checksum (speeds up router processing), no in-network fragmentation (handled via Path MTU Discovery by end hosts), fixed 40-byte base size.
Header Breakdown
→ Fixed Header: Exactly 40 Bytes
→ Source IP: 128 bits (16 B)
→ Destination IP: 128 bits (16 B)
→ Hop Limit: Replaces TTL
→ Next Header: Chains extensions
→ Flow Label: 20-bit stream tagging
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 42
2.2.5.2 IPv4 vs IPv6 & Transition Strategies
M2.2.5 IPV4 VS IPV6
IPv4 vs IPv6 Header Comparison
• Address Size: IPv4: 32 bits (4 Bytes) vs IPv6: 128 bits (16 Bytes)
• Header Length: IPv4: Variable 20-60B (IHL field) vs IPv6: Fixed 40 Bytes
• Checksum: IPv4: 16-bit header checksum vs IPv6: Removed entirely
• Fragmentation: IPv4: Routers fragment packets vs IPv6: End systems only (PMTUD)
• Broadcast: IPv4: Broadcast supported vs IPv6: Replaced by Multicast & Anycast
IPv4 to IPv6 Migration Mechanisms
• Dual Stack: Nodes run both IPv4 and IPv6 protocol stacks simultaneously on all interfaces
• Tunneling (6to4 / Teredo): IPv6 datagrams encapsulated as payload inside IPv4 packets across legacy IPv4 transit networks
• Header Translation (NAT64/DNS64): Translates IPv6 packet headers directly to IPv4 headers for legacy server interoperation
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 43
🎯 Exam Booster & Review: IPv6 Architecture
M2.2.5
📚 KTU High-Yield Questions (K2 Understand)
Q: Draw the IPv6 fixed header format and explain all fields. How does it improve router forwarding performance over IPv4? (8 Marks)
Q: Compare IPv4 and IPv6 across addressing, header structure, fragmentation, and error checking. (8 Marks)
Q: Explain the three transition mechanisms from IPv4 to IPv6: Dual Stack, Tunneling, and NAT64. (7 Marks)
💡 Critical Conceptual Takeaways
✔ IPv6 fixed 40-byte header streamlines hardware ASIC forwarding.
✔ Extension headers (Hop-by-Hop, Routing, Fragment, ESP, AH) are daisy-chained via `Next Header`.
✔ Dual stack and encapsulation tunneling enable smooth evolutionary migration from IPv4.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 44
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.6
Quality of Service (QoS) & Traffic Shaping
QoS Metrics (Delay, Jitter, Loss), Traffic Policing vs Shaping, Leaky Bucket vs Token Bucket, Scheduling (FIFO, WFQ), DiffServ vs IntServ
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 45
2.2.6.1 Traffic Shaping: Leaky Bucket vs Token Bucket
M2.2.6 TRAFFIC SHAPING
Leaky Bucket Algorithm (Constant Output)
• Concept: A bucket with a hole at the bottom; incoming packets buffer up to bucket capacity $C$ and leak out at a strictly constant rate $\rho$
• Output Profile: Strictly constant, smooth output stream regardless of incoming burstiness
• Burst Handling: Eliminates bursts entirely; discards packets if bucket overflows
• Suitability: Constant Bit Rate (CBR) traffic like uncompressed voice
Token Bucket Algorithm (Burst-Tolerant)
• Concept: Tokens generate at rate $r$ tokens/sec up to max token capacity $b$. A packet of size $m$ bytes consumes $m$ tokens to transmit
• Output Profile: Allows short-term traffic bursts up to bucket size $b$ while enforcing average long-term rate $r$
• Burst Handling: Max burst transmission speed = link wire rate $R$ for duration $T = b / (R - r)$
• Suitability: Variable Bit Rate (VBR) video streaming and web traffic
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 46
2.2.6.2 Worked KTU Numerical: Token Bucket Burst Calculation
M2.2.6 TOKEN BUCKET NUMERICAL
📌 KTU Numerical Problem Statement
A token bucket has token arrival rate r = 2 MB/sec and token bucket capacity b = 16 MB. The transmission link wire rate is R = 10 MB/sec. Calculate: (a) Maximum burst duration at wire rate R, (b) Maximum total data transmitted during this burst period.
📐 Governing Formulas & Principles:
• Burst duration formula: T = b / (R - r)
• Where b = bucket size (MB), R = peak transmission rate (MB/s), r = token replenishment rate (MB/s).
• Total data transmitted during burst: D = R * T = (b * R) / (R - r).
📝 Step-by-Step Derivation & Solution
Step 1: b = 16 MB, R = 10 MB/s, r = 2 MB/s
Step 2: T = 16 / (10 - 2) = 16 / 8 = 2.0 seconds
Step 3: Total data transmitted = R * T = 10 MB/s * 2.0 s = 20 MB
Step 4: Verification: Initial tokens (16 MB) + Newly generated tokens in 2s (2 MB/s * 2s = 4 MB) = 20 MB.
✅ FINAL ANSWER: Max Burst Duration T = 2.0 seconds | Total Burst Data = 20 MB
💡 Exam Tip: After 2 seconds, the transmission rate drops strictly to the average token rate r = 2 MB/sec.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 47
🎯 Exam Booster & Review: Quality of Service (QoS)
M2.2.6
📚 KTU High-Yield Questions (K3 Apply)
Q: Differentiate between Traffic Policing and Traffic Shaping with neat diagrams. (6 Marks)
Q: Compare Leaky Bucket and Token Bucket traffic shaping algorithms with equations and operating principles. (8 Marks)
Q: Explain Differentiated Services (DiffServ) architecture: Packet Classification, DSCP marking, and Per-Hop Behaviors (EF & AF). (7 Marks)
💡 Critical Conceptual Takeaways
✔ Leaky bucket produces rigid constant output; Token bucket permits regulated bursts.
✔ Weighted Fair Queuing (WFQ) guarantees minimum bandwidth shares to different service classes.
✔ DiffServ scales across WANs by classifying packets at boundary routers and using 6-bit DSCP markings.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 48
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.3
Linux Kernel TCP/IP Stack & Routing Implementation
Linux Network Packet Flow, sk_buff Data Structure, net_device, Forwarding Information Base (FIB), Route Cache, Linux iproute2
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 49
2.3.1 Linux Kernel Network Subsystem Architecture
M2.3 LINUX KERNEL STACK
• The `sk_buff` (Socket Buffer) Structure
The universal data structure representing network packets in Linux. Contains pointers: `head`, `data`, `tail`, `end`. Allows zero-copy header prepending/stripping across layers simply by moving the `data` pointer.
• Packet Ingress Flow (RX)
NIC receives frame -> DMA transfer to Ring Buffer -> Triggers Hard IRQ -> NAPI poll scheduled (SoftIRQ `NET_RX_SOFTIRQ`) -> `netif_receive_skb()` -> L3 `ip_rcv()` -> L4 `tcp_v4_rcv()` -> Socket receive queue -> `read()`.
• Packet Egress Flow (TX)
App calls `write()` -> L4 `tcp_sendmsg()` creates `sk_buff` -> L3 `ip_queue_xmit()` routes packet -> L2 `dev_queue_xmit()` enqueues to `qdisc` -> NIC DMA transmit -> Hardware TX IRQ.
• Forwarding Information Base (FIB)
The core kernel routing table in Linux organized as a fast LC-trie (Level-Compressed Trie) supporting sub-microsecond Longest Prefix Matching.
• Policy-Based Routing (PBR)
Linux supports multiple routing tables selected via `ip rule` based on source IP, TOS, fwmark, or incoming interface.
Kernel Data Structures
→ sk_buff: Packet descriptor
→ net_device: Hardware NIC abstraction
→ FIB: Kernel routing table trie
→ qdisc: Traffic queuing discipline
→ NAPI: Interrupt mitigation polling
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 50
2.3.2 Hands-On: Linux Kernel Routing with `iproute2`
M2.3 LINUX IPROUTE2
// Linux Socket & Protocol Implementation
# Linux iproute2 Advanced Routing Commands # 1. Inspect kernel routing table ip route show # 2. Add static route via gateway ip route add 192.168.10.0/24 via 10.0.0.1 dev eth0 # 3. Create Policy-Based Routing (PBR) table echo "200 custom_table" >> /etc/iproute2/rt_tables ip rule add from 192.168.1.50 table custom_table ip route add default via 10.0.0.254 dev eth1 table custom_table # 4. Flush and inspect route cache ip route flush cache
⚙️ System Call & Execution Workflow
• `ip route` Suite: Replaces deprecated `route` and `ifconfig` tools with direct Netlink socket communication to kernel.
• Custom Routing Tables: Linux supports up to 255 independent routing tables for multi-homing and ISP failover.
• `ip rule` Subsystem: Evaluates routing policy database (RPDB) rules sequentially to select appropriate routing table.
• Route Cache Behavior: Historical kernels maintained route hash cache; modern kernels use ultra-fast lockless FIB trie lookups.
💡 Hands-on Insight: Kernel `sk_buff` zero-copy architecture allows Linux to process millions of packets per second per CPU core.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 51
🎯 Exam Booster & Review: Linux Kernel Routing Stack
M2.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the architecture and role of the `sk_buff` data structure in Linux packet processing. (7 Marks)
Q: Trace the step-by-step path of an incoming packet from physical NIC reception to application socket delivery in the Linux kernel. (8 Marks)
Q: Demonstrate Policy-Based Routing (PBR) in Linux using `ip rule` and `ip route` commands. (6 Marks)
💡 Critical Conceptual Takeaways
✔ `sk_buff` avoids costly memory copies across protocol layers using internal buffer pointers.
✔ NAPI SoftIRQs prevent interrupt livelock during heavy packet bursts.
✔ FIB LC-trie enables sub-microsecond Longest Prefix Matching across hundreds of thousands of BGP routes.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET