## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 MASTER • MODULE 3 MASTER DECK
Data Link Layer, MAC Protocols & Wireless LANs
Complete Lecture Slides for KTU PCCST501 Computer Networks | Topics M3.1 through M3.9
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.1
Data Link Layer Design & Framing Techniques
Node-to-Node Link Services, Character Count, Byte Stuffing (Flag/ESC), Bit Stuffing (HDLC), Physical Coding Violations
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 3
3.1.1 Data Link Layer Design & Link Abstraction
M3.1 FRAMING BASICS
• Node-to-Node Service Mission
Responsible for transferring datagrams from one node (host, router, switch) to an adjacent node over an individual physical communication link.
• Link Layer Responsibilities
1. **Framing**: Encapsulating L3 datagrams into L2 frames with header and trailer. 2. **Link Access**: MAC protocols coordinate shared medium access. 3. **Reliable Delivery**: Flow control and ARQ on error-prone wireless links. 4. **Error Detection & Correction**: Parity, Checksum, CRC, Hamming codes.
• Framing Methods Overview
1. Character Count, 2. Byte Stuffing (Character-oriented), 3. Bit Stuffing (Bit-oriented), 4. Physical Layer Coding Violations (e.g., Manchester invalid transitions).
Framing Taxonomy
→ Byte Count: Header count field
→ Byte Stuffing: Flag + ESC bytes
→ Bit Stuffing: 5 consecutive 1s rule
→ Physical Violations: Line coding
→ FCS: CRC trailer at end
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
3.1.2 Stuffing Techniques: Byte Stuffing vs Bit Stuffing
M3.1 STUFFING COMPARISON
Byte Stuffing (Character-Oriented Framing)
• Delimiter: Frame begins and ends with dedicated Flag Byte `FLAG` (e.g., `0x7E` in PPP)
• Escape Mechanism: If `FLAG` occurs inside payload data, sender inserts an Escape Byte `ESC` (`0x7D`) immediately before it
• ESC in Data: If `ESC` itself appears in data, sender escapes it with another `ESC` (`ESC ESC`)
• Receiver Action: Receiver strips any `ESC` byte and treats following byte as raw data
Bit Stuffing (Bit-Oriented Framing / HDLC)
• Delimiter Pattern: Frame delimited by 8-bit flag pattern `01111110` (`0x7E`) at start and end
• Sender Rule: Whenever sender encounters **5 consecutive 1s** in data stream (`11111`), it automatically stuffs a **`0` bit** immediately after it
• Receiver Rule: Whenever receiver detects 5 consecutive 1s: if 6th bit is `0`, it de-stuffs (discards) the `0`; if 6th bit is `1` and 7th is `0`, it recognizes `FLAG`
• Advantage: Completely arbitrary payload length; zero character-set dependency
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: Data Link Layer Framing
M3.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the four framing methods used in the Data Link Layer with neat diagrams. (8 Marks)
Q: Given the data bit stream `01101111110111110010`, show the transmitted bit sequence after bit stuffing in HDLC. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Bit stuffing inserts a 0 after five consecutive 1s to prevent false flag detection.
✔ Byte stuffing uses escape characters (`ESC`) to preserve transparency in character protocols.
✔ Framing enables receivers to reliably locate the start and end of frames in raw bit streams.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 6
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.2
Data Link Control: Error Detection, Correction & Flow Control
Hamming Distance, 2D Parity, Internet Checksum, CRC-32 Modulo-2 Division, Hamming (7,4) Code, Stop-and-Wait, Go-Back-N, Selective Repeat
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 7
3.2.1 Block Coding & Hamming Distance Theory
M3.2 ERROR CONTROL THEORY
• Block Coding Principles
Dataword of $k$ bits encoded into Codeword of $n$ bits ($n > k$) by appending $r = n - k$ redundant parity bits.
• Hamming Distance $d(x,y)$
The number of bit positions in which two codewords $x$ and $y$ differ (computed by taking XOR and counting number of 1s).
• Minimum Hamming Distance ($d_{min}$)
The smallest Hamming distance between any pair of valid codewords in the codebook.
• Error Detection Capability
To detect up to $s$ bit errors: $d_{min} \ge s + 1$ (e.g., Simple Parity has $d_{min} = 2$, detects single-bit errors $s = 1$).
• Error Correction Capability
To correct up to $t$ bit errors: $d_{min} \ge 2t + 1$ (e.g., Single-bit error correction $t = 1$ requires $d_{min} \ge 3$).
Hamming Distance Rules
→ Detect s errors: d_min >= s + 1
→ Correct t errors: d_min >= 2t + 1
→ Simple Parity: d_min = 2
→ Hamming (7,4): d_min = 3
→ r parity bits: 2^r >= k + r + 1
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 8
3.2.2 Worked KTU Numerical: CRC Modulo-2 Polynomial Division
M3.2 CRC WORKED PROBLEM
📌 KTU Numerical Problem Statement
A data bit stream D = 10100100 is to be transmitted using CRC generator polynomial G(x) = x^4 + x^2 + 1 (binary generator G = 10101). (a) Determine the 4-bit CRC Checksum (Frame Check Sequence FCS), (b) What codeword is transmitted? (c) Show that receiver detects zero remainder in the absence of bit errors.
📐 Governing Formulas & Principles:
• Generator G(x) = x^4 + x^2 + 1 -> Degree r = 4 -> Generator bit string G = 10101 (5 bits).
• Step 1: Append r = 4 zeros to data D: D' = 10100100 0000 (12 bits).
• Step 2: Perform Modulo-2 binary division (XOR operations) of D' by G.
• Step 3: Remainder of division is the 4-bit CRC Checksum R.
📝 Step-by-Step Derivation & Solution
Step 1: Dividend: 101001000000 | Divisor: 10101
Step 2: 10100 XOR 10101 -> Remainder 00001; bring down bits -> 0001100...
Step 3: Continuing Modulo-2 XOR division yields 4-bit Remainder R = 1100.
Step 4: Transmitted Codeword T = Data + CRC = 10100100 1100 (12 bits).
Step 5: Receiver Divides T (101001001100) by G (10101) -> Remainder = 0000 (Valid / No errors!).
✅ FINAL ANSWER: CRC Checksum = 1100 | Transmitted Codeword = 101001001100
💡 Exam Tip: Modulo-2 addition and subtraction are both identical to bitwise XOR with zero carries/borrows.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 9
3.2.3 Worked KTU Numerical: Hamming (7,4) Single-Bit Error Correction
M3.2 HAMMING CODE WORKED
📌 KTU Numerical Problem Statement
A 4-bit dataword D = 1011 (d4=1, d3=0, d2=1, d1=1) is encoded using Hamming (7,4) code with parity bits at positions 1, 2, 4. (a) Generate 7-bit codeword. (b) If received word is R = 1011011, calculate syndrome bits (s3, s2, s1) and locate the erroneous bit position.
📐 Governing Formulas & Principles:
• Bit positions 1 to 7: p1 (pos 1), p2 (pos 2), d1 (pos 3), p4 (pos 4), d2 (pos 5), d3 (pos 6), d4 (pos 7).
• p1 checks positions with bit 1 set (1, 3, 5, 7): p1 = d1 XOR d2 XOR d4.
• p2 checks positions with bit 2 set (2, 3, 6, 7): p2 = d1 XOR d3 XOR d4.
• p4 checks positions with bit 4 set (4, 5, 6, 7): p4 = d2 XOR d3 XOR d4.
• Syndrome S = (s4 s2 s1) indicates decimal error bit position (0 = no error).
📝 Step-by-Step Derivation & Solution
Step 1: p1 = 1 XOR 1 XOR 1 = 1 | p2 = 1 XOR 0 XOR 1 = 0 | p4 = 1 XOR 0 XOR 1 = 0
Step 2: Generated Codeword: (p1, p2, d1, p4, d2, d3, d4) = (1, 0, 1, 0, 1, 0, 1) -> 1010101
Step 3: Received Word R = (r1..r7) = (1, 1, 0, 1, 1, 0, 1) (bit 2 corrupted!)
Step 4: s1 = r1 XOR r3 XOR r5 XOR r7 = 1 XOR 0 XOR 1 XOR 1 = 1
Step 5: s2 = r2 XOR r3 XOR r6 XOR r7 = 1 XOR 0 XOR 0 XOR 1 = 0
Step 6: s4 = r4 XOR r5 XOR r6 XOR r7 = 1 XOR 1 XOR 0 XOR 1 = 1 -> Syndrome = 101_2 = Pos 5 (d2 corrupted!)
✅ FINAL ANSWER: Syndrome S = 101 (Binary 5) -> Bit position 5 is inverted and corrected!
💡 Exam Tip: Hamming (7,4) code can correct any single-bit error and detect any double-bit error.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 10
3.2.4 Sliding Window Flow Control: Stop-and-Wait vs GBN vs Selective Repeat
M3.2 ARQ PROTOCOLS
Stop-and-Wait ARQ
• Window Size: $W_s = 1$, $W_r = 1$
• Sequence Bits: 1-bit ($m=1$, sequence numbers 0 and 1)
• Efficiency: Extremely low on high-bandwidth-delay product links: $\eta = 1 / (1 + 2a)$ where $a = t_{prop} / t_{trans}$
• Buffering: 1 frame buffer at sender and receiver
Go-Back-N (GBN) ARQ
• Window Size: $W_s = 2^m - 1$, $W_r = 1$ (Cumulative ACKs)
• On Loss: Discards all subsequent out-of-order frames; retransmits entire window from lost frame
• Sender Buffer: Buffers $W_s$ frames; receiver requires zero buffer
• Efficiency: High efficiency unless error rate is severe
Selective Repeat (SR) ARQ
• Window Size: $W_s = 2^{m-1}$, $W_r = 2^{m-1}$ (Individual ACKs)
• On Loss: Receiver buffers out-of-order frames; sender retransmits **only the lost frame**
• Buffer Needs: Both sender and receiver maintain $2^{m-1}$ buffer queues
• Efficiency: Optimal bandwidth utilization on noisy channels
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 11
🎯 Exam Booster & Review: Error Detection & Flow Control
M3.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain CRC error detection with a polynomial division example. Why is CRC implemented in hardware with LFSR shift registers? (8 Marks)
Q: Derive the maximum sender window size for Go-Back-N ($2^m - 1$) and Selective Repeat ($2^{m-1}$). Explain why exceeding these limits causes protocol failure. (8 Marks)
Q: Explain Hamming (7,4) code with syndrome error correction calculation. (7 Marks)
💡 Critical Conceptual Takeaways
✔ CRC detects all single-bit, double-bit, odd numbers of errors, and burst errors up to generator polynomial degree $r$.
✔ Go-Back-N window is $2^m - 1$ to prevent receiver from mistaking duplicate frames for new ones.
✔ Selective Repeat requires equal sender and receiver window sizes bounded at $2^{m-1}$.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 12
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.3
Multiple Access Control (MAC) Protocols
Random Access (Pure & Slotted ALOHA, CSMA, CSMA/CD, CSMA/CA), Controlled Access (Polling, Token Ring), Channelization (CDMA)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 13
3.3.1 Random Access: Pure ALOHA vs Slotted ALOHA
M3.3 ALOHA COMPARISON
Pure ALOHA (Norman Abramson, 1970)
• Transmission Rule: Transmit continuous frame whenever data is ready without sensing channel
• Vulnerable Period: $V_p = 2 \times T_{frame}$ (Collision occurs if any other node transmits within 2 frame times)
• Throughput Formula: $S = G \cdot e^{-2G}$ where $G$ = traffic load
• Maximum Efficiency: Maximum throughput $S_{max} = 1 / (2e) \approx 18.4\%$ at $G = 0.5$
• Collisions: High collision rate due to uncoordinated overlapping frames
Slotted ALOHA (Roberts, 1972)
• Transmission Rule: Time divided into discrete slots equal to $T_{frame}$. Nodes transmit strictly at slot boundaries
• Vulnerable Period: $V_p = 1 \times T_{frame}$ (Halves vulnerability interval)
• Throughput Formula: $S = G \cdot e^{-G}$
• Maximum Efficiency: Maximum throughput $S_{max} = 1 / e \approx 36.8\%$ at $G = 1.0$ (Exactly doubles Pure ALOHA!)
• Synchronization: Requires global slot synchronization across all nodes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 14
3.3.2 CSMA/CD: Carrier Sense Multiple Access with Collision Detection
M3.3 CSMA/CD PROTOCOL
• Carrier Sense (Listen Before Talk)
Node listens to channel before transmitting. 1-persistent: transmits immediately when idle; Non-persistent: waits random backoff if busy; p-persistent: transmits with probability $p$ when idle.
• Collision Detection (Listen While Talk)
Node continuously monitors voltage/energy on wire while transmitting. If signal amplitude exceeds collision threshold, collision is detected immediately!
• Jam Signal & Abort
Upon detecting collision, node aborts transmission immediately and broadcasts a 32-48 bit **Jam Signal** to ensure all other nodes detect the collision.
• Minimum Frame Size Constraint ($L_{min}$)
To ensure a sender does not finish transmitting before collision signal propagates back: $T_{frame} \ge 2 \times T_{prop} \implies \frac{L_{min}}{R} \ge 2 \cdot \frac{d}{s} \implies L_{min} = 2 \times T_{prop} \times R$.
• Binary Exponential Backoff (BEB)
After $k$-th collision ($k \le 10$), node picks random wait slot $r \in \{0, 1, 2, \dots, 2^k - 1\}$ and waits $r \times 512$ bit times. Aborts after 16 consecutive collisions.
CSMA/CD Summary
→ 1-persistent sense
→ Jam signal on collision
→ L_min = 2 * t_prop * R
→ Standard Ethernet L_min = 64 Bytes (512 bits)
→ Backoff range: [0, 2^k - 1]
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 15
3.3.3 Worked KTU Numerical: CSMA/CD Minimum Frame Size
M3.3 CSMA/CD NUMERICAL
📌 KTU Numerical Problem Statement
A 1 Gbps Ethernet LAN runs over a 1 km fiber link with propagation speed s = 2 * 10^8 m/s. Calculate the minimum frame size required for proper collision detection. If transmission rate is increased to 10 Gbps over the same link, what must the new minimum frame size be?
📐 Governing Formulas & Principles:
• L_min = 2 * t_prop * R
• t_prop = d / s = 1000 m / (2 * 10^8 m/s) = 5 * 10^-6 s = 5 microseconds.
• Round-trip propagation time 2 * t_prop = 10 microseconds = 10^-5 seconds.
• L_min = 2 * t_prop * R (bits).
📝 Step-by-Step Derivation & Solution
Step 1: For R = 1 Gbps = 10^9 bps:
Step 2: L_min = 10^-5 s * 10^9 bps = 10,000 bits = 10,000 / 8 = 1250 Bytes.
Step 3: For R = 10 Gbps = 10^10 bps:
Step 4: L_min = 10^-5 s * 10^10 bps = 100,000 bits = 12,500 Bytes (12.5 KB).
Step 5: Conclusion: At 10 Gbps, minimum frame size becomes unfeasibly large; hence 10 Gigabit Ethernet mandates full-duplex point-to-point links (disabling CSMA/CD entirely).
✅ FINAL ANSWER: 1 Gbps: L_min = 1250 Bytes | 10 Gbps: L_min = 12,500 Bytes
💡 Exam Tip: CSMA/CD is only applicable on half-duplex shared media; full-duplex switched Ethernet does not require CSMA/CD.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 16
🎯 Exam Booster & Review: Multiple Access Protocols
M3.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Derive the maximum channel throughput for Pure ALOHA ($18.4\%$) and Slotted ALOHA ($36.8\%$) with vulnerable period diagrams. (8 Marks)
Q: Explain the working of CSMA/CD with the Binary Exponential Backoff (BEB) algorithm and minimum frame size derivation. (8 Marks)
Q: Explain Code Division Multiple Access (CDMA) using orthogonal Walsh chip sequences with an encoding and decoding example. (7 Marks)
💡 Critical Conceptual Takeaways
✔ Slotted ALOHA doubles Pure ALOHA efficiency by eliminating partial frame collisions.
✔ Minimum frame size in CSMA/CD guarantees collision detection before transmission ends ($L_{min} = 2 \cdot t_{prop} \cdot R$).
✔ CDMA allows simultaneous transmission over the same frequency band using orthogonal chip codes.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 17
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.4
Link-Layer Addressing & Address Resolution Protocol (ARP)
48-Bit MAC Addresses (EUI-48), ARP Request (Broadcast) & ARP Reply (Unicast), ARP Cache & Timeout, Proxy ARP, Subnet Crossing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 18
3.4.1 MAC Addressing & Address Resolution Protocol (ARP)
M3.4 ARP PROTOCOL
• MAC Hardware Address (48 bits / 6 Bytes)
Burned into NIC ROM (e.g., `1A:2B:3C:4D:5E:6F`). First 24 bits = OUI (Organizationally Unique Identifier assigned by IEEE); Last 24 bits = Vendor NIC serial number.
• ARP Mission (RFC 826)
Dynamically resolves a known 32-bit IP address into its corresponding 48-bit MAC address on the local physical subnet.
• ARP Message Flow
1. **ARP Request**: Host broadcasts frame (`FF:FF:FF:FF:FF:FF`) asking: 'Who owns IP 192.168.1.5? Send your MAC to 192.168.1.2'. \n 2. **ARP Reply**: Target host unicasts reply containing its physical MAC address directly to the sender. \n 3. **ARP Table**: Sender caches the mapping in its local ARP Cache table with a TTL timer (typically 20 minutes).
• Proxy ARP & Gratuitous ARP
**Proxy ARP**: Router responds to ARP request on behalf of a remote node. **Gratuitous ARP**: Host announces its own IP/MAC to detect duplicate IP conflicts and update switch MAC tables.
ARP Key Facts
→ ARP Request: L2 Broadcast (FF:..:FF)
→ ARP Reply: L2 Unicast
→ L2 Frame Type: 0x0806 (ARP)
→ ARP Cache: Dynamic IP->MAC table
→ Gratuitous ARP: IP conflict check
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 19
3.4.2 Packet Forwarding Across Subnets (MAC & IP Rewriting)
M3.4 SUBNET ROUTING
• Scenario: Host A (Subnet 1) sends packet to Host B (Subnet 2) via Router R
Source Host A creates L3 IP packet: `Src IP = IP_A`, `Dst IP = IP_B` (IP addresses remain constant throughout end-to-end path).
• Hop 1 (Host A -> Router R)
Host A inspects routing table; determines destination `IP_B` is outside local subnet. Encapsulates IP packet into L2 frame: `Src MAC = MAC_A`, `Dst MAC = MAC_Router_Interface_1` (uses ARP to find router MAC).
• Router R Processing
Router decapsulates L2 frame, inspects L3 `Dst IP = IP_B`, consults FIB routing table, decrements TTL, recomputes IP checksum, and determines outgoing Interface 2.
• Hop 2 (Router R -> Host B)
Router encapsulates packet into a fresh L2 frame: `Src MAC = MAC_Router_Interface_2`, `Dst MAC = MAC_B` (via ARP on Subnet 2).
• Core Takeaway
**IP addresses remain unchanged end-to-end; MAC addresses change at every single router hop!**
Hop-by-Hop Headers
→ Hop 1: Src MAC_A -> Dst MAC_R1
→ Hop 2: Src MAC_R2 -> Dst MAC_B
→ End-to-End: Src IP_A -> Dst IP_B
→ L2 MAC rewritten per hop
→ L3 IP preserved end-to-end
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 20
🎯 Exam Booster & Review: MAC Addressing & ARP
M3.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the operation of Address Resolution Protocol (ARP) with request and reply frame structures. (7 Marks)
Q: Trace the step-by-step changes in Source/Destination IP and Source/Destination MAC addresses as a packet travels from Host A to Host B across an intermediate router. (8 Marks)
💡 Critical Conceptual Takeaways
✔ ARP bridges Layer 3 IP addresses to Layer 2 physical MAC addresses.
✔ ARP requests are L2 broadcasts (`FF:FF:FF:FF:FF:FF`); ARP replies are L2 unicasts.
✔ L3 IP addresses identify end hosts; L2 MAC addresses identify next-hop network interfaces.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 21
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.5
Ethernet Protocols & IEEE 802.3 Architecture
Standard Ethernet (10M), Fast Ethernet (100M), Gigabit Ethernet (1G), 10GbE, IEEE 802.3 Frame Format (64B to 1518B)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 22
3.5.1 IEEE 802.3 Ethernet Frame Format
M3.5 ETHERNET FRAME
• Preamble (7 Bytes)
7 bytes of alternating `10101010` patterns used to synchronize receiver clock circuitry.
• Start of Frame Delimiter - SFD (1 Byte)
1 byte pattern `10101011` indicating that destination MAC address begins immediately on the next bit.
• Destination MAC Address (6 Bytes)
48-bit hardware address of target NIC (or broadcast `FF:FF:FF:FF:FF:FF`).
• Source MAC Address (6 Bytes)
48-bit hardware address of sending NIC.
• Type / Length Field (2 Bytes)
If $\ge 1536$ (0x0600), specifies upper layer protocol (EtherType: IPv4 `0x0800`, ARP `0x0806`, IPv6 `0x86DD`). If $\le 1500$, specifies frame payload length.
• Payload / Data (46 to 1500 Bytes)
Carries L3 datagram. Minimum payload is 46 bytes (padded with zeros if smaller) to enforce the 64-byte minimum frame size constraint.
• Frame Check Sequence - FCS (4 Bytes)
32-bit Cyclic Redundancy Check (CRC-32) computed over Dst MAC, Src MAC, Type, and Payload.
Frame Sizes
→ Preamble + SFD: 8 Bytes
→ Header + FCS: 18 Bytes
→ Min Payload: 46 Bytes
→ Max Payload (MTU): 1500 Bytes
→ Min Frame Size: 64 Bytes
→ Max Frame Size: 1518 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 23
3.5.2 Ethernet Speed Evolution: Standard to 10GbE
M3.5 ETHERNET EVOLUTION
Standard & Fast Ethernet
• Standard (10 Mbps): 10Base5 (Thicknet coaxial), 10Base2 (Thinnet), 10Base-T (UTP Cat 3/5 with Hub/Switch). Uses Manchester line coding
• Fast Ethernet (100 Mbps): 100Base-TX (Cat 5 UTP using 4B/5B and MLT-3 coding), 100Base-FX (Fiber). Introduces Auto-Negotiation
Gigabit & 10G Ethernet
• Gigabit Ethernet (1 Gbps): 1000Base-T (Cat 5e/6 UTP using 4 pairs full-duplex with 8B/10B coding), 1000Base-SX/LX (Fiber). Introduces Carrier Extension and Packet Bursting for half-duplex
• 10 Gigabit Ethernet (10 Gbps): 10GBase-T (Cat 6a/7) and 10GBase-SR/LR. Exclusively full-duplex switched connections; eliminates CSMA/CD completely
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 24
🎯 Exam Booster & Review: IEEE 802.3 Ethernet
M3.5
📚 KTU High-Yield Questions (K2 Understand)
Q: Draw the IEEE 802.3 Ethernet frame format and explain the function of each field. Why is the minimum frame size 64 bytes and maximum 1518 bytes? (8 Marks)
Q: Compare Standard Ethernet, Fast Ethernet, Gigabit Ethernet, and 10 Gigabit Ethernet with respect to medium, coding, and transmission modes. (7 Marks)
💡 Critical Conceptual Takeaways
✔ Preamble and SFD synchronize bit timing; FCS trailer provides CRC-32 error detection.
✔ 64-byte minimum frame ensures collision detection in 10/100 Mbps CSMA/CD networks.
✔ 10GbE operates strictly in full-duplex mode over switches and fiber links.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 25
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.5V
Virtual Local Area Networks (VLANs - IEEE 802.1Q)
Broadcast Containment, Port-Based vs Tagged VLANs, IEEE 802.1Q 4-Byte Tag (VID 1-4094), Access vs Trunk Ports, Router-on-a-Stick
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 26
3.5V.1 VLAN Motivation & IEEE 802.1Q Tagged Framing
M3.5V VLAN ARCHITECTURE
• VLAN Motivation
Physically co-located hosts can be partitioned into logical broadcast domains regardless of physical switch topology. Prevents broadcast storms, enhances security, and organizes departments logically (e.g., Faculty VLAN, Student VLAN, Lab VLAN).
• Port-Based VLAN (Untagged)
Switch ports assigned static VLAN IDs. Traffic inside switch segregated by port group; frames on access links remain standard untagged Ethernet frames.
• IEEE 802.1Q Tagged Frame (4 Bytes Inserted after Source MAC)
1. **TPID (Tag Protocol Identifier - 16 bits)**: Set to `0x8100` (identifies frame as 802.1Q tagged). \n 2. **PCP (Priority Code Point - 3 bits)**: IEEE 802.1p Quality of Service priority (0 to 7). \n 3. **DEI (Drop Eligible Indicator - 1 bit)**: Set to 1 if frame can be dropped during congestion. \n 4. **VID (VLAN Identifier - 12 bits)**: Uniquely identifies VLAN number (1 to 4094; 0 and 4095 reserved).
• Access Port vs Trunk Port
**Access Port**: Connects end hosts; carries traffic for 1 untagged VLAN only. **Trunk Port**: Interconnects switches/routers; carries multiplexed tagged traffic for multiple VLANs simultaneously.
IEEE 802.1Q Tag
→ TPID: 0x8100 (16 bits)
→ PCP: 3 bits (QoS Priority)
→ DEI: 1 bit (Drop eligibility)
→ VID: 12 bits (4094 VLANs)
→ Trunking: Carries tagged frames
→ Access: Carries untagged frames
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 27
3.5V.2 Inter-VLAN Routing: Router-on-a-Stick vs Layer 3 Switch
M3.5V INTER-VLAN ROUTING
• Why Inter-VLAN Routing?
By design, hosts on different VLANs cannot communicate at Layer 2 even if plugged into the same physical switch. Inter-VLAN routing requires Layer 3 packet forwarding.
• Router-on-a-Stick (Legacy Approach)
A single physical Ethernet interface on an external router is connected to a switch Trunk port. The router interface is divided into logical **Sub-interfaces** (e.g., `eth0.10`, `eth0.20`), each configured with the default gateway IP and 802.1Q encapsulation for its respective VLAN.
• Layer 3 Switch (Modern Core Routing)
Switches with built-in hardware ASIC routing capabilities. Configured with **Switched Virtual Interfaces (SVIs)** (`interface vlan 10`, `interface vlan 20`) providing multi-gigabit wire-speed inter-VLAN routing without external router bottleneck.
Inter-VLAN Methods
→ Router-on-a-Stick: 1 Trunk link
→ Sub-interfaces: eth0.10, eth0.20
→ L3 Switch: Hardware SVI routing
→ Wire-speed routing in L3 switch
→ Isolates broadcast domains
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 28
🎯 Exam Booster & Review: Virtual LANs (VLANs)
M3.5V
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the benefits of VLANs and illustrate the 4-byte IEEE 802.1Q tag header format. (7 Marks)
Q: Differentiate between Access ports and Trunk ports on an Ethernet switch. (5 Marks)
Q: Explain Inter-VLAN routing using the Router-on-a-Stick architecture with a network diagram and configuration concepts. (7 Marks)
💡 Critical Conceptual Takeaways
✔ VLANs partition a single physical switch into multiple isolated broadcast domains.
✔ IEEE 802.1Q tag inserts 4 bytes (TPID 0x8100 + 12-bit VID for 4094 VLANs).
✔ Trunk links carry tagged multiplexed frames between switches and routers.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 29
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.6
Connecting Devices & Spanning Tree Protocol (STP)
Repeaters, Hubs (L1), Bridges & Layer 2 Switches (MAC Learning), Spanning Tree Protocol (IEEE 802.1D STP), Routers & Layer 3 Switches
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 30
3.6.1 Connecting Devices Taxonomy & Collision/Broadcast Domains
M3.6 CONNECTING DEVICES
Layer 1: Repeaters & Hubs
• Operating Layer: Physical Layer (L1)
• Function: Regenerates and amplifies electrical/optical signals; broadcasts incoming bits to all ports
• Collision Domains: Single shared collision domain across all ports
• Broadcast Domains: Single broadcast domain
• Intelligence: Zero intelligence / No buffering
Layer 2: Bridges & Switches
• Operating Layer: Data Link Layer (L2)
• Function: Inspects MAC addresses; filters and forwards frames selectively using hardware MAC Learning table
• Collision Domains: Microsegmentation: **Each individual port is an isolated collision domain**
• Broadcast Domains: Single broadcast domain (unless partitioned via VLANs)
• Buffering: Store-and-forward / Cut-through
Layer 3: Routers & L3 Switches
• Operating Layer: Network Layer (L3)
• Function: Routes packets across heterogeneous networks using IP addresses
• Collision Domains: Separate collision domain per port
• Broadcast Domains: **Separates broadcast domains** (does not forward L2 broadcasts)
• Routing Table: Maintains FIB routing table
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 31
3.6.2 Spanning Tree Protocol (IEEE 802.1D STP)
M3.6 SPANNING TREE PROTOCOL
• The Layer 2 Loop Problem
Redundant links between switches provide fault tolerance, but create disastrous **Broadcast Storms**, multiple frame copies, and MAC table instability.
• STP Goal
Logically disables redundant links by placing them in Blocking state, dynamically constructing a loop-free active tree topology while keeping backup paths on standby.
• BPDU (Bridge Protocol Data Units)
Switches exchange BPDUs containing: `Bridge ID = Priority (2B) + MAC Address (6B)` (Default priority = 32768).
• 4-Step STP Algorithm
1. **Root Bridge Election**: Switch with the lowest Bridge ID becomes the Root Bridge. \n 2. **Root Port (RP) Selection**: On each non-root switch, the port with the lowest path cost to the Root Bridge is selected as RP. \n 3. **Designated Port (DP) Selection**: On each LAN segment, the port with the lowest path cost to Root becomes DP. \n 4. **Blocking State**: All remaining ports are placed in Blocking/Discarding state to break loops.
STP Algorithm Steps
→ 1. Lowest Bridge ID -> Root Bridge
→ 2. Lowest Cost to Root -> Root Port (RP)
→ 3. Lowest Cost per Link -> Designated Port (DP)
→ 4. Remaining Ports -> Blocked / Alternate
→ Convergence time: ~30-50 seconds (RSTP: < 1s)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 32
🎯 Exam Booster & Review: Connecting Devices & STP
M3.6
📚 KTU High-Yield Questions (K3 Apply)
Q: Compare Repeaters, Hubs, Switches, and Routers with respect to operating layer, collision domains, and broadcast domains. (8 Marks)
Q: Explain the working of the Spanning Tree Protocol (IEEE 802.1D) with Bridge ID, Root Bridge election, Root Ports, and Blocking ports. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Hubs extend collision domains; Switches isolate collision domains; Routers isolate broadcast domains.
✔ Transparent switches dynamically populate MAC tables by inspecting source MACs of arriving frames.
✔ STP prevents broadcast storms by breaking physical switching loops into a single logical tree.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 33
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.7
Wireless LANs: IEEE 802.11 (Wi-Fi) Architecture
BSS, AP, ESS, Distribution System, Hidden/Exposed Terminal Problems, CSMA/CA with RTS/CTS, SIFS/PIFS/DIFS, 802.11 Frame (4 Addresses)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 34
3.7.1 IEEE 802.11 Architecture & Terminal Problems
M3.7 WIRELESS ARCHITECTURE
• Basic Service Set (BSS)
The fundamental building block consisting of wireless stations and a central Access Point (AP) in Infrastructure mode (or peer-to-peer in Ad-hoc / IBSS mode).
• Extended Service Set (ESS)
Multiple BSSs interconnected via a wired Distribution System (DS) sharing a common SSID, enabling seamless roaming across campus.
• Hidden Terminal Problem
Nodes A and C cannot hear each other due to distance or physical obstacles, but both are in range of AP B. If A and C transmit simultaneously, their frames collide at B!
• Exposed Terminal Problem
Node B is transmitting to A. Node C wants to transmit to D (away from A). C senses B transmitting and unnecessarily defers, wasting channel capacity.
• Solution: CSMA/CA with RTS/CTS Handshake
Sender transmits short **RTS (Request to Send)** frame (20B). AP replies with **CTS (Clear to Send)** broadcast (14B) containing Network Allocation Vector (NAV) reservation time, silencing hidden terminals.
802.11 Topology
→ BSS: AP + Associated Stations
→ ESS: Multiple BSSs + Wired DS
→ Hidden Terminal: Collisions at AP
→ RTS/CTS: Virtual carrier sensing
→ NAV: Channel reservation timer
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 35
3.7.2 CSMA/CA Protocol Timing Intervals & 4-Address Frame
M3.7 CSMA/CA TIMING
• Inter-Frame Space (IFS) Hierarchy
1. **SIFS (Short IFS)**: Highest priority; used for immediate ACKs, CTS, and fragmented frames. \n 2. **PIFS (PCF IFS)**: Medium priority; used in polling mode. \n 3. **DIFS (DCF IFS)**: Standard priority; minimum wait time before station can contend for channel.
• Contention Window (CW) & Backoff
Station waits DIFS; if idle, selects random backoff slot in $[0, CW]$. Counts down while channel is idle; freezes counter during busy periods.
• IEEE 802.11 4-Address Frame Format
Frame Control (2B) | Duration/ID (2B) | Address 1 (6B: Receiver MAC) | Address 2 (6B: Transmitter MAC) | Address 3 (6B: Original Source or Final Dest MAC) | Sequence Control (2B) | Address 4 (6B: Used strictly when bridging across WDS wireless distribution links) | Payload (0-2312B) | FCS (4B).
Timing Hierarchy
→ SIFS < PIFS < DIFS < EIFS
→ SIFS: ACKs & CTS (Highest priority)
→ DIFS: Standard data contention
→ Addr 1: Immediate Receiver
→ Addr 2: Immediate Transmitter
→ Addr 3: Original Source / Dest
→ Addr 4: WDS Wireless Bridge
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 36
🎯 Exam Booster & Review: IEEE 802.11 Wireless LANs
M3.7
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the Hidden Terminal and Exposed Terminal problems in Wireless LANs. How does CSMA/CA with RTS/CTS resolve them? (8 Marks)
Q: Explain the timing relationships between SIFS, PIFS, and DIFS in IEEE 802.11 CSMA/CA with a neat timing diagram. (7 Marks)
Q: Explain the four MAC address fields in the IEEE 802.11 frame format. When is Address 4 used? (6 Marks)
💡 Critical Conceptual Takeaways
✔ Wireless radios cannot detect collisions while transmitting; hence Wi-Fi uses collision avoidance (CSMA/CA).
✔ RTS and CTS frames carry NAV reservation timers to silence hidden nodes.
✔ Address 4 is populated only when frames are bridged between two wireless APs in WDS mode.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 37
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.8
Mobile IP Architecture & Protocols
Mobile Node (MN), Home Agent (HA), Foreign Agent (FA), Home Address (HoA), Care-of Address (CoA), Tunneling & Triangle Routing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 38
3.8.1 Mobile IP Architecture & Entities (RFC 5944)
M3.8 MOBILE IP BASICS
• The Mobility Challenge
Standard IP routing uses destination IP prefixes. If a mobile laptop moves to a new subnet, changing its IP address terminates all active TCP connections! Mobile IP allows a host to retain its permanent IP transparently.
• Mobile IP Entities
1. **Mobile Node (MN)**: The roaming host. \n 2. **Home Network & Home Agent (HA)**: The home subnet and the router acting on behalf of MN when away. \n 3. **Foreign Network & Foreign Agent (FA)**: The visited subnet router assisting MN. \n 4. **Correspondent Node (CN)**: The peer host communicating with MN.
• Dual-Address Mechanism
1. **Home Address (HoA)**: Permanent IP address assigned in home subnet (used for active TCP sessions). \n 2. **Care-of Address (CoA)**: Temporary IP address associated with visited foreign network.
Core Entities
→ MN: Mobile Node
→ HA: Home Agent router
→ FA: Foreign Agent router
→ HoA: Permanent IP address
→ CoA: Temporary visited IP
→ CN: Correspondent Node
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 39
3.8.2 Operational Phases: Registration, Tunneling & Triangle Routing
M3.8 MOBILE IP PHASES
• Phase 1: Agent Discovery
Foreign Agents broadcast periodic Agent Advertisements (ICMP extension); MN detects it has moved and obtains a CoA.
• Phase 2: Registration
MN sends Registration Request to FA -> FA forwards to Home Agent (HA) -> HA updates binding table (`HoA -> CoA`) and sends Registration Reply.
• Phase 3: Data Transfer (IP-in-IP Encapsulation Tunneling)
CN sends packet to `HoA` -> Routed to Home Network -> Home Agent intercepts packet via Proxy ARP -> HA encapsulates packet inside a new IP header (`Src IP = HA`, `Dst IP = CoA`) -> Transmits through IP tunnel to FA -> FA decapsulates and delivers to MN.
• Reverse Path & Triangle Routing Problem
MN sends directly to CN via standard IP routing. However, traffic from CN travels through HA -> FA -> MN (inefficient Triangle Routing). Solution: Route Optimization allows CN to cache MN's CoA and tunnel directly.
Tunneling Flow
→ CN -> Home Agent (HoA)
→ HA intercepts (Proxy ARP)
→ HA tunnels to FA (IP-in-IP)
→ FA decapsulates -> MN
→ MN replies directly to CN
→ Triangle Routing fixed via CoA cache
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 40
🎯 Exam Booster & Review: Mobile IP Architecture
M3.8
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the architecture and entities of Mobile IP (MN, HA, FA, HoA, CoA) with a neat diagram. (8 Marks)
Q: Explain the three operational phases of Mobile IP: Agent Discovery, Registration, and Encapsulation Tunneling. (8 Marks)
Q: What is the Triangle Routing problem in Mobile IP, and how does Route Optimization solve it? (6 Marks)
💡 Critical Conceptual Takeaways
✔ Mobile IP preserves TCP connection survivability during subnet roaming.
✔ Home Agent intercepts packets using Proxy ARP and encapsulates them via IP-in-IP tunneling to the Care-of Address.
✔ Triangle routing introduces latency by routing all forward traffic through the Home Agent.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 41
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.9
Linux Network Programming: Raw Sockets & PF_PACKET
Data Link Provider Interface (DLPI), BSD Packet Filter (BPF), Linux PF_PACKET / AF_PACKET (SOCK_RAW, ETH_P_ALL), Promiscuous Sniffer
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 42
3.9.1 Hands-On: Packet Sniffing with Linux `PF_PACKET`
M3.9 LINUX RAW SOCKETS
// Linux Socket & Protocol Implementation
#include <sys/socket.h> #include <netinet/ether.h> #include <net/if.h> #include <sys/ioctl.h> int main() { // 1. Create Raw Packet Socket to capture all Ethernet frames int raw_sock = socket(AF_PACKET, SOCK_RAW, htons(ETH_P_ALL)); // 2. Enable Promiscuous Mode on network interface eth0 struct ifreq ifr; strcpy(ifr.ifr_name, "eth0"); ioctl(raw_sock, SIOCGIFFLAGS, &ifr); ifr.ifr_flags |= IFF_PROMISC; ioctl(raw_sock, SIOCSIFFLAGS, &ifr); // 3. Capture and Dissect Raw Ethernet Frame unsigned char buffer[2048]; while (1) { int len = recvfrom(raw_sock, buffer, sizeof(buffer), 0, NULL, NULL); struct ether_header *eth = (struct ether_header *)buffer; printf("Src MAC: %s -> Dst MAC: %s | Protocol: 0x%04X\n", ether_ntoa((struct ether_addr *)eth->ether_shost), ether_ntoa((struct ether_addr *)eth->ether_dhost), ntohs(eth->ether_type)); } }
⚙️ System Call & Execution Workflow
• `AF_PACKET` / `PF_PACKET`: Linux-specific socket domain allowing direct interaction with Layer 2 device drivers, bypassing the standard kernel TCP/IP protocol stack entirely.
• `SOCK_RAW` vs `SOCK_DGRAM`: `SOCK_RAW` provides raw Ethernet frames including L2 header and trailer; `SOCK_DGRAM` provides frames with L2 header stripped.
• Protocol Filter `ETH_P_ALL`: Captures all incoming and outgoing frames (IPv4, ARP, IPv6, STP, VLAN).
• Promiscuous Mode (`IFF_PROMISC`): Instructs the NIC hardware to disable MAC address filtering and deliver all overheard frames on the physical wire to the OS.
💡 Hands-on Insight: Used by network diagnostic tools like Wireshark, tcpdump, and custom IDS packet analysis engines.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 43
🎯 Exam Booster & Review: Linux Raw Sockets
M3.9
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the difference between standard Berkeley sockets (`AF_INET`) and Linux packet sockets (`AF_PACKET`). (6 Marks)
Q: Write a C program using `PF_PACKET` and `SOCK_RAW` to capture Ethernet frames and extract Source and Destination MAC addresses. (8 Marks)
💡 Critical Conceptual Takeaways
✔ `AF_PACKET` gives direct access to Layer 2 raw Ethernet frames.
✔ Promiscuous mode captures all frames on the shared link regardless of destination MAC.
✔ `ETH_P_ALL` captures all Layer 3 protocol payloads.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET