## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 MASTER • MODULE 4 MASTER DECK
Network Management & Physical Layer Fundamentals
Complete Lecture Slides for KTU PCCST501 Computer Networks | Topics M4.1 through M4.6
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.1
Network Management Architecture & SNMP Protocol
Managing Entities (Managers), Managed Devices (Agents), MIB, SNMP Protocol Operations, SNMPv1 vs SNMPv2c vs SNMPv3 (USM & VACM)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 3
4.1.1 Network Management Framework & SNMP Operations
M4.1 SNMP FRAMEWORK
• Network Management Architecture
Consists of 4 pillars: 1. **Managing Entity (Manager / NMS)**: Centralized workstation running management software. 2. **Managed Devices**: Routers, switches, servers, hosts containing management data. 3. **Management Agent**: Software daemon running inside managed device. 4. **Management Information Base (MIB)**: Virtual database of manageable object variables.
• SNMP Protocol (Simple Network Management Protocol - RFC 3411)
Operates over UDP port 161 (Manager to Agent queries) and UDP port 162 (Agent to Manager asynchronous Traps).
• Core SNMP Protocol Operations
1. **GetRequest**: Manager fetches value of 1 or more MIB variables from Agent. \n 2. **GetNextRequest**: Manager fetches the lexicographically next MIB variable (used for MIB tree walking and table traversal). \n 3. **GetBulkRequest (v2c/v3)**: Fetches large blocks of table rows in a single packet. \n 4. **SetRequest**: Manager sets/modifies configuration value on Agent device. \n 5. **Response**: Agent returns requested data values or error status. \n 6. **Trap / InformRequest**: Unsolicited alert sent by Agent to Manager upon an event (e.g., link failure, reboot). `InformRequest` requires Manager ACK.
SNMP Ports & PDUs
→ UDP Port 161: Agent listener
→ UDP Port 162: Manager Trap listener
→ GetRequest: Read variable
→ SetRequest: Write configuration
→ GetNext: Sequential MIB walk
→ GetBulk: Fast table download
→ Trap: Asynchronous alert
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 4
4.1.2 SNMP Version Evolution: SNMPv1 vs SNMPv2c vs SNMPv3
M4.1 SNMP EVOLUTION
SNMPv1 & SNMPv2c
• Security Model: Plaintext Community Strings (`public` for read-only, `private` for read-write). Vulnerable to packet sniffing
• Operations (v1): Get, GetNext, Set, Response, Trap
• Enhancements (v2c): Adds `GetBulkRequest` for fast table fetching and 64-bit high-capacity counters (`Counter64`), but retains plaintext community security
• Suitability: Isolated, trusted internal LANs only
SNMPv3 (Cryptographically Secure)
• Security Model: User-Based Security Model (USM) + View-Based Access Control Model (VACM)
• Authentication: Message digest authentication via HMAC-MD5 or HMAC-SHA (verifies origin and prevents tampering)
• Confidentiality: Payload encryption via DES or AES-128 / AES-256 (prevents eavesdropping)
• Message Freshness: Timestamps and boot counters prevent Replay attacks
• Enterprise Standard: Mandatory standard for secure network management
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
🎯 Exam Booster & Review: Network Management & SNMP
M4.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the four components of the Network Management architecture (Manager, Agent, MIB, SNMP) with a neat diagram. (7 Marks)
Q: Describe the various SNMP protocol operations (GetRequest, GetNextRequest, GetBulkRequest, SetRequest, Trap, InformRequest). (8 Marks)
Q: Compare SNMPv1, SNMPv2c, and SNMPv3 with focus on the User-Based Security Model (USM) in SNMPv3. (7 Marks)
💡 Critical Conceptual Takeaways
✔ SNMP uses UDP port 161 for synchronous polling and port 162 for asynchronous event Traps.
✔ SNMPv2c introduced `GetBulk` and 64-bit counters; SNMPv3 added cryptographic authentication and AES encryption.
✔ `InformRequest` provides reliable delivery of trap notifications with manager acknowledgments.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 6
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.2
Structure of Management Information (SMI) & ASN.1
Abstract Syntax Notation One (ASN.1), SMIv2 Macro Definitions, MIB OID Tree Hierarchy (1.3.6.1.2.1), Standard MIB-II Groups, BER Encoding
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 7
4.2.1 SMIv2 & MIB Object Identifier (OID) Tree Hierarchy
M4.2 SMI & MIB HIERARCHY
• SMI (Structure of Management Information - RFC 2578)
The formal language defining the rules for naming, specifying data types, and structuring management objects in the MIB.
• ASN.1 (Abstract Syntax Notation One)
A formal notation for describing data structures independently of machine hardware architectures. Defines primitives (INTEGER, OCTET STRING, OBJECT IDENTIFIER, SEQUENCE).
• Globally Unique OID Tree Hierarchy
Every manageable variable is assigned a globally unique dot-delimited Object Identifier (OID) arranged in an inverted tree:
• Standard Internet MIB-2 Path
`iso(1)` -> `org(3)` -> `dod(6)` -> `internet(1)` -> `mgmt(2)` -> `mib-2(1)` = **`1.3.6.1.2.1`**.
• Standard MIB-II Functional Groups
1. `system (1.3.6.1.2.1.1)`: Device name, description, uptime, contact. \n 2. `interfaces (1.3.6.1.2.1.2)`: Subnet interfaces, MTU, speed, packet counters. \n 3. `ip (1.3.6.1.2.1.4)`: IP routing tables, forward state, TTL, packet discards. \n 4. `tcp (1.3.6.1.2.1.6)`: Active TCP connection table, current connections, timeouts. \n 5. `udp (1.3.6.1.2.1.7)`: UDP listener table and datagram counters.
• Basic Encoding Rules (BER)
Transfers data over wire using **TLV format**: `Tag (Type)` | `Length` | `Value`.
Standard MIB-2 Groups
→ 1.3.6.1.2.1.1: system
→ 1.3.6.1.2.1.2: interfaces
→ 1.3.6.1.2.1.4: ip
→ 1.3.6.1.2.1.6: tcp
→ 1.3.6.1.2.1.7: udp
→ 1.3.6.1.2.1.11: snmp
→ Encoding: BER TLV format
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 8
🎯 Exam Booster & Review: SMI & ASN.1
M4.2
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the role of SMI and ASN.1 in SNMP network management. (6 Marks)
Q: Illustrate the MIB Object Identifier (OID) tree hierarchy from Root to MIB-II (`1.3.6.1.2.1`) and describe the primary MIB-II groups (`system`, `interfaces`, `ip`, `tcp`). (8 Marks)
Q: Explain Basic Encoding Rules (BER) and the Tag-Length-Value (TLV) encoding format with an example. (6 Marks)
💡 Critical Conceptual Takeaways
✔ SMI defines how MIB data objects are formally defined using ASN.1 syntax.
✔ OID `1.3.6.1.2.1` is the root prefix for all standard Internet MIB-II management objects.
✔ BER encodes variables into machine-independent Tag-Length-Value (TLV) binary streams.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 9
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.3
Data and Signals: Theoretical Channel Capacity
Analog vs Digital Signals, Bandwidth, Transmission Impairments (Attenuation, Noise), Signal-to-Noise Ratio (SNR), Nyquist Rate vs Shannon Capacity
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 10
4.3.1 Signals, Bandwidth & Transmission Impairments
M4.3 DATA & SIGNALS
• Analog vs Digital Signals
Analog signals have infinitely many continuous values over time (e.g., sine wave $s(t) = A \sin(2\pi f t + \phi)$). Digital signals have discrete discrete levels (e.g., 0V and 5V pulses representing bits 0 and 1).
• Bandwidth ($B$)
The range of frequencies contained in a composite signal: $B = f_{max} - f_{min}$ Hertz (Hz).
• Transmission Impairments
1. **Attenuation**: Loss of signal energy over distance (measured in decibels $dB = 10 \log_{10} (P_2 / P_1)$). Corrected via amplifiers/repeaters. \n 2. **Distortion**: Different frequency components travel at different speeds, altering composite waveform shape. \n 3. **Noise**: Unwanted external energy added to signal (Thermal noise $N_0 = kTB$, Induced noise, Crosstalk, Impulse noise).
• Signal-to-Noise Ratio (SNR)
Ratio of signal power to noise power: $SNR = \frac{P_{signal}}{P_{noise}}$. In decibels: $SNR_{dB} = 10 \log_{10} (SNR)$ (e.g., $SNR = 1000 \implies SNR_{dB} = 30$ dB).
Key Formulas
→ Bandwidth: B = f_max - f_min (Hz)
→ Decibels: dB = 10 * log10(P2 / P1)
→ SNR = P_signal / P_noise
→ SNR_dB = 10 * log10(SNR)
→ SNR = 10^(SNR_dB / 10)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 11
4.3.2 Channel Capacity Limits: Nyquist vs Shannon
M4.3 NYQUIST VS SHANNON
Nyquist Bit Rate (Noiseless Channel)
• Formulated By: Harry Nyquist (1928)
• Channel Condition: Assumes theoretical **noiseless** channel with bandwidth $B$ Hz and $L$ discrete signaling levels
• Formula: $C = 2 \times B \times \log_2 (L)$ bps
• Implication: Data rate can be increased indefinitely by increasing the number of signal levels $L$, but is constrained by noise in practice
Shannon Capacity (Noisy Channel)
• Formulated By: Claude Shannon (1948)
• Channel Condition: Assumes real-world channel contaminated with Thermal White Noise (Gaussian Noise)
• Formula: $C = B \times \log_2 (1 + SNR)$ bps
• Implication: Defines the absolute physical upper bound on error-free channel capacity regardless of how many signal levels $L$ are used
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 12
4.3.3 Worked KTU Numerical: Nyquist & Shannon Capacity
M4.3 CAPACITY NUMERICAL
📌 KTU Numerical Problem Statement
A telephone line has bandwidth B = 3000 Hz and Signal-to-Noise ratio SNR_dB = 31.62 dB (SNR approx 1452). (a) Calculate the theoretical maximum Shannon channel capacity. (b) To achieve this capacity on a noiseless line with B = 3000 Hz, how many signal levels L are required by Nyquist formula?
📐 Governing Formulas & Principles:
• Shannon Capacity: C = B * log2(1 + SNR) bps
• Given SNR_dB = 31.62 dB -> SNR = 10^(31.62 / 10) = 10^3.162 = 1452.1
• Nyquist Bit Rate: C = 2 * B * log2(L) bps -> log2(L) = C / (2 * B) -> L = 2^(C / 2B).
📝 Step-by-Step Derivation & Solution
Step 1: 1 + SNR = 1 + 1452.1 = 1453.1
Step 2: log2(1453.1) = log10(1453.1) / log10(2) = 3.1623 / 0.30103 = 10.505 bits
Step 3: Shannon Capacity C = 3000 Hz * 10.505 = 31,515 bps (approx 31.5 kbps).
Step 4: Equating to Nyquist: 31,515 = 2 * 3000 * log2(L) = 6000 * log2(L)
Step 5: log2(L) = 31,515 / 6000 = 5.2525 -> L = 2^5.2525 = 38.12 -> L = 38 signal levels.
✅ FINAL ANSWER: Shannon Capacity C = 31.5 kbps | Required Nyquist signal levels L = 38
💡 Exam Tip: Shannon determines the upper capacity limit; Nyquist tells us how many signal levels L are required to realize it.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 13
🎯 Exam Booster & Review: Channel Capacity & Signals
M4.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the three transmission impairments: Attenuation, Distortion, and Noise with diagrams and formulas. (7 Marks)
Q: State and derive the Nyquist Bit Rate formula for noiseless channels and Shannon Capacity theorem for noisy channels. (8 Marks)
Q: A channel has bandwidth B = 4 kHz. Calculate Shannon capacity if SNR_dB = 20 dB. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Nyquist bit rate ($2B \log_2 L$) applies to ideal noiseless channels.
✔ Shannon capacity ($B \log_2(1+SNR)$) establishes the fundamental thermodynamic limit of noisy channels.
✔ Decibels convert logarithmic power ratios into simple additive terms.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 14
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.4
Digital Transmission & Line Coding Schemes
Line Coding Criteria (DC, Sync, Baseline Wander), Unipolar, Polar (NRZ, RZ, Manchester, Diff Manchester), Bipolar (AMI), Block Coding (4B/5B), PCM & DM
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 15
4.4.1 Line Coding Design Criteria & Characteristics
M4.4 LINE CODING CRITERIA
• Line Coding Definition
The process of converting a sequence of digital bits (1s and 0s) into a discrete electrical/optical signal waveform for baseband transmission.
• Key Line Coding Design Criteria
1. **Signal Level vs Data Level**: Number of voltage states ($L$) vs bit values. \n 2. **DC Component**: Frequencies around 0 Hz create heat, cannot pass through transformers/capacitors, and waste transmitter power. Desirable = Zero DC. \n 3. **Self-Synchronization**: Signal transitions (edges) must allow receiver clock to synchronize timing, especially during long strings of consecutive 0s or 1s. \n 4. **Baseline Wander**: Running average of signal voltage must remain constant to maintain accurate decision slicing threshold. \n 5. **Error Detection**: Built-in coding violations indicate physical link errors.
• Pulse Code Modulation (PCM)
Digitizes analog signals in 3 steps: 1. **Sampling** (Nyquist Rate $f_s \ge 2 f_{max}$), 2. **Quantization** (approximates sample amplitudes to discrete levels; introduces Quantization Error), 3. **Encoding** (maps quantized levels into $n$-bit binary codewords: Bit Rate $= n \times f_s$).
Line Coding Goals
→ Eliminate DC components
→ Provide self-synchronization
→ Prevent baseline wander
→ Minimize bandwidth needs
→ PCM: Sample -> Quantize -> Encode
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 16
4.4.2 Major Line Coding Schemes Comparison
M4.4 SCHEMES COMPARISON
Unipolar & Polar NRZ
• Unipolar NRZ: Bit 1 = Positive voltage $+V$, Bit 0 = Zero 0V. Severe DC component; no synchronization on long 0s/1s
• Polar NRZ-L (Level): Bit 1 = Negative $-V$, Bit 0 = Positive $+V$. Sensitive to polarity inversion
• Polar NRZ-I (Invert): Bit 1 = Transition at start of bit interval; Bit 0 = No transition. Immune to polarity inversion, but fails on consecutive 0s
Biphase: Manchester & Differential Manchester
• Manchester (IEEE 802.3): Mid-bit transition: Bit 1 = High-to-Low transition; Bit 0 = Low-to-High transition. Perfect clock synchronization and Zero DC component, but doubles bandwidth requirement ($2 \times$ baud rate)
• Differential Manchester (Token Ring): Always transitions in the middle for clocking. Bit 0 = Transition at start of bit interval; Bit 1 = No transition at start. Highly robust against wire twists
Bipolar AMI & Multilevel
• Bipolar AMI: Bit 0 = Zero 0V; Bit 1 = Alternating positive $+V$ and negative $-V$. Zero DC component, low bandwidth, but loses sync on long 0s (solved via B8ZS/HDB3 scrambling)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 17
🎯 Exam Booster & Review: Digital Transmission & Line Coding
M4.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the line coding waveforms for the bit stream `10110001` using: (a) Unipolar NRZ, (b) NRZ-L, (c) NRZ-I, (d) Manchester, (e) Differential Manchester, (f) Bipolar AMI. (9 Marks)
Q: Explain the working of Pulse Code Modulation (PCM) with Sampling Theorem ($f_s \ge 2f_{max}$), Quantization, and Encoding. (8 Marks)
Q: What is the DC component problem and baseline wander in digital transmission? (5 Marks)
💡 Critical Conceptual Takeaways
✔ Manchester coding guarantees a transition in every single bit cell for foolproof clock synchronization.
✔ Differential Manchester transitions at the start for bit 0, and has no start transition for bit 1.
✔ PCM digitizes voice signals at 8000 samples/sec $\times$ 8 bits/sample = 64 kbps (standard DS0 channel).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 18
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.5
Analog Transmission & Bandwidth Utilization (Multiplexing)
Digital-to-Analog Modulation (ASK, FSK, PSK, QAM), Multiplexing Techniques (FDM, WDM, Synchronous vs Statistical TDM), Spread Spectrum (FHSS, DSSS)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 19
4.5.1 Digital Modulation Schemes: ASK vs FSK vs PSK vs QAM
M4.5 MODULATION SCHEMES
ASK, FSK & PSK
• ASK (Amplitude Shift Keying / BASK): Bit 1 = High amplitude carrier $A_1 \cos(2\pi f_c t)$; Bit 0 = Low amplitude $A_2$ (or 0 in OOK). Susceptible to noise
• FSK (Frequency Shift Keying / BFSK): Bit 1 = Frequency $f_1$; Bit 0 = Frequency $f_2$. Robust against amplitude noise; requires higher bandwidth
• PSK (Phase Shift Keying / BPSK & QPSK): BPSK: Bit 1 = $0^\circ$ phase, Bit 0 = $180^\circ$ phase. QPSK: 2 bits per baud ($00, 01, 10, 11$) using 4 orthogonal phases ($45^\circ, 135^\circ, 225^\circ, 315^\circ$)
QAM (Quadrature Amplitude Modulation)
• Concept: Combines Amplitude Modulation (ASK) and Phase Modulation (PSK) simultaneously to maximize spectral efficiency
• 16-QAM & 64-QAM: 16-QAM encodes 4 bits/symbol ($2^4 = 16$ constellation points); 64-QAM encodes 6 bits/symbol; 256-QAM encodes 8 bits/symbol
• Constellation Diagrams: Visualizes constellation constellation points in In-Phase ($I$) and Quadrature ($Q$) 2D plane
• Applications: Wi-Fi (802.11ac/ax), 4G/5G LTE, Cable modems (DOCSIS)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 20
4.5.2 Multiplexing: FDM vs WDM vs Synchronous TDM vs Statistical TDM
M4.5 MULTIPLEXING TAXONOMY
Frequency & Optical Multiplexing
• FDM (Frequency-Division Multiplexing): Divides total analog bandwidth into distinct frequency channels separated by **Guard Bands** (e.g., FM radio, cable TV)
• WDM (Wavelength-Division Multiplexing): Optical analog of FDM. Combines multiple laser light beams of different wavelengths (e.g., 1550 nm, 1310 nm) onto a single optical fiber using diffraction prisms. DWDM handles 80+ channels
Time-Division Multiplexing (TDM)
• Synchronous TDM: Time divided into fixed recurring frames containing dedicated slots allocated round-robin to each input line. Slot wasted if an input line is idle
• Statistical TDM (Asynchronous): Dynamically allocates time slots **on demand** only to active lines transmitting data. Eliminates idle slot waste by adding channel address headers to each slot
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 21
🎯 Exam Booster & Review: Analog Transmission & Multiplexing
M4.5
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain Quadrature Amplitude Modulation (QAM) and draw the constellation diagrams for 4-QAM and 16-QAM. (8 Marks)
Q: Compare Synchronous TDM and Statistical TDM with framing and slot allocation diagrams. (7 Marks)
Q: Explain Spread Spectrum techniques: Frequency Hopping Spread Spectrum (FHSS) vs Direct Sequence Spread Spectrum (DSSS). (7 Marks)
💡 Critical Conceptual Takeaways
✔ QAM modulates both amplitude and phase to pack multiple bits into a single baud symbol.
✔ FDM shares bandwidth in frequency; TDM shares bandwidth in time slots.
✔ Statistical TDM dynamically allocates slots on demand, achieving much higher link utilization than Synchronous TDM.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 22
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.6
Physical Transmission Media
Guided Media (Twisted Pair UTP/STP, Coaxial Cable, Fiber Optics SMF/MMF), Unguided Wireless (Radio Waves, Microwaves, Infrared)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 23
4.6.1 Guided Media: Twisted Pair vs Coaxial vs Optical Fiber
M4.6 GUIDED MEDIA
Twisted-Pair & Coaxial Cable
• Twisted-Pair (UTP / STP): Two insulated copper wires twisted together to cancel electromagnetic interference (crosstalk). Cat 5e (100 MHz, 1 Gbps), Cat 6 (250 MHz, 10 Gbps up to 55m), Cat 6a (500 MHz, 10 Gbps 100m). Terminated with RJ-45 connectors
• Coaxial Cable: Central copper core surrounded by dielectric insulator, metallic braided shield, and outer jacket. 10Base5 (Thicknet, 500m), 10Base2 (Thinnet, 185m), RG-59 (Cable TV). Terminated with BNC connectors
Optical Fiber (Total Internal Reflection)
• Physics Principle: Light pulses propagate via Total Internal Reflection inside glass core (refractive index $n_1$) surrounded by cladding ($n_2 < n_1$) when incident angle exceeds critical angle
• Multimode Step-Index: Multiple light rays reflect abruptly at core-cladding boundary; causes modal dispersion (short distances)
• Multimode Graded-Index: Core refractive index decreases gradually outward; light rays curve smoothly, reducing modal dispersion
• Single-Mode Fiber (SMF): Ultra-narrow core (8-10 $\mu$m); single light ray propagates straight; zero modal dispersion; enables 100+ km long-haul backbone links
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 24
4.6.2 Unguided Media: Wireless Electromagnetic Spectrum
M4.6 UNGUIDED WIRELESS
• Radio Waves (3 kHz to 1 GHz)
Omnidirectional radiation pattern (transmitting antenna broadcasts signals in all directions). Penetrates physical walls effortlessly. Subject to multi-path interference. Used in AM/FM radio and cordless phones.
• Microwaves (1 GHz to 300 GHz)
Unidirectional, Line-of-Sight propagation. Focused beam using parabolic dish or horn antennas. Cannot penetrate solid obstacles (walls, hills). Used in cellular networks, satellite communications, and GPS.
• Infrared Waves (300 GHz to 400 THz)
High-frequency, short-range line-of-sight communication. Completely blocked by walls and solid obstacles (ensures indoor security without room-to-room interference). Used in TV remote controls and IrDA devices.
Wireless Spectrum
→ Radio: Omnidirectional (Wall penetration)
→ Microwaves: Line-of-sight (Dish antenna)
→ Infrared: Short range (Blocked by walls)
→ Satellite: Geosynchronous (36,000 km)
→ Fiber: Total Internal Reflection
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 25
🎯 Exam Booster & Review: Transmission Media
M4.6
📚 KTU High-Yield Questions (K2 Understand)
Q: Compare Step-Index Multimode, Graded-Index Multimode, and Single-Mode optical fibers with refractive index profiles and light propagation paths. (8 Marks)
Q: Compare Twisted-Pair Cable, Coaxial Cable, and Optical Fiber across bandwidth, attenuation, EMI immunity, and cost. (7 Marks)
Q: Differentiate between Radio waves, Microwaves, and Infrared wireless media. (6 Marks)
💡 Critical Conceptual Takeaways
✔ Optical fibers provide immense bandwidth, zero EMI susceptibility, and ultra-low attenuation.
✔ Single-mode fiber eliminates modal dispersion for high-speed long-distance backbones.
✔ Microwaves require line-of-sight parabolic antennas; Infrared is safely contained by room walls.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET