## Slide 1
PCCST501 Computer Networks | KTU 2024 Scheme • PCCST501 MASTER • COMPLETE COURSE DECK
PCCST501 Computer Networks
KTU 2024 Scheme Curriculum • Modules 1 to 4 Complete Comprehensive Lecture Deck
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 2
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 MASTER • MODULE 1 MASTER DECK
Application Layer & Internet Fundamentals
Complete Lecture Slides for KTU PCCST501 Computer Networks | Topics M1.1 through M1.9
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 3
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.1
Overview of the Internet Architecture & Performance Metrics
Network Edge, Network Core, Packet vs Circuit Switching, Delay Models, Queuing Loss & Throughput Bottlenecks
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 4
1.1.1 The Internet: Structural Hierarchy
M1.1 INTERNET OVERVIEW
• The Internet: Network of Networks
A vast, distributed interconnection of billions of heterogeneous computing devices (end systems / hosts) running networked software.
• Network Edge
End systems (clients, servers, mobile, IoT devices) that generate and consume application data. Connected via Access Networks (DSL, FTTH, 4G/5G, Wi-Fi 6).
• Network Core
The mesh of interconnected packet switches (routers and link-layer switches) responsible for routing and forwarding data across global ISP tiers.
• ISP Tier Hierarchy
Tier-1 ISPs (global transit providers like Lumen, AT&T), connected via IXPs (Internet Exchange Points), supplying regional and local access ISPs.
• Protocols & Standards
Network protocols define message format, ordering, transmission rules, and error handling. Governed by IETF RFCs and IEEE standards.
Key Structural Layers
→ Tier-1 ISPs: Global backbone
→ IXPs: Free/peered routing exchange
→ Regional ISPs: Connect local access
→ Access Nets: DSL, PON/Fiber, Wireless
→ End Systems: Run user applications
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 5
1.1.2 Switching Paradigms: Packet vs Circuit Switching
M1.1 SWITCHING COMPARISON
Packet Switching (Internet)
• Data Unit: Discrete chunks called packets (Header + Payload)
• Multiplexing: Statistical Multiplexing — resources allocated on demand
• Link Utilization: High efficiency; handles bursty internet traffic seamlessly
• Delays & Loss: Queuing delay occurs; buffers drop packets on congestion
• State Maintenance: Stateless core routers; adaptive per-packet dynamic routing
Circuit Switching (Legacy PSTN)
• Data Unit: Continuous bit stream over reserved physical channel
• Multiplexing: Fixed allocation via FDM (Frequency) or TDM (Time) slots
• Link Utilization: Low; reserved bandwidth wasted during idle/silent periods
• Delays & Loss: Zero queuing delay; calls blocked if no circuit available
• State Maintenance: Dedicated call setup and teardown state in every switch
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 6
1.1.3 Mathematical Delay Models in Packet Networks
M1.1 NODAL DELAY
• Total Nodal Delay ($d_{nodal}$)
Sum of 4 fundamental delay components at each intermediate router hop: $d_{nodal} = d_{proc} + d_{queue} + d_{trans} + d_{prop}$.
• Nodal Processing Delay ($d_{proc}$)
Time taken by router CPU to inspect packet header, compute bit checksums, and determine output interface (microseconds).
• Queuing Delay ($d_{queue}$)
Time packet waits inside output buffer queue before transmission. Governed by Traffic Intensity $I = (L \cdot a) / R$ ($L$ = bits, $a$ = arrival rate, $R$ = bandwidth).
• Transmission Delay ($d_{trans}$)
Time required to push all $L$ bits of the packet onto the link at rate $R$: $d_{trans} = L / R$ seconds.
• Propagation Delay ($d_{prop}$)
Time for a physical bit to travel through the physical medium over distance $d$ at speed $s \approx 2 \times 10^8$ m/s in copper/fiber: $d_{prop} = d / s$ seconds.
• Packet Loss & Throughput
When arriving traffic exceeds buffer capacity, packet drop occurs. End-to-end throughput is bottlenecked by the minimum link capacity along the transmission path.
Delay Formulas
→ d_nodal = d_proc + d_queue + d_trans + d_prop
→ d_trans = L / R (sec)
→ d_prop = d / s (sec)
→ Traffic Intensity: I = (L * a) / R
→ If I -> 1: Queuing delay -> infinity
→ Bottleneck Throughput = min(R1, R2, ...)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 7
1.1.4 Worked KTU Numerical: Delay & Throughput
M1.1 WORKED PROBLEM
📌 KTU Numerical Problem Statement
A 1500-byte packet is transmitted over a 100 km fiber link with transmission rate R = 10 Mbps. Propagation speed in fiber is s = 2 * 10^8 m/s. Nodal processing delay is 5 microseconds and the router queue currently holds 2 packets of 1500 bytes each. Calculate: (a) Transmission delay, (b) Propagation delay, (c) Queuing delay, (d) Total nodal delay.
📐 Governing Formulas & Principles:
• L = 1500 bytes = 1500 * 8 = 12,000 bits
• R = 10 Mbps = 10 * 10^6 bps
• d = 100 km = 10^5 m, s = 2 * 10^8 m/s
• d_trans = L / R, d_prop = d / s, d_queue = 2 * (L / R)
📝 Step-by-Step Derivation & Solution
Step 1: d_trans = 12,000 / 10^7 = 1.2 * 10^-3 s = 1.2 ms
Step 2: d_prop = 10^5 / (2 * 10^8) = 0.5 * 10^-3 s = 0.5 ms
Step 3: d_queue = 2 * 1.2 ms = 2.4 ms (2 packets ahead in queue)
Step 4: d_proc = 5 microseconds = 0.005 ms
Step 5: d_nodal = 0.005 + 2.4 + 1.2 + 0.5 = 4.105 ms
✅ FINAL ANSWER: Total Nodal Delay = 4.105 ms (Queuing delay is dominant)
💡 Exam Tip: In university exams, always convert bytes to bits (multiply by 8) before dividing by transmission rate R (bps).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 8
🎯 Exam Booster & Review: Internet Architecture & Delay Models
M1.1
📚 KTU High-Yield Questions (K2 / K3 Apply)
Q: Differentiate between packet switching and circuit switching with respect to bandwidth utilization, delays, and state maintenance. (7 Marks)
Q: Derive the four components of nodal delay in packet-switched networks with mathematical equations and units. (7 Marks)
Q: Explain statistical multiplexing and explain why traffic intensity I > 1 causes buffer overflow and packet loss. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Packet switching enables statistical multiplexing without dedicated circuits.
✔ Transmission delay (L/R) depends on bandwidth; Propagation delay (d/s) depends on distance.
✔ Queuing delay grows non-linearly as traffic intensity I = (L*a)/R approaches 1.
✔ End-to-end throughput is always throttled by the bottleneck link on the path.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 9
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.2
Protocol Layering & Network Models
Layering Principles, OSI 7-Layer Reference Model, TCP/IP 5-Layer Stack, PDU Encapsulation & Addressing Hierarchy
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 10
1.2.1 Principles of Layered Network Architecture
M1.2 PROTOCOL LAYERING
• Modularity & Abstraction
Dividing the massive complexity of network communication into decoupled functional layers. Each layer provides well-defined services to the layer above.
• Layer Independence
The internal implementation of a layer protocol can be completely modified or replaced without affecting adjacent layers as long as the layer interface remains unchanged.
• Encapsulation at Sender
Data moves top-down; each layer adds its own Protocol Header (and L2 adds a trailer) containing control metadata (addresses, sequence numbers, checksums).
• Decapsulation at Receiver
Data moves bottom-up; each layer processes and strips its corresponding header, passing the demultiplexed payload to the upper layer.
• Protocol Data Unit (PDU) Terminology
L5: Message (App) -> L4: Segment (TCP) / Datagram (UDP) -> L3: Packet / Datagram (IP) -> L2: Frame (Ethernet/Wi-Fi) -> L1: Raw Bit Stream.
Benefits of Layering
→ Simplifies system design
→ Standardizes interfaces
→ Enables multi-vendor hardware
→ Isolates layer troubleshooting
→ Facilitates protocol evolution
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 11
1.2.2 Comprehensive Architecture: OSI 7-Layer vs TCP/IP Stack
M1.2 OSI VS TCP/IP
OSI 7-Layer Model (ISO Conceptual)
• 7. Application: User applications & network services (HTTP, DNS)
• 6. Presentation: Data formatting, compression, encryption/decryption
• 5. Session: Dialog management, token coordination, checkpoints
• 4. Transport: End-to-end reliability, flow control, port addressing
• 3. Network: Logical host addressing (IP) & packet routing
• 2. Data Link: Node-to-node frame transfer & MAC error control
• 1. Physical: Unstructured bit transmission over raw copper/fiber/air
TCP/IP 5-Layer Internet Stack (Practical)
• 5. Application: Integrates OSI L7, L6, L5; protocols: HTTP, SMTP, DNS
• 4. Transport: Process-to-process multiplexing: TCP (reliable) & UDP
• 3. Network (Internet): Host-to-host delivery across networks: IPv4, IPv6, ICMP
• 2. Data Link: Hardware framing, MAC addressing: Ethernet, 802.11
• 1. Physical: Signals, voltages, optical pulses, RF frequencies
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 12
1.2.3 Addressing Hierarchy & PDU Encapsulation
M1.2 ADDRESSING HIERARCHY
• Application Layer Addressing
Uniform Resource Identifiers (URIs), Domain Names (FQDNs), and standardized Port Numbers.
• Transport Layer Addressing (Port Numbers)
16-bit Port Number (0 - 65,535). Well-known ports (0-1023: HTTP 80, HTTPS 443, SSH 22), Registered (1024-49151), Dynamic/Private (49152-65535).
• Network Layer Addressing (IP Addresses)
Logical 32-bit IPv4 or 128-bit IPv6 address used for global routing across subnets and autonomous systems.
• Data Link Layer Addressing (MAC Addresses)
Physical 48-bit (6-byte) EUI-48 hardware address burned into the NIC (e.g., `00:1A:2B:3C:4D:5E`). Used strictly on the local link.
• Cross-Layer Demultiplexing
L2 Frame Type field identifies L3 (IPv4 0x0800, ARP 0x0806) -> L3 Protocol field identifies L4 (TCP 6, UDP 17) -> L4 Port identifies L5 application.
Addressing Summary
→ Process ID: 16-bit Port Number
→ Host ID: 32-bit / 128-bit IP
→ NIC ID: 48-bit MAC Address
→ L2 Type 0x0800 -> IPv4
→ L3 Protocol 6 -> TCP
→ L3 Protocol 17 -> UDP
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 13
🎯 Exam Booster & Review: Protocol Layering & Network Models
M1.2
📚 KTU High-Yield Questions (K2 Understand)
Q: Compare the OSI 7-Layer model with the TCP/IP 5-Layer stack. Explain why the Presentation and Session layers are merged in TCP/IP. (8 Marks)
Q: Illustrate the step-by-step PDU encapsulation and decapsulation process across all layers with a neat labeled diagram. (7 Marks)
Q: Explain the three-level addressing hierarchy (Port, IP, MAC) and describe how demultiplexing occurs at each layer. (6 Marks)
💡 Critical Conceptual Takeaways
✔ OSI is a conceptual model; TCP/IP is the practical architecture implemented across the Internet.
✔ Headers prepend metadata: Port at L4, IP at L3, MAC and CRC FCS trailer at L2.
✔ L2 MAC changes at every router hop; L3 Source and Destination IP remain unchanged end-to-end (without NAT).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 14
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.3
Application Layer Paradigms & Requirements
Client-Server vs P2P Architectures, Transport Service Needs (Integrity, Throughput, Timing, Security), Socket Interface
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 15
1.3.1 Application Paradigms: Client-Server vs P2P
M1.3 APPLICATION PARADIGMS
Client-Server Architecture
• Centralized Server: Always-on host with fixed, well-known IP address
• Client Behavior: Initiate requests on demand; clients do not speak to each other
• Scalability Limit: Server upload capacity bottlenecks under massive simultaneous loads ($D_{CS} = \max\{N \cdot F / u_s, F / d_i\}$)
• Infrastructure Cost: Requires massive data centers, load balancers, and CDN caching
• Examples: Web (HTTP), Email (SMTP/IMAP), Remote Login (SSH)
Peer-to-Peer (P2P) Architecture
• Decentralized Peers: Arbitrary end systems communicate directly without dedicated central servers
• Self-Scalability: Peers are both consumers (downloaders) and producers (uploaders) of data
• Scalability Formula: Distribution time grows logarithmically: $D_{P2P} = \max\{F / u_s, F / d_{min}, N \cdot F / (u_s + \sum u_i)\}$
• Challenges: Churn (peers join/leave dynamically), security, ISP asymmetric bandwidth
• Examples: BitTorrent, IPFS, Blockchain, Skype (original)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 16
1.3.2 Transport Layer Service Requirements for Applications
M1.3 TRANSPORT REQUIREMENTS
• Data Integrity / Reliability
Loss-intolerant applications (Web documents, file transfer, email, banking) require 100% reliable transport (TCP). Loss-tolerant applications (audio/video streaming, VoIP) can tolerate slight packet loss (UDP).
• Throughput Guarantees
Bandwidth-sensitive applications (HD video streaming, real-time conferencing) need minimum throughput guarantees. Elastic applications (Email, Web, FTP) make use of whatever bandwidth is available.
• Timing / Latency Guarantees
Interactive gaming and VoIP require tight upper bounds on end-to-end delay (e.g., < 150 ms) to prevent human-perceptible lag.
• Security & Encryption
Application data privacy, server authentication, and message integrity provided via TLS (Transport Layer Security) running on top of TCP (e.g., HTTPS, SMTPS).
• Transport Choice Mapping
TCP: HTTP/1.1 (80), HTTPS (443), FTP (20/21), SMTP (25), SSH (22). UDP: DNS (53), SNMP (161), RTP/RTSP, DHCP (67/68), QUIC/HTTP3 (443).
Service Classification
→ Reliability: TCP (Strict) vs UDP (Loss-tolerant)
→ Timing: Sensitive (VoIP) vs Elastic (Email/Web)
→ Security: TLS/SSL cryptographic wrapper
→ Multiplexing: 16-bit Port numbers
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 17
🎯 Exam Booster & Review: Application Paradigms & Requirements
M1.3
📚 KTU High-Yield Questions (K2 Understand)
Q: Differentiate between Client-Server and Peer-to-Peer network paradigms with real-world examples. (6 Marks)
Q: Identify the transport service requirements (loss, throughput, timing, security) for HTTP, VoIP, DNS, and FTP. (6 Marks)
Q: Explain how the socket interface acts as an API bridge between application-layer user processes and kernel transport protocols. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Client-Server has centralized control and fixed IP; P2P possesses self-scalability as each leecher becomes a seeder.
✔ TCP provides 100% reliable byte-stream delivery with flow and congestion control.
✔ UDP provides low-latency, lightweight datagram delivery without handshake or congestion throttling.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 18
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.4
World Wide Web & HTTP Protocol Suite
HTTP/1.0, HTTP/1.1 (Persistent vs Non-Persistent, Pipelining), HTTP/2 (Binary Framing, Streams, Push), HTTP/3 (QUIC), Caching & Cookies
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 19
1.4.1 HTTP Protocol Fundamentals & Message Structure
M1.4 HTTP OVERVIEW
• HTTP (HyperText Transfer Protocol)
Stateless, application-layer request-response protocol operating over TCP (standard port 80, TLS encrypted HTTPS port 443).
• HTTP Request Structure
Method (GET, POST, HEAD, PUT, DELETE) + Request-URI + HTTP-Version \r\n Header Lines (Host, User-Agent, Accept, Cookie) \r\n\r\n [Optional Entity Body].
• HTTP Response Structure
HTTP-Version + Status Code (200 OK, 301 Moved, 304 Not Modified, 404 Not Found, 500 Server Error) + Status Phrase \r\n Headers (Content-Type, Content-Length, Set-Cookie, Cache-Control) \r\n\r\n [Data Body].
• Statelessness & State Management
HTTP servers maintain no state across successive requests from the same client. State is tracked using Cookies (via `Set-Cookie` and `Cookie` headers) and Session Tokens.
• Conditional GET & Web Caching
Clients and Proxy Caches avoid re-transmitting unmodified objects using the `If-Modified-Since` request header. If object unchanged, server responds `304 Not Modified` with zero body bits.
Key Status Codes
→ 200 OK: Request succeeded
→ 301 Moved Permanently: Redirect
→ 304 Not Modified: Cache hit
→ 400 Bad Request: Syntax error
→ 404 Not Found: Resource absent
→ 503 Service Unavailable: Busy
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 20
1.4.2 HTTP/1.0 vs HTTP/1.1 vs HTTP/2 vs HTTP/3
M1.4 HTTP EVOLUTION
HTTP/1.0 & HTTP/1.1
• 1.0 Non-Persistent: Opens fresh TCP connection per object ($2 \cdot RTT$ per object); high latency
• 1.1 Persistent: Reuses single TCP connection for multiple objects; default `Keep-Alive`
• Pipelining: Sends multiple requests without waiting for replies (suffers Head-of-Line blocking)
HTTP/2 (RFC 7540)
• Binary Framing: Replaces plain text with binary frame parser (Headers & Data frames)
• Multiplexing: Interleaves streams over single TCP; eliminates HTTP Head-of-Line blocking
• Server Push: Proactively pushes critical resources (CSS, JS) before client requests them
• HPACK: Compresses redundant header fields
HTTP/3 (QUIC / RFC 9000)
• QUIC over UDP: Replaces TCP with QUIC transport layer over UDP
• Zero HoL Blocking: Packet loss in one stream never stalls unrelated streams
• 0-RTT Handshake: Combines connection setup and TLS 1.3 cryptographic handshake in 1 round-trip
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 21
1.4.3 Worked KTU Numerical: Web Page Retrieval Time
M1.4 WORKED PROBLEM
📌 KTU Numerical Problem Statement
A base HTML page references 8 small embedded JPEG images located on the same server. Round-Trip Time between client and server is RTT = 40 ms. Base HTML transmission time is negligible. Calculate total retrieval time for: (a) HTTP/1.0 Non-Persistent with sequential TCP connections, (b) HTTP/1.1 Persistent without pipelining, (c) HTTP/1.1 Persistent with pipelining.
📐 Governing Formulas & Principles:
• Non-Persistent: 1 TCP Handshake (1 RTT) + 1 Request/Response (1 RTT) = 2 RTT per object
• Persistent without Pipelining: 1 TCP Handshake (1 RTT) + 1 RTT for Base + N * 1 RTT for images
• Persistent with Pipelining: 1 TCP Handshake (1 RTT) + 1 RTT for Base + 1 RTT for all images
📝 Step-by-Step Derivation & Solution
Step 1: Total objects = 1 Base HTML + 8 Images = 9 objects.
Step 2: (a) Non-Persistent: 9 objects * 2 RTT = 18 RTT = 18 * 40 ms = 720 ms.
Step 3: (b) Persistent without Pipelining: 1 RTT (TCP setup) + 1 RTT (Base HTML) + (8 * 1 RTT) = 10 RTT = 10 * 40 ms = 400 ms.
Step 4: (c) Persistent with Pipelining: 1 RTT (TCP setup) + 1 RTT (Base HTML) + 1 RTT (pipelined batch) = 3 RTT = 3 * 40 ms = 120 ms.
✅ FINAL ANSWER: Non-Persistent: 720 ms | Persistent: 400 ms | Pipelined: 120 ms
💡 Exam Tip: Always remember: TCP 3-way handshake consumes 1 full RTT before any HTTP request can be transmitted.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 22
🎯 Exam Booster & Review: World Wide Web & HTTP
M1.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the difference between non-persistent and persistent HTTP connections with timing diagrams. (7 Marks)
Q: What is Head-of-Line (HoL) blocking? How do HTTP/2 binary framing and HTTP/3 QUIC solve it? (8 Marks)
Q: Describe the mechanism of Web Caching using the Conditional GET request (`If-Modified-Since`). (5 Marks)
💡 Critical Conceptual Takeaways
✔ HTTP/1.0 incurs 2 RTT per object; HTTP/1.1 persistent reuses TCP connections to save handshakes.
✔ HTTP/2 multiplexes streams over 1 TCP connection using binary framing, but TCP packet loss stalls all streams.
✔ HTTP/3 runs over UDP with QUIC to provide independent stream streams and 0-RTT connection re-establishment.
✔ Web caches reduce traffic intensity on access links and drastically cut down end-user latency.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 23
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.5
FTP (File Transfer Protocol) Architecture
Out-of-Band Control vs In-Band Data, Control Port 21 vs Data Port 20, Active Mode (PORT) vs Passive Mode (PASV), Stateful Operation
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 24
1.5.1 Dual-Channel Architecture of FTP (RFC 959)
M1.5 FTP ARCHITECTURE
• Out-of-Band Control Connection (Port 21)
FTP establishes a dedicated TCP connection on port 21 solely for control commands (USER, PASS, LIST, RETR, STOR, QUIT) and server status replies (e.g., 220, 331, 230). Remains open throughout session.
• In-Band Data Connection (Port 20)
A separate, independent TCP connection created strictly for data transfer (file upload/download, directory listings). Opened per file transfer and closed immediately upon completion.
• Stateful Connection
Unlike stateless HTTP, FTP servers maintain extensive session state: current working directory, authenticated user credentials, transfer mode (ASCII vs Binary), and client IP/port.
• Security Limitations of Plain FTP
Credentials and data transmitted in unencrypted cleartext. Modern secure alternatives: FTPS (FTP over TLS/SSL) and SFTP (SSH File Transfer Protocol).
FTP Commands
→ USER / PASS: Authentication
→ LIST: Directory listing
→ RETR: Retrieve / Download file
→ STOR: Store / Upload file
→ TYPE A / I: ASCII / Binary mode
→ QUIT: Close session
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 25
1.5.2 Active Mode (`PORT`) vs Passive Mode (`PASV`)
M1.5 ACTIVE VS PASSIVE
Active Mode FTP (`PORT`)
• Control Channel: Client connects from random port $N$ to Server Port 21
• Data Channel Initiation: Client sends `PORT IP,p1,p2` command. Server initiates data connection from Server Port 20 to Client Port $P$
• Firewall Problem: Client-side firewalls and NATs block inbound connections initiated by external servers
• Usage: Legacy environments without client NAT firewalls
Passive Mode FTP (`PASV`)
• Control Channel: Client connects from random port $N$ to Server Port 21
• Data Channel Initiation: Client sends `PASV` command. Server opens random port $M$ and replies with `227 Entering Passive Mode`
• Firewall Friendly: Client initiates outbound connection to Server Port $M$; traversable through client NATs/firewalls
• Usage: Standard default mode across modern Internet
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 26
🎯 Exam Booster & Review: FTP Architecture & Modes
M1.5
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain why FTP is called an 'out-of-band' control protocol. How does it differ from HTTP? (6 Marks)
Q: Compare Active Mode and Passive Mode in FTP with step-by-step connection flow diagrams. Explain why Passive mode is preferred behind NAT firewalls. (8 Marks)
💡 Critical Conceptual Takeaways
✔ FTP separates control signaling (Port 21) from data bulk transfer (Port 20).
✔ In Active mode, server connects to client (fails behind client firewalls).
✔ In Passive mode, client connects to server's dynamically assigned high port (bypasses client NAT restrictions).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 27
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.6
Electronic Mail Architecture & Protocols
User Agents (UA), Mail Transfer Agents (MTA), SMTP Push Protocol (Port 25/587), MIME 7-Bit ASCII Encoding, POP3 vs IMAP4 vs Webmail
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 28
1.6.1 Email System Architecture & Message Flow
M1.6 EMAIL ARCHITECTURE
• Core Components
Three major components: User Agents (mail clients like Thunderbird, Outlook), Mail Servers (run mailboxes and outgoing message queues), and Mail Transfer Protocols.
• SMTP (Simple Mail Transfer Protocol - RFC 5321)
Push protocol operating over TCP port 25 (inter-server relay) and port 587 (client message submission with STARTTLS).
• End-to-End Delivery Flow
Alice (UA) -> Alice's Mail Server (MTA) -> [Internet Relay via SMTP over TCP] -> Bob's Mail Server (MTA mailbox) -> Bob (UA via POP3/IMAP4/HTTPS).
• SMTP Push vs Pull Architecture
SMTP pushes email from sender to receiver's server. Receiver cannot use SMTP to pull mail to their local client because client may not be online with fixed IP.
• SMTP Message Format (RFC 5322)
Header lines (`From:`, `To:`, `Subject:`, `Date:`) separated from Message Body by a blank line `\r\n`. Handled as 7-bit ASCII text.
SMTP Command Flow
→ HELO / EHLO: Client intro
→ MAIL FROM: Sender envelope
→ RCPT TO: Recipient address
→ DATA: Start message payload
→ . (Single period): End of data
→ QUIT: Terminate TCP session
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 29
1.6.2 MIME Extensions & Mail Access: POP3 vs IMAP4
M1.6 MIME & ACCESS PROTOCOLS
MIME (Multipurpose Internet Mail Extensions)
• Purpose: Allows non-ASCII binary data (images, audio, PDFs, attachments) over 7-bit ASCII SMTP
• MIME Headers: `MIME-Version: 1.0`, `Content-Type: multipart/mixed; boundary=...`, `Content-Transfer-Encoding: base64`
• Base64 Encoding: Converts 3 binary bytes (24 bits) into 4 printable ASCII characters (6 bits each; 33% overhead)
Mail Access: POP3 vs IMAP4
• POP3 (Post Office Protocol v3): TCP Port 110. 'Download and Delete' mode — copies email to local device; no server synchronization
• IMAP4 (Internet Message Access Protocol): TCP Port 143. Retains all messages/folders on server; multi-device synchronization; supports partial retrieval (e.g., fetch headers only)
• Webmail (HTTP/HTTPS): User agent runs inside web browser; uses HTTPS to communicate with webmail server
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 30
🎯 Exam Booster & Review: Electronic Mail Protocols
M1.6
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain why SMTP cannot be used by an end user to pull emails from the mail server. (5 Marks)
Q: Differentiate between POP3 and IMAP4 access protocols with respect to folder synchronization and multi-device access. (6 Marks)
Q: Explain the role of MIME in electronic mail. How does Base64 encoding convert 8-bit binary data to 7-bit ASCII? (6 Marks)
💡 Critical Conceptual Takeaways
✔ SMTP is strictly a push protocol; POP3 and IMAP4 are pull protocols.
✔ POP3 is simple and offline-oriented; IMAP4 maintains centralized state and synchronized folders across devices.
✔ MIME headers allow multimedia attachments; Base64 maps 3 binary bytes into 4 ASCII symbols.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 31
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.7
Domain Name System (DNS) Architecture
Hierarchical Distributed Database, Root/TLD/Authoritative Servers, Iterative vs Recursive Queries, DNS Caching & TTL, Resource Records (RR)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 32
1.7.1 DNS: Distributed Hierarchical Database
M1.7 DNS ARCHITECTURE
• DNS Core Function
Application-layer service translating human-readable hostnames (e.g., `www.vjcet.ac.in`) into 32-bit IPv4 / 128-bit IPv6 machine addresses.
• Why Distributed & Hierarchical?
A single centralized database would suffer single-point failure, massive traffic congestion, geographic distance delay, and impossible maintenance.
• Root DNS Servers
13 logical root server addresses (A through M, replicated worldwide via Anycast routing). Directs queries to appropriate TLD servers.
• Top-Level Domain (TLD) Servers
Responsible for generic TLDs (`.com`, `.org`, `.net`, `.edu`) and country-code ccTLDs (`.in`, `.uk`, `.de`, `.jp`).
• Authoritative DNS Servers
Maintained by organizations/service providers containing the definitive, official mapping records for an institution's public hosts.
• Local DNS Name Server (Resolver)
ISP / Campus resolver (e.g., Google 8.8.8.8, Cloudflare 1.1.1.1) acting as proxy intermediary cache for client queries.
DNS Hierarchy
→ Root Servers: Global root '.'
→ TLD Servers: .com, .in, .org
→ Authoritative: vjcet.ac.in
→ Local Resolver: ISP DNS cache
→ Runs on UDP Port 53
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 33
1.7.2 DNS Resolution Mechanisms: Iterative vs Recursive
M1.7 RESOLUTION COMPARISON
Iterative DNS Query
• Client Interaction: Local DNS server handles resolution
• Server Response: Contacted server replies: 'I don't know the exact IP, but you should ask this next DNS server' (returns referral delegation)
• Query Load: Local DNS server sequentially queries Root -> TLD -> Authoritative
• Server Burden: Puts minimal load on Root and TLD server infrastructure
Recursive DNS Query
• Server Action: Contacted server takes full responsibility to obtain the final IP address on behalf of the requester
• Chain of Queries: Client -> Local -> Root -> TLD -> Authoritative (and returns back up the chain)
• Server Burden: Heavy connection holding state and CPU burden on high-level servers; generally restricted at Root/TLD
• Standard Practice: Client to Local DNS is Recursive; Local DNS to Root/TLD/Authoritative is Iterative
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 34
1.7.3 DNS Resource Records (RR) & Message Caching
M1.7 RESOURCE RECORDS
• Resource Record (RR) 4-Tuple Format
`(Name, Value, Type, TTL)` stored in DNS database.
• Type A Record
`Name` = Hostname, `Value` = IPv4 Address (e.g., `(vjcet.ac.in, 117.211.89.5, A, 3600)`).
• Type AAAA Record
`Name` = Hostname, `Value` = 128-bit IPv6 Address.
• Type CNAME Record
`Name` = Alias hostname, `Value` = Canonical / True hostname (e.g., `(www.vjcet.org, vjcet.ac.in, CNAME, 86400)`).
• Type NS Record
`Name` = Domain, `Value` = Hostname of Authoritative Name Server for domain (e.g., `(vjcet.ac.in, ns1.vjcet.ac.in, NS, 86400)`).
• Type MX Record
`Name` = Domain, `Value` = Hostname of Mail Server for domain (e.g., `(vjcet.ac.in, mail.vjcet.ac.in, MX, 3600)`).
• DNS Caching & TTL
Resolvers cache mapping records for `TTL` seconds, dramatically reducing query delays and global root traffic.
RR Summary Table
→ Type A: Hostname -> IPv4
→ Type AAAA: Hostname -> IPv6
→ Type CNAME: Alias -> Canonical
→ Type NS: Domain -> Name Server
→ Type MX: Domain -> Mail Server
→ Type PTR: IP -> Hostname (Reverse)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 35
🎯 Exam Booster & Review: Domain Name System (DNS)
M1.7
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw and explain the step-by-step resolution process for `www.vjcet.ac.in` comparing Iterative and Recursive queries. (8 Marks)
Q: Explain the format and role of DNS Resource Records (A, AAAA, CNAME, NS, MX, PTR) with examples. (7 Marks)
Q: Why does DNS use UDP on port 53 for standard queries instead of TCP? When is TCP used in DNS? (5 Marks)
💡 Critical Conceptual Takeaways
✔ Standard DNS uses UDP port 53 for fast 1-round-trip resolution without 3-way handshake overhead.
✔ TCP port 53 is used for DNS Zone Transfers between primary/secondary servers and responses exceeding 512 bytes (EDNS0).
✔ DNS caching drastically improves web browsing latency across the globe.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 36
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.8
Peer-to-Peer Paradigm & BitTorrent Case Study
P2P File Distribution Time ($D_{P2P}$ vs $D_{CS}$), Torrents, Trackers & DHT, Chunks & Pieces, Rarest-First, Tit-for-Tat Choking
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 37
1.8.1 P2P File Distribution vs Client-Server Scalability
M1.8 P2P SCALABILITY
• File Distribution Problem
A server holds a file of size $F$ bits and needs to distribute copies to $N$ independent peer clients. Server upload rate is $u_s$, peer upload rates $u_i$, peer download rates $d_i$.
• Client-Server Distribution Time ($D_{CS}$)
$D_{CS} \ge \max \{ \frac{N \cdot F}{u_s}, \frac{F}{d_{min}} \}$. As $N$ grows, $D_{CS}$ increases linearly with $N$. Adding more clients degrades service.
• P2P Distribution Time ($D_{P2P}$)
$D_{P2P} \ge \max \{ \frac{F}{u_s}, \frac{F}{d_{min}}, \frac{N \cdot F}{u_s + \sum_{i=1}^N u_i} \}$. Each client donates upload capacity ($u_i$) back to the swarm.
• Self-Scalability of P2P
As $N \to \infty$, the total upload capacity $(u_s + \sum u_i)$ scales proportionally with demand $N \cdot F$, bounding distribution time to a sub-linear / constant asymptote.
Scalability Formulas
→ D_CS >= max(N*F/u_s, F/d_min)
→ D_P2P >= max(F/u_s, F/d_min, N*F / (u_s + sum(u_i)))
→ Client-Server scales O(N)
→ P2P scales O(1) / O(log N)
→ Peers act as uploaders
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 38
1.8.2 BitTorrent Protocol Architecture & Mechanics
M1.8 BITTORRENT PROTOCOL
• Torrents & Swarms
The collection of all peers participating in the distribution of a specific file is called a Swarm. File metadata is encoded in a `.torrent` file containing SHA-1 hashes of chunks.
• Chunks & Pieces
The file is partitioned into equal chunks (typically 256 KB to 2 MB). As soon as a peer downloads a chunk, it can immediately upload it to other peers.
• Tracker & Trackerless DHT
A central Tracker node maintains the list of active IP addresses in the swarm. Modern BitTorrent uses Kademlia Distributed Hash Tables (DHT) for trackerless operation.
• Rarest-First Chunk Selection
A peer determines which chunks are least common among its neighbors and requests those first. Ensures rare chunks are duplicated rapidly across the swarm to prevent missing chunk bottlenecks.
• Tit-for-Tat (TFT) Choking Algorithm
A peer gives upload priority to the top 4 peers currently supplying data to it at the highest rates (unchoked every 10 s).
• Optimistic Unchoking
Every 30 s, a peer randomly picks 1 additional peer to upload to, discovering new faster partners and allowing newcomers to obtain their initial chunk.
BitTorrent Mechanics
→ Swarm: Group of active peers
→ Chunk Size: 256 KB - 2 MB
→ Rarest-First: Balances supply
→ Tit-for-Tat: Incentivizes uploading
→ Optimistic Unchoking: Finds peers
→ Seeders: 100% complete file
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 39
🎯 Exam Booster & Review: P2P & BitTorrent
M1.8
📚 KTU High-Yield Questions (K3 Apply)
Q: Derive the theoretical file distribution time for Client-Server ($D_{CS}$) and P2P ($D_{P2P}$) architectures. (8 Marks)
Q: Explain the working of BitTorrent with focus on Rarest-First chunk selection, Tit-for-Tat choking, and Optimistic Unchoking. (8 Marks)
Q: What is peer churn in P2P networks, and how does Distributed Hash Table (DHT) handle it? (5 Marks)
💡 Critical Conceptual Takeaways
✔ Client-Server distribution time increases linearly with $N$, whereas P2P distributes the upload burden.
✔ Rarest-First ensures even chunk distribution across the swarm.
✔ Tit-for-Tat solves free-riding by rewarding peers who contribute upload bandwidth.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 40
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 1 • M1.9
Application Layer Case Study: CDNs & Video Streaming
Content Distribution Networks (CDNs), DNS Redirection, Edge Server Placement, DASH (Dynamic Adaptive Streaming over HTTP)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 41
1.9.1 Content Distribution Networks (CDNs)
M1.9 CDN ARCHITECTURE
• The Web Scale Problem
Serving massive video traffic (YouTube, Netflix) from a single mega data center causes single point of failure, network congestion, long-distance delay, and repeated link traversals.
• CDN Philosophy
Deploy thousands of geographically distributed server clusters (Points of Presence - PoPs) at edge ISPs across the globe. Store replicated video copies close to end users.
• Server Placement Philosophies
1. Enter Deep (Akamai): Deploy clusters inside thousands of access ISPs close to users. 2. Bring Home (Limelight): Deploy fewer large clusters at Tier-1 PoPs interconnected by private backbone.
• CDN DNS Redirection
When user requests `video.netflix.com`, authoritative DNS intercepts the request and returns a CNAME pointing to CDN domain. CDN's DNS resolver uses client IP to return the IP address of the geographically closest edge cache server.
CDN Benefits
→ Ultra-low latency to users
→ Reduces ISP transit costs
→ Absorbs DDoS attacks
→ High availability & redundancy
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 42
1.9.2 DASH: Dynamic Adaptive Streaming over HTTP
M1.9 DASH VIDEO
• Video Encoding & Chunks
Video is pre-encoded at multiple quality/bitrate versions (e.g., 360p 500 kbps, 720p 2 Mbps, 1080p 5 Mbps, 4K 15 Mbps) and partitioned into small chunks (2 to 10 seconds each).
• MPD (Media Presentation Description)
An XML manifest file listing the URLs and bitrates for all chunks across every quality level.
• Client-Side Dynamic Adaptation
The client player continuously monitors available download bandwidth and buffer occupancy. It dynamically requests high-quality chunks when bandwidth is ample, and gracefully steps down to lower bitrates to avoid playback stalling.
• Transport over HTTP/TCP
Streams over standard HTTP/HTTPS port 80/443, effortlessly traversing firewalls and NATs without requiring proprietary streaming server protocols.
DASH Algorithm
→ MPD Manifest: Lists chunks & bitrates
→ Client measures throughput
→ If buffer high -> Request 4K/1080p
→ If bandwidth drops -> Request 720p
→ Zero playback interruption
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 43
🎯 Exam Booster & Review: CDN & Streaming Case Study
M1.9
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain how Content Distribution Networks (CDNs) use DNS redirection to route user requests to the optimal edge server. (8 Marks)
Q: Describe the architecture and working of Dynamic Adaptive Streaming over HTTP (DASH). (7 Marks)
💡 Critical Conceptual Takeaways
✔ CDNs bring content close to users, cutting down WAN transit delays and backbone congestion.
✔ DNS CNAME redirection enables real-time dynamic traffic routing based on network conditions.
✔ DASH shifts streaming intelligence to the client, adapting video bitrate in real time.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 44
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 MASTER • MODULE 2 MASTER DECK
Transport & Network Layer Architecture
Complete Lecture Slides for KTU PCCST501 Computer Networks | Topics M2.1.1 through M2.3
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 45
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.1
Transport Layer Services & Multiplexing Principles
Process-to-Process Communication, Port Addressing, Connectionless vs Connection-Oriented Demultiplexing (2-Tuple vs 4-Tuple)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 46
2.1.1.1 Transport Layer Core Responsibilities
M2.1.1 TRANSPORT SERVICES
• Process-to-Process Logical Delivery
While the Network Layer delivers packets host-to-host between IP addresses, the Transport Layer extends this to deliver messages process-to-process between application sockets.
• Port Addressing & Socket Binding
Processes are identified via 16-bit Port Numbers (0 to 65,535). Sockets bind an IP address and Port number together as an end-to-end communication endpoint.
• Transport Layer Responsibilities
1. Multiplexing & Demultiplexing, 2. Reliability (Loss detection, ACKs, retransmissions), 3. Flow Control (Preventing receiver buffer overflow), 4. Congestion Control (Preventing network core collapse).
• Transport Limitations
Transport protocols cannot provide hard real-time delay bounds or guaranteed bandwidth on standard best-effort IP networks.
Key Port Numbers
→ Port 80: HTTP
→ Port 443: HTTPS
→ Port 22: SSH
→ Port 53: DNS
→ Port 25: SMTP
→ Port 21: FTP Control
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 47
2.1.1.2 Demultiplexing: Connectionless (UDP) vs Connection-Oriented (TCP)
M2.1.1 DEMULTIPLEXING
UDP Demultiplexing (2-Tuple)
• Identifier Tuple: Identified strictly by: `(Destination IP, Destination Port)`
• Behavior: Two UDP datagrams arriving from different source IP/ports targeted at same Dest Port are delivered to the exact same socket
• State: Completely stateless; no connection handshake or per-peer buffers
• Speed: Zero connection establishment latency
TCP Demultiplexing (4-Tuple)
• Identifier Tuple: Identified by 4-tuple: `(Source IP, Source Port, Destination IP, Destination Port)`
• Behavior: Server listening socket (`listen()`) forks/spawns a distinct connected socket (`accept()`) for each unique client 4-tuple
• State: Full connection state, sequence tracking, and dedicated receive buffers per connection
• Scalability: Enables concurrent multi-client web/database servers
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 48
🎯 Exam Booster & Review: Transport Layer Services
M2.1.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Differentiate between host-to-host delivery and process-to-process delivery with a neat diagram. (6 Marks)
Q: Explain how multiplexing and demultiplexing work in UDP and TCP. Why does TCP require a 4-tuple while UDP needs only a 2-tuple? (8 Marks)
💡 Critical Conceptual Takeaways
✔ Network layer provides host-to-host IP delivery; Transport layer provides process-to-process port delivery.
✔ UDP demux uses Destination Port only; TCP demux uses Source IP, Source Port, Dest IP, Dest Port.
✔ TCP creates separate connected sockets for every distinct client connection.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 49
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.2
Transport Protocols & User Datagram Protocol (UDP)
UDP Segment Header Structure, 16-Bit 1's Complement Checksum with Pseudo-Header, UDP Applications & Use Cases
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 50
2.1.2.1 UDP Protocol Architecture & 8-Byte Header
M2.1.2 UDP ARCHITECTURE
• UDP Characteristics (RFC 768)
Connectionless, unreliable, lightweight, message-oriented transport protocol. Provides bare minimum services: process multiplexing and optional error checking.
• Why Use UDP?
1. No connection establishment delay (0-RTT), 2. No connection state at server, 3. Small header overhead (8 bytes vs TCP 20 bytes), 4. Unregulated send rate (no congestion throttling).
• UDP 8-Byte Header Format (32-bit width)
Source Port (16 bits) | Destination Port (16 bits) \n Length (16 bits, header + payload in bytes) | Checksum (16 bits).
• Message Boundary Preservation
UDP sends data in discrete datagrams. If sender writes 500 bytes twice, receiver reads 500 bytes twice (preserves message boundaries, unlike TCP byte stream).
Header Breakdown
→ Source Port: 16 bits
→ Destination Port: 16 bits
→ Length: 16 bits (Min 8 B)
→ Checksum: 16 bits
→ Total Header: Exactly 8 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 51
2.1.2.2 UDP 16-Bit 1's Complement Checksum Calculation
M2.1.2 CHECKSUM CALCULATION
📌 KTU Numerical Problem Statement
Compute the UDP checksum for three 16-bit words: Word 1 = 0x66B4 (0110 0110 1011 0100), Word 2 = 0x5555 (0101 0101 0101 0101), Word 3 = 0x8F0C (1000 1111 0000 1100). Show wraparound carry addition and 1's complement inversion. Also explain how the receiver verifies checksum integrity.
📐 Governing Formulas & Principles:
• Step 1: Sum 16-bit words using standard binary addition.
• Step 2: If sum produces a 17th bit (carry overflow), wrap it around and add to the least significant bit.
• Step 3: Invert all bits (1's complement) to obtain the transmitted Checksum field.
• Receiver: Sums all received words including Checksum; valid result must be 0xFFFF (all 1s).
📝 Step-by-Step Derivation & Solution
Step 1: Sum Word 1 + Word 2: 0x66B4 + 0x5555 = 0xBC09 (1011 1100 0000 1001)
Step 2: Add Word 3: 0xBC09 + 0x8F0C = 0x14B15 (1 0100 1011 0001 0101 - Carry generated!)
Step 3: Wrap carry around: 0x4B15 + 1 = 0x4B16 (0100 1011 0001 0110)
Step 4: Take 1's complement (~0x4B16): 1011 0100 1110 1001 = 0xB4E9 (Checksum transmitted)
Step 5: Receiver Verification: 0x4B16 + 0xB4E9 = 0xFFFF (1111 1111 1111 1111 -> Verified Valid!)
✅ FINAL ANSWER: Transmitted Checksum = 0xB4E9 | Receiver sum = 0xFFFF
💡 Exam Tip: Note: UDP includes an IP Pseudo-Header (Source IP, Dest IP, Protocol 17, UDP Length) in checksum calculation to detect misrouted packets.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 52
🎯 Exam Booster & Review: UDP Protocol & Checksum
M2.1.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the UDP segment header format and explain all fields. Why is UDP header size fixed at 8 bytes? (6 Marks)
Q: Explain the step-by-step procedure for computing the UDP 16-bit 1's complement checksum. What is the role of the pseudo-header? (8 Marks)
Q: Why is UDP preferred over TCP for DNS queries, SNMP, and real-time gaming? (5 Marks)
💡 Critical Conceptual Takeaways
✔ UDP header is minimal (8 bytes) with Source Port, Dest Port, Length, and Checksum.
✔ Checksum calculation wraps around carry bits and inverts result for easy receiver verification (0xFFFF).
✔ UDP avoids TCP connection overhead and latency fluctuations from retransmissions.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 53
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.3
Transmission Control Protocol (TCP) Architecture
TCP 20-Byte Header Format, 3-Way Handshake Connection Setup, 4-Way Connection Teardown (TIME_WAIT 2MSL), Sequence/ACK Mechanics
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 54
2.1.3.1 TCP Header Architecture (RFC 793 / 9293)
M2.1.3 TCP HEADER
• Connection-Oriented Byte Stream
TCP provides full-duplex, reliable, sequenced byte-stream transfer between communicating processes.
• Header Format (20 to 60 Bytes)
Source Port (16b) | Destination Port (16b) \n Sequence Number (32b: byte-stream offset) \n Acknowledgment Number (32b: next expected byte) \n Data Offset (4b: header length in 32-bit words) | Reserved (4b) | Flags (8b) | Window Size (16b) \n Checksum (16b) | Urgent Pointer (16b) \n Options (0 to 40 bytes: MSS, Window Scale, SACK, Timestamps).
• TCP Control Flags
SYN (Establish connection), ACK (Ack valid), FIN (Close connection), RST (Reset/abort connection), PSH (Push data immediately to app), URG (Urgent pointer active), ECE & CWR (Explicit Congestion Notification).
• Cumulative Acknowledgment
TCP Ack number $N$ indicates the receiver has successfully received all contiguous bytes up to $N-1$ and is expecting byte $N$.
TCP Control Flags
→ SYN: Connection request
→ ACK: Acknowledgment field
→ FIN: Graceful teardown
→ RST: Reset connection
→ PSH: Push buffer to app
→ URG: Out-of-band data
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 55
2.1.3.2 Connection Lifecycle: 3-Way Handshake vs 4-Way Teardown
M2.1.3 TCP LIFECYCLE
3-Way Handshake (Connection Setup)
• Step 1 (Client -> Server): Client sends `SYN = 1`, `Seq = x` (Initial Sequence Number $ISN_c$). Enters `SYN_SENT` state
• Step 2 (Server -> Client): Server allocates buffers, replies `SYN = 1`, `ACK = 1`, `Seq = y` ($ISN_s$), `Ack = x + 1`. Enters `SYN_RCVD`
• Step 3 (Client -> Server): Client sends `ACK = 1`, `Seq = x + 1`, `Ack = y + 1` (may piggyback initial application data). Enters `ESTABLISHED`
• SYN Flood Defense: TCP SYN Cookies prevent server memory exhaustion from bogus SYN requests
4-Way Connection Teardown (Graceful Close)
• Step 1 (Client -> Server): Client finishes sending, transmits `FIN = 1`, `Seq = u`. Enters `FIN_WAIT_1`
• Step 2 (Server -> Client): Server acknowledges with `ACK = 1`, `Ack = u + 1`. Enters `CLOSE_WAIT`; Client enters `FIN_WAIT_2`
• Step 3 (Server -> Client): Server finishes outstanding data, transmits `FIN = 1`, `Seq = v`. Enters `LAST_ACK`
• Step 4 (Client -> Server): Client replies `ACK = 1`, `Ack = v + 1`. Client enters `TIME_WAIT` for 2MSL (Maximum Segment Lifetime = 60-120s) before terminating to ensure final ACK delivery
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 56
🎯 Exam Booster & Review: TCP Connection Management
M2.1.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the complete TCP segment header format and explain all fields, especially Sequence Number, ACK Number, and Control Flags. (8 Marks)
Q: Illustrate the TCP 3-Way Handshake with sequence and acknowledgment numbers. Why is a 2-way handshake insufficient? (8 Marks)
Q: Explain the purpose of the `TIME_WAIT` state and the 2MSL timer during TCP connection termination. (5 Marks)
💡 Critical Conceptual Takeaways
✔ TCP Sequence number tracks the byte offset of transmitted data; ACK number represents the next expected byte.
✔ 3-way handshake is mandatory to synchronize Initial Sequence Numbers (ISNs) bi-directionally and verify full-duplex connectivity.
✔ `TIME_WAIT` (2MSL) guarantees that any lingering duplicate packets in the network expire before the socket is reused.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 57
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.4
TCP Flow & Congestion Control Mechanisms
Sliding Window Flow Control, Silly Window Syndrome, Congestion Window (cwnd), Slow Start, AIMD, Fast Retransmit, TCP Tahoe vs Reno
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 58
2.1.4.1 Flow Control & Silly Window Syndrome
M2.1.4 FLOW CONTROL
• Flow Control Goal
Matches the sender's transmission rate to the receiver's consumption rate to prevent receiver buffer overflow.
• Receive Window (`rwnd`) Mechanics
Receiver advertises remaining buffer space via `rwnd` field in TCP header. Sender ensures: $\text{LastByteSent} - \text{LastByteAcked} \le \min(\text{cwnd}, \text{rwnd})$.
• Zero-Window Probing
When receiver buffer is full (`rwnd = 0`), sender stops transmitting but periodically sends 1-byte probe segments to force receiver to return window update ACKs.
• Silly Window Syndrome (SWS)
Occurs when data is transmitted in tiny chunks (1 byte payload + 40 bytes header = 97.5% overhead).
• SWS Solutions
1. **Nagle's Algorithm (Sender-side)**: Send first small segment; buffer subsequent data until all previous data is ACKed or MSS is reached. 2. **Clark's Solution (Receiver-side)**: Receiver advertises `rwnd = 0` until buffer space is at least MSS or 50% buffer capacity.
Key Variables
→ rwnd: Receiver buffer limit
→ cwnd: Network congestion limit
→ Effective Win = min(cwnd, rwnd)
→ Nagle's: Buffers small writes
→ Clark's: Suppresses tiny rwnd
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 59
2.1.4.2 Congestion Control: TCP Tahoe vs TCP Reno
M2.1.4 TAHOE VS RENO
TCP Tahoe (Legacy)
• Slow Start Phase: Begins with `cwnd = 1 MSS`. Increases `cwnd` exponentially: doubles every RTT (`cwnd += 1 MSS` per ACK received)
• Congestion Avoidance: When `cwnd >= ssthresh`, transitions to AIMD: increases `cwnd` linearly by 1 MSS per RTT
• On Loss Detection (Timeout or 3 Dup ACKs): 1. `ssthresh = cwnd / 2` \n 2. Drops `cwnd = 1 MSS` (always resets to slow start)
• Performance: Severe throughput collapse upon any single packet loss
TCP Reno (Standard)
• Slow Start & Congestion Avoidance: Identical to Tahoe during normal growth
• On Timeout Loss: Severe congestion: `ssthresh = cwnd / 2`, `cwnd = 1 MSS` (resets to Slow Start)
• On 3 Duplicate ACKs (Fast Retransmit): Mild congestion: Retransmits lost segment immediately without waiting for retransmission timer to expire
• Fast Recovery Phase: Skips slow start! Sets `ssthresh = cwnd / 2`, sets `cwnd = ssthresh + 3 MSS`, continues linear AIMD growth
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 60
2.1.4.3 Worked KTU Numerical: TCP Congestion Window Evolution
M2.1.4 WORKED PROBLEM
📌 KTU Numerical Problem Statement
A TCP Reno connection has ssthresh = 16 MSS. Starting at RTT 1 with cwnd = 1 MSS in Slow Start: (a) Trace cwnd values up to RTT 8. (b) At RTT 8, three duplicate ACKs are received. Calculate new ssthresh and cwnd for RTT 9 and RTT 10 under Fast Recovery.
📐 Governing Formulas & Principles:
• Slow Start: cwnd doubles every RTT until ssthresh is reached.
• Congestion Avoidance (AIMD): cwnd increases by +1 MSS per RTT.
• Fast Retransmit / Fast Recovery (3 Dup ACKs): ssthresh_new = cwnd / 2, cwnd_new = ssthresh_new.
📝 Step-by-Step Derivation & Solution
Step 1: RTT 1: cwnd = 1 MSS (Slow Start)
Step 2: RTT 2: cwnd = 2 MSS | RTT 3: cwnd = 4 MSS | RTT 4: cwnd = 8 MSS | RTT 5: cwnd = 16 MSS (ssthresh reached)
Step 3: RTT 6: cwnd = 17 MSS (AIMD Linear) | RTT 7: cwnd = 18 MSS | RTT 8: cwnd = 19 MSS
Step 4: At RTT 8, 3 Dup ACKs occur: ssthresh_new = 19 / 2 = 9.5 -> 9 MSS.
Step 5: RTT 9: Under TCP Reno Fast Recovery, cwnd = 9 MSS. RTT 10: cwnd = 10 MSS (continues linear AIMD).
✅ FINAL ANSWER: RTT 8: 19 MSS -> Loss -> RTT 9: cwnd = 9 MSS, ssthresh = 9 MSS
💡 Exam Tip: If loss was caused by Timeout instead of 3 Dup ACKs, cwnd would drop to 1 MSS.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 61
🎯 Exam Booster & Review: TCP Flow & Congestion Control
M2.1.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain TCP Sliding Window flow control and how the receiver window `rwnd` prevents buffer overrun. (7 Marks)
Q: What is Silly Window Syndrome? Explain Nagle's algorithm and Clark's solution with examples. (8 Marks)
Q: Compare TCP Tahoe and TCP Reno congestion control algorithms with a neat graph plotting `cwnd` versus Transmission RTTs. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Flow control is receiver-driven (`rwnd`); Congestion control is network-driven (`cwnd`).
✔ Effective transmission window is the minimum of `cwnd` and `rwnd`.
✔ TCP Reno avoids slow start upon 3 duplicate ACKs via Fast Retransmit and Fast Recovery.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 62
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.1.5
Berkeley Socket API & I/O Multiplexing
Socket System Calls Lifecycle (TCP & UDP), I/O Multiplexing with select() and poll(), fd_set Macros, Non-Blocking Sockets
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 63
2.1.5.1 Berkeley Socket API System Call Lifecycle
M2.1.5 SOCKET API
• Socket Abstraction
A socket is a kernel endpoint for network I/O represented as an integer file descriptor in Linux (`int sockfd`).
• TCP Server Lifecycle
1. `socket(AF_INET, SOCK_STREAM, 0)` -> Creates endpoint \n 2. `bind(sockfd, &addr, sizeof)` -> Associates socket with IP/Port \n 3. `listen(sockfd, backlog)` -> Sets passive listening mode and backlog queue \n 4. `accept(sockfd, &client_addr, &len)` -> Blocks until client connects, returns new connected descriptor \n 5. `read()` / `write()` or `recv()` / `send()` -> Data exchange \n 6. `close(sockfd)` -> Tears down connection.
• TCP Client Lifecycle
1. `socket()` -> 2. `connect(sockfd, &server_addr, sizeof)` (initiates 3-way handshake) -> 3. `write()` / `read()` -> 4. `close()`.
• UDP Sockets
Connectionless: Server calls `socket()` -> `bind()` -> `recvfrom()` -> `sendto()`. Client calls `socket()` -> `sendto()` -> `recvfrom()` without `listen()` or `accept()`.
Key System Calls
→ socket(): Create fd
→ bind(): Bind IP & Port
→ listen(): Passive queue
→ accept(): Return client fd
→ connect(): 3-way handshake
→ sendto()/recvfrom(): UDP
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 64
2.1.5.2 I/O Multiplexing: `select()` System Call
M2.1.5 IO MULTIPLEXING
// Linux Socket & Protocol Implementation
#include <sys/select.h> int max_fd = listen_fd; fd_set read_fds; while (1) { FD_ZERO(&read_fds); FD_SET(listen_fd, &read_fds); // Add active client descriptors for (int i = 0; i < max_clients; i++) { if (client_fds[i] > 0) FD_SET(client_fds[i], &read_fds); if (client_fds[i] > max_fd) max_fd = client_fds[i]; } // Block until at least one descriptor is ready for read int activity = select(max_fd + 1, &read_fds, NULL, NULL, NULL); if (FD_ISSET(listen_fd, &read_fds)) { int new_fd = accept(listen_fd, ...); // Add new_fd to client list } }
⚙️ System Call & Execution Workflow
• Why I/O Multiplexing?: Allows a single-threaded server process to monitor multiple socket descriptors simultaneously without blocking on any single slow client.
• `fd_set` Bitmask Macros: `FD_ZERO(&set)` clears mask, `FD_SET(fd, &set)` adds fd, `FD_CLR(fd, &set)` removes fd, `FD_ISSET(fd, &set)` tests readiness.
• `select()` Parameters: `int select(int nfds, fd_set *readfds, fd_set *writefds, fd_set *exceptfds, struct timeval *timeout)`. `nfds` is `max_fd + 1`.
• `poll()` vs `select()`: `poll()` uses array of `struct pollfd` (no `FD_SETSIZE` 1024 descriptor limit and separate input/output events).
💡 Hands-on Insight: Single-threaded I/O multiplexing handles hundreds of concurrent connections with minimal memory overhead compared to multi-threading.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 65
🎯 Exam Booster & Review: Socket API & select()
M2.1.5
📚 KTU High-Yield Questions (K3 Apply)
Q: Write the sequence of Berkeley socket system calls executed on both server and client for TCP connection establishment and data transfer. (8 Marks)
Q: Explain the working of I/O multiplexing using the `select()` system call with code structure and `fd_set` macros. (8 Marks)
Q: Differentiate between blocking, non-blocking, and I/O multiplexed socket architectures. (6 Marks)
💡 Critical Conceptual Takeaways
✔ `listen()` creates a passive socket queue; `accept()` extracts the next connection from the queue.
✔ `select()` monitors multiple file descriptors simultaneously, unblocking as soon as any fd is ready.
✔ `poll()` and `epoll()` overcome the 1024 file descriptor limitation of traditional `select()`.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 66
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.1
Network Layer Architecture & Router Design
Data Plane (Forwarding) vs Control Plane (Routing), Datagram Networks vs Virtual Circuits, Router Fabrics & Buffer Queuing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 67
2.2.1.1 Network Layer: Data Plane vs Control Plane
M2.2.1 NETWORK ARCHITECTURE
• Network Layer Core Mission
Achieving end-to-end host-to-host packet delivery across multiple heterogeneous intermediate networks.
• Data Plane (Forwarding)
Local, per-router action. Takes a packet arriving on an input link interface and moves it to the appropriate output link interface in nanoseconds. Implemented in high-speed hardware ASIC/TCAM.
• Control Plane (Routing)
Network-wide logic. Determines the end-to-end global path that packets take from source to destination. Implemented in software routing algorithms (OSPF, RIP, BGP) or centralized SDN controllers.
• Service Models
Internet uses Best-Effort Service Model: no guarantees on delivery, delay, bandwidth, or ordering. Simplicity in the network core pushed intelligence to end hosts.
Plane Separation
→ Data Plane: Local forwarding (ASIC/Hardware)
→ Control Plane: Global routing (Software/OSPF)
→ Nanosecond speed in Data Plane
→ Millisecond speed in Control Plane
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 68
2.2.1.2 Network Models: Datagram vs Virtual Circuit
M2.2.1 DATAGRAM VS VC
Datagram Networks (Internet IP)
• Connection Setup: No connection setup phase; packets injected immediately
• Addressing: Packets carry full global 32-bit/128-bit Source and Destination IP
• Routing Path: Each packet routed independently; successive packets may follow different paths
• Router State: Stateless routers; failure of a link triggers automatic rerouting
• Complexity: Pushed to network edge end hosts
Virtual Circuit Networks (ATM / Frame Relay)
• Connection Setup: Mandatory end-to-end signaling setup before data transfer
• Addressing: Packets carry small local Virtual Circuit Identifier (VCI)
• Routing Path: All packets in a connection follow the exact same fixed virtual path
• Router State: Routers maintain per-connection state tables; link failure drops VC
• Complexity: Heavy complexity in network core switches
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 69
🎯 Exam Booster & Review: Network Layer Architecture
M2.2.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Differentiate between the Data Plane and Control Plane of the Network Layer. (6 Marks)
Q: Compare Datagram networks and Virtual Circuit networks with respect to connection setup, addressing, and router state. (8 Marks)
Q: Describe the internal architecture of a modern high-speed router (Input Ports, Switching Fabric, Output Ports). (7 Marks)
💡 Critical Conceptual Takeaways
✔ Forwarding is local and hardware-based; Routing is global and software-based.
✔ Internet uses datagram packet switching with stateless routers for maximum resilience.
✔ Crossbar switching fabrics eliminate internal shared bus contention in high-speed routers.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 70
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.2
IPv4 Addressing, Subnetting, CIDR & NAT
IPv4 20-60 Byte Header, Fragmentation & Reassembly, Classless Addressing (CIDR), Subnet Design, NAT/PAT, ICMP Protocol
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 71
2.2.2.1 IPv4 Header Format & Fragmentation
M2.2.2 IPV4 HEADER
• IPv4 Header Structure (20 to 60 Bytes)
Version (4b: 4) | IHL (4b: Header length in 32-bit words, min 5 = 20B) | DSCP/ECN (8b: QoS) | Total Length (16b: Header + Payload, max 65535B) \n Identification (16b) | Flags (3b: Reserved, DF, MF) | Fragment Offset (13b: measured in 8-byte units) \n TTL (8b: Time-to-Live, decremented per hop) | Protocol (8b: ICMP=1, TCP=6, UDP=17) | Header Checksum (16b) \n Source IP (32b) \n Destination IP (32b) \n Options (0-40B).
• Fragmentation Fields
**Identification**: Identifies fragments belonging to same original datagram. **DF (Don't Fragment)**: If set to 1, router drops packet if larger than MTU. **MF (More Fragments)**: 1 for all fragments except the final one (0). **Fragment Offset**: Byte offset divided by 8.
• Reassembly
Occurs strictly at the final destination host before delivering to the transport layer.
Key Header Fields
→ IHL: Header words (x4 bytes)
→ Total Length: Max 65,535 B
→ TTL: Prevents routing loops
→ Protocol: 6=TCP, 17=UDP, 1=ICMP
→ Offset unit = 8 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 72
2.2.2.2 Worked KTU Numerical: IPv4 Fragmentation
M2.2.2 FRAGMENTATION PROBLEM
📌 KTU Numerical Problem Statement
An IPv4 datagram with Total Length = 4000 bytes (20-byte IP header + 3980 bytes payload) arrives at a router whose outgoing link has Maximum Transmission Unit MTU = 1500 bytes. Calculate the Total Length, Payload Length, MF flag, and Fragment Offset for all resulting fragments.
📐 Governing Formulas & Principles:
• MTU = 1500 bytes (Max payload per fragment = 1500 - 20 = 1480 bytes).
• 1480 is divisible by 8 (1480 / 8 = 185) -> Valid maximum payload per fragment.
• Total payload to fragment = 3980 bytes.
• Fragment Offset = Total previous payload bytes divided by 8.
📝 Step-by-Step Derivation & Solution
Step 1: Frag 1: Header = 20 B, Payload = 1480 B, Total Length = 1500 B, MF = 1, Offset = 0 / 8 = 0
Step 2: Frag 2: Header = 20 B, Payload = 1480 B, Total Length = 1500 B, MF = 1, Offset = 1480 / 8 = 185
Step 3: Remaining payload = 3980 - 1480 - 1480 = 1020 B.
Step 4: Frag 3: Header = 20 B, Payload = 1020 B, Total Length = 1040 B, MF = 0 (last fragment!), Offset = 2960 / 8 = 370
✅ FINAL ANSWER: Frag 1: Len 1500, MF=1, Off=0 | Frag 2: Len 1500, MF=1, Off=185 | Frag 3: Len 1040, MF=0, Off=370
💡 Exam Tip: Always verify that Fragment Offset values are integer multiples of 8 bytes!
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 73
2.2.2.3 Worked KTU Numerical: CIDR Subnetting
M2.2.2 SUBNETTING PROBLEM
📌 KTU Numerical Problem Statement
An organization is allocated the block `200.50.16.0/24`. Design 4 equal-sized subnets. For each subnet, specify: (a) Subnet Mask, (b) Network Address, (c) Usable Host Range, (d) Direct Broadcast Address, (e) Maximum usable hosts.
📐 Governing Formulas & Principles:
• Given /24 network: 8 host bits (256 addresses).
• To create 4 subnets: Need 2 subnet bits (2^2 = 4). New prefix = /24 + 2 = /26.
• Block size per subnet = 256 / 4 = 64 addresses.
• Usable hosts per subnet = 2^(32 - 26) - 2 = 64 - 2 = 62 hosts.
📝 Step-by-Step Derivation & Solution
Step 1: Subnet Mask: 255.255.255.192 (/26)
Step 2: Subnet 1: Net = 200.50.16.0/26 | Hosts = 200.50.16.1 to 200.50.16.62 | Broadcast = 200.50.16.63
Step 3: Subnet 2: Net = 200.50.16.64/26 | Hosts = 200.50.16.65 to 200.50.16.126 | Broadcast = 200.50.16.127
Step 4: Subnet 3: Net = 200.50.16.128/26 | Hosts = 200.50.16.129 to 200.50.16.190 | Broadcast = 200.50.16.191
Step 5: Subnet 4: Net = 200.50.16.192/26 | Hosts = 200.50.16.193 to 200.50.16.254 | Broadcast = 200.50.16.255
✅ FINAL ANSWER: 4 Subnets of /26 mask (255.255.255.192), each accommodating 62 usable hosts
💡 Exam Tip: First address is Network ID; Last address is Directed Broadcast; both cannot be assigned to hosts.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 74
🎯 Exam Booster & Review: IPv4, CIDR & NAT
M2.2.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the complete IPv4 header format and explain all fields with numerical significance. (8 Marks)
Q: Explain the working of Network Address Translation (NAT) and Port Address Translation (PAT) with translation table examples. (7 Marks)
Q: What is ICMP? Explain its role in error reporting (Destination Unreachable, Time Exceeded) and diagnostic tools (`ping`, `traceroute`). (6 Marks)
💡 Critical Conceptual Takeaways
✔ IPv4 fragmentation uses ID, Flags (DF, MF), and Offset in 8-byte blocks.
✔ CIDR replaces classful boundaries with arbitrary prefix lengths (/N) and Longest Prefix Matching.
✔ NAT allows private IP subnets (RFC 1918) to share a single public IP using port mapping tables.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 75
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.3
Unicast Routing Protocols & Algorithms
Link-State Routing & Dijkstra's Algorithm, Distance-Vector & Bellman-Ford, Count-to-Infinity, RIP, OSPF & BGP-4
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 76
2.2.3.1 Link-State (LS) vs Distance-Vector (DV) Algorithms
M2.2.3 LS VS DV ROUTING
Link-State (LS) Routing (e.g., OSPF)
• Global Topology Knowledge: Every router floods link-state advertisements (LSAs); all nodes possess full network topology graph
• Algorithm: Dijkstra's Shortest Path Algorithm run locally on each router
• Convergence Speed: Ultra-fast convergence; zero routing loops
• Message Overhead: $O(N \cdot E)$ messages flooded periodically
• Complexity: $O(V^2)$ or $O(E \log V)$ computation per router
Distance-Vector (DV) Routing (e.g., RIP)
• Local Knowledge Only: Routers only know cost to immediate direct neighbors; exchange vectors periodically
• Algorithm: Distributed Bellman-Ford equation: $d_x(y) = \min_v \{c(x,v) + d_v(y)\}$
• Convergence Speed: Slow convergence; susceptible to Count-to-Infinity problem
• Mitigation: Split Horizon and Poisoned Reverse rules
• Simplicity: Lightweight computation; suitable for small networks
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 77
2.2.3.2 Internet Routing Protocols: RIP vs OSPF vs BGP-4
M2.2.3 PROTOCOL COMPARISON
• RIP (Routing Information Protocol - RFC 2453)
Intra-AS Distance Vector protocol. Uses Hop Count metric (max 15 hops; 16 = infinity). Updates broadcast every 30s over UDP port 520.
• OSPF (Open Shortest Path First - RFC 2328)
Intra-AS Link State protocol. Uses link cost based on inverse bandwidth. Hierarchical design with Area 0 (Backbone Area) and non-backbone areas. Runs directly over IP protocol 89. Supports authenticated LSA flooding and ECMP (Equal-Cost Multi-Path).
• BGP-4 (Border Gateway Protocol - RFC 4271)
Inter-AS Path Vector protocol glueing the global Internet together. Operates over reliable TCP port 179. Advertises AS-PATH attributes to prevent loops and enforces policy-based business routing between Autonomous Systems (eBGP and iBGP).
Protocol Matrix
→ RIP: DV, Hop count (Max 15), UDP 520
→ OSPF: LS, Dijkstra, IP 89, Areas
→ BGP: Path Vector, AS-PATH, TCP 179
→ Intra-AS: RIP, OSPF
→ Inter-AS: BGP-4
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 78
🎯 Exam Booster & Review: Unicast Routing Protocols
M2.2.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain Dijkstra's shortest path algorithm with a step-by-step table derivation for a 5-node network graph. (9 Marks)
Q: What is the Count-to-Infinity problem in Distance Vector routing? Explain how Split Horizon and Poisoned Reverse mitigate it. (8 Marks)
Q: Compare RIP, OSPF, and BGP-4 with respect to routing algorithm, metric, transport protocol, and scalability. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Dijkstra computes shortest path trees using complete topological knowledge.
✔ Distance vector iterates Bellman-Ford equations among adjacent neighbors.
✔ OSPF structures networks into areas with Area 0 backbone to scale within large enterprises.
✔ BGP-4 implements policy routing and loop prevention across Autonomous Systems using AS-PATH.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 79
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.4
Multicast Routing Protocols & IGMP
Multicast Addressing (Class D), IGMP Host-Router Membership, Source-Based Trees vs Group-Shared Trees, RPF, PIM-DM vs PIM-SM
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 80
2.2.4.1 Multicast Fundamentals & IGMP Protocol
M2.2.4 MULTICAST BASICS
• Multicast Concept
Delivering a single stream of datagrams from one or more sources to a specific group of interested receivers simultaneously without duplicate packet transmission on shared links.
• Multicast Addressing
IPv4 Class D range `224.0.0.0` to `239.255.255.255`. Special groups: `224.0.0.1` (All systems on subnet), `224.0.0.2` (All routers).
• IGMP (Internet Group Management Protocol - RFC 3376)
Operates locally between end hosts and their attached first-hop multicast router. Hosts send IGMP Membership Reports; router sends periodic Membership Queries.
• Multicast Routing Trees
1. **Source-Based Tree (Shortest Path Tree)**: Builds a separate tree rooted at each sender source (used in DVMRP, PIM-DM). 2. **Group-Shared Tree (Core-Based Tree)**: All sources transmit to a shared Rendezvous Point (RP) / Core router (used in PIM-SM).
• Reverse Path Forwarding (RPF)
Loop-prevention rule: Router accepts a multicast packet only if it arrived on the interface that is the shortest path back to the sender source.
Key Mechanisms
→ Class D: 224.0.0.0/4
→ IGMP: Local group membership
→ Source Tree: Optimal delay per source
→ Shared Tree: Minimal router state
→ RPF: Prevents multicast loops
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 81
2.2.4.2 PIM Protocols: Dense Mode (PIM-DM) vs Sparse Mode (PIM-SM)
M2.2.4 PIM DENSE VS SPARSE
PIM Dense Mode (PIM-DM / Flood & Prune)
• Assumed Environment: Receivers densely populated across almost every subnet
• Tree Construction: Source-Based Shortest Path Trees
• Mechanics: 1. **Flood**: Broadcasts multicast traffic everywhere \n 2. **Prune**: Routers with no interested members send Prune messages back upstream \n 3. **Graft**: New receivers send Graft to re-attach
• Overhead: High periodic flooding overhead
PIM Sparse Mode (PIM-SM / Explicit Join)
• Assumed Environment: Receivers sparsely distributed across wide area WAN
• Tree Construction: Group-Shared Tree rooted at Rendezvous Point (RP)
• Mechanics: 1. Receivers send explicit `IGMP Join` -> Router sends `PIM Join` towards RP \n 2. Sources register with RP \n 3. Traffic flows down shared tree
• Overhead: Zero flooding; highly scalable for enterprise IPTV
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 82
🎯 Exam Booster & Review: Multicast Routing
M2.2.4
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the role of IGMP in managing multicast group memberships on local subnets. (6 Marks)
Q: Compare Source-Based Trees and Group-Shared Trees in multicast routing. (7 Marks)
Q: Explain the working of PIM-DM (Flood and Prune) versus PIM-SM (Rendezvous Point and Explicit Joins). (8 Marks)
💡 Critical Conceptual Takeaways
✔ IGMP connects local hosts to their edge multicast router.
✔ Source-based trees minimize latency per sender; Shared trees minimize router state.
✔ RPF algorithm discards packets that do not arrive on the shortest return path to the source.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 83
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.5
Next Generation IP: IPv6 Architecture
IPv6 128-Bit Addressing, 40-Byte Fixed Header, Extension Headers, IPv4 vs IPv6 Comparison, Transition Strategies (Dual Stack, Tunneling, NAT64)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 84
2.2.5.1 IPv6 Addressing & 40-Byte Fixed Header
M2.2.5 IPV6 ARCHITECTURE
• Motivation for IPv6
Exhaustion of the 32-bit IPv4 address space ($2^{32} \approx 4.3 \times 10^9$ addresses). IPv6 provides $2^{128} \approx 3.4 \times 10^{38}$ unique addresses.
• IPv6 Address Notation
8 groups of 4 hexadecimal digits separated by colons (e.g., `2001:0db8:85a3:0000:0000:8a2e:0370:7334`). Leading zeros omitted (`2001:db8:85a3::8a2e:370:7334`); `::` compresses consecutive zero blocks once.
• 40-Byte Fixed Header Format
Version (4b: 6) | Traffic Class (8b: QoS DSCP) | Flow Label (20b: identifies packet flow for non-default routing) \n Payload Length (16b: data + extension headers) | Next Header (8b: specifies upper layer or extension header) | Hop Limit (8b: decremented per hop, replaces TTL) \n Source IPv6 Address (128 bits / 16 bytes) \n Destination IPv6 Address (128 bits / 16 bytes).
• Key Structural Improvements
No header checksum (speeds up router processing), no in-network fragmentation (handled via Path MTU Discovery by end hosts), fixed 40-byte base size.
Header Breakdown
→ Fixed Header: Exactly 40 Bytes
→ Source IP: 128 bits (16 B)
→ Destination IP: 128 bits (16 B)
→ Hop Limit: Replaces TTL
→ Next Header: Chains extensions
→ Flow Label: 20-bit stream tagging
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 85
2.2.5.2 IPv4 vs IPv6 & Transition Strategies
M2.2.5 IPV4 VS IPV6
IPv4 vs IPv6 Header Comparison
• Address Size: IPv4: 32 bits (4 Bytes) vs IPv6: 128 bits (16 Bytes)
• Header Length: IPv4: Variable 20-60B (IHL field) vs IPv6: Fixed 40 Bytes
• Checksum: IPv4: 16-bit header checksum vs IPv6: Removed entirely
• Fragmentation: IPv4: Routers fragment packets vs IPv6: End systems only (PMTUD)
• Broadcast: IPv4: Broadcast supported vs IPv6: Replaced by Multicast & Anycast
IPv4 to IPv6 Migration Mechanisms
• Dual Stack: Nodes run both IPv4 and IPv6 protocol stacks simultaneously on all interfaces
• Tunneling (6to4 / Teredo): IPv6 datagrams encapsulated as payload inside IPv4 packets across legacy IPv4 transit networks
• Header Translation (NAT64/DNS64): Translates IPv6 packet headers directly to IPv4 headers for legacy server interoperation
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 86
🎯 Exam Booster & Review: IPv6 Architecture
M2.2.5
📚 KTU High-Yield Questions (K2 Understand)
Q: Draw the IPv6 fixed header format and explain all fields. How does it improve router forwarding performance over IPv4? (8 Marks)
Q: Compare IPv4 and IPv6 across addressing, header structure, fragmentation, and error checking. (8 Marks)
Q: Explain the three transition mechanisms from IPv4 to IPv6: Dual Stack, Tunneling, and NAT64. (7 Marks)
💡 Critical Conceptual Takeaways
✔ IPv6 fixed 40-byte header streamlines hardware ASIC forwarding.
✔ Extension headers (Hop-by-Hop, Routing, Fragment, ESP, AH) are daisy-chained via `Next Header`.
✔ Dual stack and encapsulation tunneling enable smooth evolutionary migration from IPv4.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 87
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.2.6
Quality of Service (QoS) & Traffic Shaping
QoS Metrics (Delay, Jitter, Loss), Traffic Policing vs Shaping, Leaky Bucket vs Token Bucket, Scheduling (FIFO, WFQ), DiffServ vs IntServ
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 88
2.2.6.1 Traffic Shaping: Leaky Bucket vs Token Bucket
M2.2.6 TRAFFIC SHAPING
Leaky Bucket Algorithm (Constant Output)
• Concept: A bucket with a hole at the bottom; incoming packets buffer up to bucket capacity $C$ and leak out at a strictly constant rate $\rho$
• Output Profile: Strictly constant, smooth output stream regardless of incoming burstiness
• Burst Handling: Eliminates bursts entirely; discards packets if bucket overflows
• Suitability: Constant Bit Rate (CBR) traffic like uncompressed voice
Token Bucket Algorithm (Burst-Tolerant)
• Concept: Tokens generate at rate $r$ tokens/sec up to max token capacity $b$. A packet of size $m$ bytes consumes $m$ tokens to transmit
• Output Profile: Allows short-term traffic bursts up to bucket size $b$ while enforcing average long-term rate $r$
• Burst Handling: Max burst transmission speed = link wire rate $R$ for duration $T = b / (R - r)$
• Suitability: Variable Bit Rate (VBR) video streaming and web traffic
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 89
2.2.6.2 Worked KTU Numerical: Token Bucket Burst Calculation
M2.2.6 TOKEN BUCKET NUMERICAL
📌 KTU Numerical Problem Statement
A token bucket has token arrival rate r = 2 MB/sec and token bucket capacity b = 16 MB. The transmission link wire rate is R = 10 MB/sec. Calculate: (a) Maximum burst duration at wire rate R, (b) Maximum total data transmitted during this burst period.
📐 Governing Formulas & Principles:
• Burst duration formula: T = b / (R - r)
• Where b = bucket size (MB), R = peak transmission rate (MB/s), r = token replenishment rate (MB/s).
• Total data transmitted during burst: D = R * T = (b * R) / (R - r).
📝 Step-by-Step Derivation & Solution
Step 1: b = 16 MB, R = 10 MB/s, r = 2 MB/s
Step 2: T = 16 / (10 - 2) = 16 / 8 = 2.0 seconds
Step 3: Total data transmitted = R * T = 10 MB/s * 2.0 s = 20 MB
Step 4: Verification: Initial tokens (16 MB) + Newly generated tokens in 2s (2 MB/s * 2s = 4 MB) = 20 MB.
✅ FINAL ANSWER: Max Burst Duration T = 2.0 seconds | Total Burst Data = 20 MB
💡 Exam Tip: After 2 seconds, the transmission rate drops strictly to the average token rate r = 2 MB/sec.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 90
🎯 Exam Booster & Review: Quality of Service (QoS)
M2.2.6
📚 KTU High-Yield Questions (K3 Apply)
Q: Differentiate between Traffic Policing and Traffic Shaping with neat diagrams. (6 Marks)
Q: Compare Leaky Bucket and Token Bucket traffic shaping algorithms with equations and operating principles. (8 Marks)
Q: Explain Differentiated Services (DiffServ) architecture: Packet Classification, DSCP marking, and Per-Hop Behaviors (EF & AF). (7 Marks)
💡 Critical Conceptual Takeaways
✔ Leaky bucket produces rigid constant output; Token bucket permits regulated bursts.
✔ Weighted Fair Queuing (WFQ) guarantees minimum bandwidth shares to different service classes.
✔ DiffServ scales across WANs by classifying packets at boundary routers and using 6-bit DSCP markings.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 91
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 2 • M2.3
Linux Kernel TCP/IP Stack & Routing Implementation
Linux Network Packet Flow, sk_buff Data Structure, net_device, Forwarding Information Base (FIB), Route Cache, Linux iproute2
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 92
2.3.1 Linux Kernel Network Subsystem Architecture
M2.3 LINUX KERNEL STACK
• The `sk_buff` (Socket Buffer) Structure
The universal data structure representing network packets in Linux. Contains pointers: `head`, `data`, `tail`, `end`. Allows zero-copy header prepending/stripping across layers simply by moving the `data` pointer.
• Packet Ingress Flow (RX)
NIC receives frame -> DMA transfer to Ring Buffer -> Triggers Hard IRQ -> NAPI poll scheduled (SoftIRQ `NET_RX_SOFTIRQ`) -> `netif_receive_skb()` -> L3 `ip_rcv()` -> L4 `tcp_v4_rcv()` -> Socket receive queue -> `read()`.
• Packet Egress Flow (TX)
App calls `write()` -> L4 `tcp_sendmsg()` creates `sk_buff` -> L3 `ip_queue_xmit()` routes packet -> L2 `dev_queue_xmit()` enqueues to `qdisc` -> NIC DMA transmit -> Hardware TX IRQ.
• Forwarding Information Base (FIB)
The core kernel routing table in Linux organized as a fast LC-trie (Level-Compressed Trie) supporting sub-microsecond Longest Prefix Matching.
• Policy-Based Routing (PBR)
Linux supports multiple routing tables selected via `ip rule` based on source IP, TOS, fwmark, or incoming interface.
Kernel Data Structures
→ sk_buff: Packet descriptor
→ net_device: Hardware NIC abstraction
→ FIB: Kernel routing table trie
→ qdisc: Traffic queuing discipline
→ NAPI: Interrupt mitigation polling
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 93
2.3.2 Hands-On: Linux Kernel Routing with `iproute2`
M2.3 LINUX IPROUTE2
// Linux Socket & Protocol Implementation
# Linux iproute2 Advanced Routing Commands # 1. Inspect kernel routing table ip route show # 2. Add static route via gateway ip route add 192.168.10.0/24 via 10.0.0.1 dev eth0 # 3. Create Policy-Based Routing (PBR) table echo "200 custom_table" >> /etc/iproute2/rt_tables ip rule add from 192.168.1.50 table custom_table ip route add default via 10.0.0.254 dev eth1 table custom_table # 4. Flush and inspect route cache ip route flush cache
⚙️ System Call & Execution Workflow
• `ip route` Suite: Replaces deprecated `route` and `ifconfig` tools with direct Netlink socket communication to kernel.
• Custom Routing Tables: Linux supports up to 255 independent routing tables for multi-homing and ISP failover.
• `ip rule` Subsystem: Evaluates routing policy database (RPDB) rules sequentially to select appropriate routing table.
• Route Cache Behavior: Historical kernels maintained route hash cache; modern kernels use ultra-fast lockless FIB trie lookups.
💡 Hands-on Insight: Kernel `sk_buff` zero-copy architecture allows Linux to process millions of packets per second per CPU core.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 94
🎯 Exam Booster & Review: Linux Kernel Routing Stack
M2.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the architecture and role of the `sk_buff` data structure in Linux packet processing. (7 Marks)
Q: Trace the step-by-step path of an incoming packet from physical NIC reception to application socket delivery in the Linux kernel. (8 Marks)
Q: Demonstrate Policy-Based Routing (PBR) in Linux using `ip rule` and `ip route` commands. (6 Marks)
💡 Critical Conceptual Takeaways
✔ `sk_buff` avoids costly memory copies across protocol layers using internal buffer pointers.
✔ NAPI SoftIRQs prevent interrupt livelock during heavy packet bursts.
✔ FIB LC-trie enables sub-microsecond Longest Prefix Matching across hundreds of thousands of BGP routes.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 95
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 MASTER • MODULE 3 MASTER DECK
Data Link Layer, MAC Protocols & Wireless LANs
Complete Lecture Slides for KTU PCCST501 Computer Networks | Topics M3.1 through M3.9
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 96
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.1
Data Link Layer Design & Framing Techniques
Node-to-Node Link Services, Character Count, Byte Stuffing (Flag/ESC), Bit Stuffing (HDLC), Physical Coding Violations
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 97
3.1.1 Data Link Layer Design & Link Abstraction
M3.1 FRAMING BASICS
• Node-to-Node Service Mission
Responsible for transferring datagrams from one node (host, router, switch) to an adjacent node over an individual physical communication link.
• Link Layer Responsibilities
1. **Framing**: Encapsulating L3 datagrams into L2 frames with header and trailer. 2. **Link Access**: MAC protocols coordinate shared medium access. 3. **Reliable Delivery**: Flow control and ARQ on error-prone wireless links. 4. **Error Detection & Correction**: Parity, Checksum, CRC, Hamming codes.
• Framing Methods Overview
1. Character Count, 2. Byte Stuffing (Character-oriented), 3. Bit Stuffing (Bit-oriented), 4. Physical Layer Coding Violations (e.g., Manchester invalid transitions).
Framing Taxonomy
→ Byte Count: Header count field
→ Byte Stuffing: Flag + ESC bytes
→ Bit Stuffing: 5 consecutive 1s rule
→ Physical Violations: Line coding
→ FCS: CRC trailer at end
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 98
3.1.2 Stuffing Techniques: Byte Stuffing vs Bit Stuffing
M3.1 STUFFING COMPARISON
Byte Stuffing (Character-Oriented Framing)
• Delimiter: Frame begins and ends with dedicated Flag Byte `FLAG` (e.g., `0x7E` in PPP)
• Escape Mechanism: If `FLAG` occurs inside payload data, sender inserts an Escape Byte `ESC` (`0x7D`) immediately before it
• ESC in Data: If `ESC` itself appears in data, sender escapes it with another `ESC` (`ESC ESC`)
• Receiver Action: Receiver strips any `ESC` byte and treats following byte as raw data
Bit Stuffing (Bit-Oriented Framing / HDLC)
• Delimiter Pattern: Frame delimited by 8-bit flag pattern `01111110` (`0x7E`) at start and end
• Sender Rule: Whenever sender encounters **5 consecutive 1s** in data stream (`11111`), it automatically stuffs a **`0` bit** immediately after it
• Receiver Rule: Whenever receiver detects 5 consecutive 1s: if 6th bit is `0`, it de-stuffs (discards) the `0`; if 6th bit is `1` and 7th is `0`, it recognizes `FLAG`
• Advantage: Completely arbitrary payload length; zero character-set dependency
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 99
🎯 Exam Booster & Review: Data Link Layer Framing
M3.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the four framing methods used in the Data Link Layer with neat diagrams. (8 Marks)
Q: Given the data bit stream `01101111110111110010`, show the transmitted bit sequence after bit stuffing in HDLC. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Bit stuffing inserts a 0 after five consecutive 1s to prevent false flag detection.
✔ Byte stuffing uses escape characters (`ESC`) to preserve transparency in character protocols.
✔ Framing enables receivers to reliably locate the start and end of frames in raw bit streams.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 100
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.2
Data Link Control: Error Detection, Correction & Flow Control
Hamming Distance, 2D Parity, Internet Checksum, CRC-32 Modulo-2 Division, Hamming (7,4) Code, Stop-and-Wait, Go-Back-N, Selective Repeat
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 101
3.2.1 Block Coding & Hamming Distance Theory
M3.2 ERROR CONTROL THEORY
• Block Coding Principles
Dataword of $k$ bits encoded into Codeword of $n$ bits ($n > k$) by appending $r = n - k$ redundant parity bits.
• Hamming Distance $d(x,y)$
The number of bit positions in which two codewords $x$ and $y$ differ (computed by taking XOR and counting number of 1s).
• Minimum Hamming Distance ($d_{min}$)
The smallest Hamming distance between any pair of valid codewords in the codebook.
• Error Detection Capability
To detect up to $s$ bit errors: $d_{min} \ge s + 1$ (e.g., Simple Parity has $d_{min} = 2$, detects single-bit errors $s = 1$).
• Error Correction Capability
To correct up to $t$ bit errors: $d_{min} \ge 2t + 1$ (e.g., Single-bit error correction $t = 1$ requires $d_{min} \ge 3$).
Hamming Distance Rules
→ Detect s errors: d_min >= s + 1
→ Correct t errors: d_min >= 2t + 1
→ Simple Parity: d_min = 2
→ Hamming (7,4): d_min = 3
→ r parity bits: 2^r >= k + r + 1
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 102
3.2.2 Worked KTU Numerical: CRC Modulo-2 Polynomial Division
M3.2 CRC WORKED PROBLEM
📌 KTU Numerical Problem Statement
A data bit stream D = 10100100 is to be transmitted using CRC generator polynomial G(x) = x^4 + x^2 + 1 (binary generator G = 10101). (a) Determine the 4-bit CRC Checksum (Frame Check Sequence FCS), (b) What codeword is transmitted? (c) Show that receiver detects zero remainder in the absence of bit errors.
📐 Governing Formulas & Principles:
• Generator G(x) = x^4 + x^2 + 1 -> Degree r = 4 -> Generator bit string G = 10101 (5 bits).
• Step 1: Append r = 4 zeros to data D: D' = 10100100 0000 (12 bits).
• Step 2: Perform Modulo-2 binary division (XOR operations) of D' by G.
• Step 3: Remainder of division is the 4-bit CRC Checksum R.
📝 Step-by-Step Derivation & Solution
Step 1: Dividend: 101001000000 | Divisor: 10101
Step 2: 10100 XOR 10101 -> Remainder 00001; bring down bits -> 0001100...
Step 3: Continuing Modulo-2 XOR division yields 4-bit Remainder R = 1100.
Step 4: Transmitted Codeword T = Data + CRC = 10100100 1100 (12 bits).
Step 5: Receiver Divides T (101001001100) by G (10101) -> Remainder = 0000 (Valid / No errors!).
✅ FINAL ANSWER: CRC Checksum = 1100 | Transmitted Codeword = 101001001100
💡 Exam Tip: Modulo-2 addition and subtraction are both identical to bitwise XOR with zero carries/borrows.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 103
3.2.3 Worked KTU Numerical: Hamming (7,4) Single-Bit Error Correction
M3.2 HAMMING CODE WORKED
📌 KTU Numerical Problem Statement
A 4-bit dataword D = 1011 (d4=1, d3=0, d2=1, d1=1) is encoded using Hamming (7,4) code with parity bits at positions 1, 2, 4. (a) Generate 7-bit codeword. (b) If received word is R = 1011011, calculate syndrome bits (s3, s2, s1) and locate the erroneous bit position.
📐 Governing Formulas & Principles:
• Bit positions 1 to 7: p1 (pos 1), p2 (pos 2), d1 (pos 3), p4 (pos 4), d2 (pos 5), d3 (pos 6), d4 (pos 7).
• p1 checks positions with bit 1 set (1, 3, 5, 7): p1 = d1 XOR d2 XOR d4.
• p2 checks positions with bit 2 set (2, 3, 6, 7): p2 = d1 XOR d3 XOR d4.
• p4 checks positions with bit 4 set (4, 5, 6, 7): p4 = d2 XOR d3 XOR d4.
• Syndrome S = (s4 s2 s1) indicates decimal error bit position (0 = no error).
📝 Step-by-Step Derivation & Solution
Step 1: p1 = 1 XOR 1 XOR 1 = 1 | p2 = 1 XOR 0 XOR 1 = 0 | p4 = 1 XOR 0 XOR 1 = 0
Step 2: Generated Codeword: (p1, p2, d1, p4, d2, d3, d4) = (1, 0, 1, 0, 1, 0, 1) -> 1010101
Step 3: Received Word R = (r1..r7) = (1, 1, 0, 1, 1, 0, 1) (bit 2 corrupted!)
Step 4: s1 = r1 XOR r3 XOR r5 XOR r7 = 1 XOR 0 XOR 1 XOR 1 = 1
Step 5: s2 = r2 XOR r3 XOR r6 XOR r7 = 1 XOR 0 XOR 0 XOR 1 = 0
Step 6: s4 = r4 XOR r5 XOR r6 XOR r7 = 1 XOR 1 XOR 0 XOR 1 = 1 -> Syndrome = 101_2 = Pos 5 (d2 corrupted!)
✅ FINAL ANSWER: Syndrome S = 101 (Binary 5) -> Bit position 5 is inverted and corrected!
💡 Exam Tip: Hamming (7,4) code can correct any single-bit error and detect any double-bit error.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 104
3.2.4 Sliding Window Flow Control: Stop-and-Wait vs GBN vs Selective Repeat
M3.2 ARQ PROTOCOLS
Stop-and-Wait ARQ
• Window Size: $W_s = 1$, $W_r = 1$
• Sequence Bits: 1-bit ($m=1$, sequence numbers 0 and 1)
• Efficiency: Extremely low on high-bandwidth-delay product links: $\eta = 1 / (1 + 2a)$ where $a = t_{prop} / t_{trans}$
• Buffering: 1 frame buffer at sender and receiver
Go-Back-N (GBN) ARQ
• Window Size: $W_s = 2^m - 1$, $W_r = 1$ (Cumulative ACKs)
• On Loss: Discards all subsequent out-of-order frames; retransmits entire window from lost frame
• Sender Buffer: Buffers $W_s$ frames; receiver requires zero buffer
• Efficiency: High efficiency unless error rate is severe
Selective Repeat (SR) ARQ
• Window Size: $W_s = 2^{m-1}$, $W_r = 2^{m-1}$ (Individual ACKs)
• On Loss: Receiver buffers out-of-order frames; sender retransmits **only the lost frame**
• Buffer Needs: Both sender and receiver maintain $2^{m-1}$ buffer queues
• Efficiency: Optimal bandwidth utilization on noisy channels
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 105
🎯 Exam Booster & Review: Error Detection & Flow Control
M3.2
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain CRC error detection with a polynomial division example. Why is CRC implemented in hardware with LFSR shift registers? (8 Marks)
Q: Derive the maximum sender window size for Go-Back-N ($2^m - 1$) and Selective Repeat ($2^{m-1}$). Explain why exceeding these limits causes protocol failure. (8 Marks)
Q: Explain Hamming (7,4) code with syndrome error correction calculation. (7 Marks)
💡 Critical Conceptual Takeaways
✔ CRC detects all single-bit, double-bit, odd numbers of errors, and burst errors up to generator polynomial degree $r$.
✔ Go-Back-N window is $2^m - 1$ to prevent receiver from mistaking duplicate frames for new ones.
✔ Selective Repeat requires equal sender and receiver window sizes bounded at $2^{m-1}$.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 106
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.3
Multiple Access Control (MAC) Protocols
Random Access (Pure & Slotted ALOHA, CSMA, CSMA/CD, CSMA/CA), Controlled Access (Polling, Token Ring), Channelization (CDMA)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 107
3.3.1 Random Access: Pure ALOHA vs Slotted ALOHA
M3.3 ALOHA COMPARISON
Pure ALOHA (Norman Abramson, 1970)
• Transmission Rule: Transmit continuous frame whenever data is ready without sensing channel
• Vulnerable Period: $V_p = 2 \times T_{frame}$ (Collision occurs if any other node transmits within 2 frame times)
• Throughput Formula: $S = G \cdot e^{-2G}$ where $G$ = traffic load
• Maximum Efficiency: Maximum throughput $S_{max} = 1 / (2e) \approx 18.4\%$ at $G = 0.5$
• Collisions: High collision rate due to uncoordinated overlapping frames
Slotted ALOHA (Roberts, 1972)
• Transmission Rule: Time divided into discrete slots equal to $T_{frame}$. Nodes transmit strictly at slot boundaries
• Vulnerable Period: $V_p = 1 \times T_{frame}$ (Halves vulnerability interval)
• Throughput Formula: $S = G \cdot e^{-G}$
• Maximum Efficiency: Maximum throughput $S_{max} = 1 / e \approx 36.8\%$ at $G = 1.0$ (Exactly doubles Pure ALOHA!)
• Synchronization: Requires global slot synchronization across all nodes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 108
3.3.2 CSMA/CD: Carrier Sense Multiple Access with Collision Detection
M3.3 CSMA/CD PROTOCOL
• Carrier Sense (Listen Before Talk)
Node listens to channel before transmitting. 1-persistent: transmits immediately when idle; Non-persistent: waits random backoff if busy; p-persistent: transmits with probability $p$ when idle.
• Collision Detection (Listen While Talk)
Node continuously monitors voltage/energy on wire while transmitting. If signal amplitude exceeds collision threshold, collision is detected immediately!
• Jam Signal & Abort
Upon detecting collision, node aborts transmission immediately and broadcasts a 32-48 bit **Jam Signal** to ensure all other nodes detect the collision.
• Minimum Frame Size Constraint ($L_{min}$)
To ensure a sender does not finish transmitting before collision signal propagates back: $T_{frame} \ge 2 \times T_{prop} \implies \frac{L_{min}}{R} \ge 2 \cdot \frac{d}{s} \implies L_{min} = 2 \times T_{prop} \times R$.
• Binary Exponential Backoff (BEB)
After $k$-th collision ($k \le 10$), node picks random wait slot $r \in \{0, 1, 2, \dots, 2^k - 1\}$ and waits $r \times 512$ bit times. Aborts after 16 consecutive collisions.
CSMA/CD Summary
→ 1-persistent sense
→ Jam signal on collision
→ L_min = 2 * t_prop * R
→ Standard Ethernet L_min = 64 Bytes (512 bits)
→ Backoff range: [0, 2^k - 1]
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 109
3.3.3 Worked KTU Numerical: CSMA/CD Minimum Frame Size
M3.3 CSMA/CD NUMERICAL
📌 KTU Numerical Problem Statement
A 1 Gbps Ethernet LAN runs over a 1 km fiber link with propagation speed s = 2 * 10^8 m/s. Calculate the minimum frame size required for proper collision detection. If transmission rate is increased to 10 Gbps over the same link, what must the new minimum frame size be?
📐 Governing Formulas & Principles:
• L_min = 2 * t_prop * R
• t_prop = d / s = 1000 m / (2 * 10^8 m/s) = 5 * 10^-6 s = 5 microseconds.
• Round-trip propagation time 2 * t_prop = 10 microseconds = 10^-5 seconds.
• L_min = 2 * t_prop * R (bits).
📝 Step-by-Step Derivation & Solution
Step 1: For R = 1 Gbps = 10^9 bps:
Step 2: L_min = 10^-5 s * 10^9 bps = 10,000 bits = 10,000 / 8 = 1250 Bytes.
Step 3: For R = 10 Gbps = 10^10 bps:
Step 4: L_min = 10^-5 s * 10^10 bps = 100,000 bits = 12,500 Bytes (12.5 KB).
Step 5: Conclusion: At 10 Gbps, minimum frame size becomes unfeasibly large; hence 10 Gigabit Ethernet mandates full-duplex point-to-point links (disabling CSMA/CD entirely).
✅ FINAL ANSWER: 1 Gbps: L_min = 1250 Bytes | 10 Gbps: L_min = 12,500 Bytes
💡 Exam Tip: CSMA/CD is only applicable on half-duplex shared media; full-duplex switched Ethernet does not require CSMA/CD.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 110
🎯 Exam Booster & Review: Multiple Access Protocols
M3.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Derive the maximum channel throughput for Pure ALOHA ($18.4\%$) and Slotted ALOHA ($36.8\%$) with vulnerable period diagrams. (8 Marks)
Q: Explain the working of CSMA/CD with the Binary Exponential Backoff (BEB) algorithm and minimum frame size derivation. (8 Marks)
Q: Explain Code Division Multiple Access (CDMA) using orthogonal Walsh chip sequences with an encoding and decoding example. (7 Marks)
💡 Critical Conceptual Takeaways
✔ Slotted ALOHA doubles Pure ALOHA efficiency by eliminating partial frame collisions.
✔ Minimum frame size in CSMA/CD guarantees collision detection before transmission ends ($L_{min} = 2 \cdot t_{prop} \cdot R$).
✔ CDMA allows simultaneous transmission over the same frequency band using orthogonal chip codes.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 111
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.4
Link-Layer Addressing & Address Resolution Protocol (ARP)
48-Bit MAC Addresses (EUI-48), ARP Request (Broadcast) & ARP Reply (Unicast), ARP Cache & Timeout, Proxy ARP, Subnet Crossing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 112
3.4.1 MAC Addressing & Address Resolution Protocol (ARP)
M3.4 ARP PROTOCOL
• MAC Hardware Address (48 bits / 6 Bytes)
Burned into NIC ROM (e.g., `1A:2B:3C:4D:5E:6F`). First 24 bits = OUI (Organizationally Unique Identifier assigned by IEEE); Last 24 bits = Vendor NIC serial number.
• ARP Mission (RFC 826)
Dynamically resolves a known 32-bit IP address into its corresponding 48-bit MAC address on the local physical subnet.
• ARP Message Flow
1. **ARP Request**: Host broadcasts frame (`FF:FF:FF:FF:FF:FF`) asking: 'Who owns IP 192.168.1.5? Send your MAC to 192.168.1.2'. \n 2. **ARP Reply**: Target host unicasts reply containing its physical MAC address directly to the sender. \n 3. **ARP Table**: Sender caches the mapping in its local ARP Cache table with a TTL timer (typically 20 minutes).
• Proxy ARP & Gratuitous ARP
**Proxy ARP**: Router responds to ARP request on behalf of a remote node. **Gratuitous ARP**: Host announces its own IP/MAC to detect duplicate IP conflicts and update switch MAC tables.
ARP Key Facts
→ ARP Request: L2 Broadcast (FF:..:FF)
→ ARP Reply: L2 Unicast
→ L2 Frame Type: 0x0806 (ARP)
→ ARP Cache: Dynamic IP->MAC table
→ Gratuitous ARP: IP conflict check
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 113
3.4.2 Packet Forwarding Across Subnets (MAC & IP Rewriting)
M3.4 SUBNET ROUTING
• Scenario: Host A (Subnet 1) sends packet to Host B (Subnet 2) via Router R
Source Host A creates L3 IP packet: `Src IP = IP_A`, `Dst IP = IP_B` (IP addresses remain constant throughout end-to-end path).
• Hop 1 (Host A -> Router R)
Host A inspects routing table; determines destination `IP_B` is outside local subnet. Encapsulates IP packet into L2 frame: `Src MAC = MAC_A`, `Dst MAC = MAC_Router_Interface_1` (uses ARP to find router MAC).
• Router R Processing
Router decapsulates L2 frame, inspects L3 `Dst IP = IP_B`, consults FIB routing table, decrements TTL, recomputes IP checksum, and determines outgoing Interface 2.
• Hop 2 (Router R -> Host B)
Router encapsulates packet into a fresh L2 frame: `Src MAC = MAC_Router_Interface_2`, `Dst MAC = MAC_B` (via ARP on Subnet 2).
• Core Takeaway
**IP addresses remain unchanged end-to-end; MAC addresses change at every single router hop!**
Hop-by-Hop Headers
→ Hop 1: Src MAC_A -> Dst MAC_R1
→ Hop 2: Src MAC_R2 -> Dst MAC_B
→ End-to-End: Src IP_A -> Dst IP_B
→ L2 MAC rewritten per hop
→ L3 IP preserved end-to-end
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 114
🎯 Exam Booster & Review: MAC Addressing & ARP
M3.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the operation of Address Resolution Protocol (ARP) with request and reply frame structures. (7 Marks)
Q: Trace the step-by-step changes in Source/Destination IP and Source/Destination MAC addresses as a packet travels from Host A to Host B across an intermediate router. (8 Marks)
💡 Critical Conceptual Takeaways
✔ ARP bridges Layer 3 IP addresses to Layer 2 physical MAC addresses.
✔ ARP requests are L2 broadcasts (`FF:FF:FF:FF:FF:FF`); ARP replies are L2 unicasts.
✔ L3 IP addresses identify end hosts; L2 MAC addresses identify next-hop network interfaces.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 115
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.5
Ethernet Protocols & IEEE 802.3 Architecture
Standard Ethernet (10M), Fast Ethernet (100M), Gigabit Ethernet (1G), 10GbE, IEEE 802.3 Frame Format (64B to 1518B)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 116
3.5.1 IEEE 802.3 Ethernet Frame Format
M3.5 ETHERNET FRAME
• Preamble (7 Bytes)
7 bytes of alternating `10101010` patterns used to synchronize receiver clock circuitry.
• Start of Frame Delimiter - SFD (1 Byte)
1 byte pattern `10101011` indicating that destination MAC address begins immediately on the next bit.
• Destination MAC Address (6 Bytes)
48-bit hardware address of target NIC (or broadcast `FF:FF:FF:FF:FF:FF`).
• Source MAC Address (6 Bytes)
48-bit hardware address of sending NIC.
• Type / Length Field (2 Bytes)
If $\ge 1536$ (0x0600), specifies upper layer protocol (EtherType: IPv4 `0x0800`, ARP `0x0806`, IPv6 `0x86DD`). If $\le 1500$, specifies frame payload length.
• Payload / Data (46 to 1500 Bytes)
Carries L3 datagram. Minimum payload is 46 bytes (padded with zeros if smaller) to enforce the 64-byte minimum frame size constraint.
• Frame Check Sequence - FCS (4 Bytes)
32-bit Cyclic Redundancy Check (CRC-32) computed over Dst MAC, Src MAC, Type, and Payload.
Frame Sizes
→ Preamble + SFD: 8 Bytes
→ Header + FCS: 18 Bytes
→ Min Payload: 46 Bytes
→ Max Payload (MTU): 1500 Bytes
→ Min Frame Size: 64 Bytes
→ Max Frame Size: 1518 Bytes
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 117
3.5.2 Ethernet Speed Evolution: Standard to 10GbE
M3.5 ETHERNET EVOLUTION
Standard & Fast Ethernet
• Standard (10 Mbps): 10Base5 (Thicknet coaxial), 10Base2 (Thinnet), 10Base-T (UTP Cat 3/5 with Hub/Switch). Uses Manchester line coding
• Fast Ethernet (100 Mbps): 100Base-TX (Cat 5 UTP using 4B/5B and MLT-3 coding), 100Base-FX (Fiber). Introduces Auto-Negotiation
Gigabit & 10G Ethernet
• Gigabit Ethernet (1 Gbps): 1000Base-T (Cat 5e/6 UTP using 4 pairs full-duplex with 8B/10B coding), 1000Base-SX/LX (Fiber). Introduces Carrier Extension and Packet Bursting for half-duplex
• 10 Gigabit Ethernet (10 Gbps): 10GBase-T (Cat 6a/7) and 10GBase-SR/LR. Exclusively full-duplex switched connections; eliminates CSMA/CD completely
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 118
🎯 Exam Booster & Review: IEEE 802.3 Ethernet
M3.5
📚 KTU High-Yield Questions (K2 Understand)
Q: Draw the IEEE 802.3 Ethernet frame format and explain the function of each field. Why is the minimum frame size 64 bytes and maximum 1518 bytes? (8 Marks)
Q: Compare Standard Ethernet, Fast Ethernet, Gigabit Ethernet, and 10 Gigabit Ethernet with respect to medium, coding, and transmission modes. (7 Marks)
💡 Critical Conceptual Takeaways
✔ Preamble and SFD synchronize bit timing; FCS trailer provides CRC-32 error detection.
✔ 64-byte minimum frame ensures collision detection in 10/100 Mbps CSMA/CD networks.
✔ 10GbE operates strictly in full-duplex mode over switches and fiber links.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 119
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.5V
Virtual Local Area Networks (VLANs - IEEE 802.1Q)
Broadcast Containment, Port-Based vs Tagged VLANs, IEEE 802.1Q 4-Byte Tag (VID 1-4094), Access vs Trunk Ports, Router-on-a-Stick
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 120
3.5V.1 VLAN Motivation & IEEE 802.1Q Tagged Framing
M3.5V VLAN ARCHITECTURE
• VLAN Motivation
Physically co-located hosts can be partitioned into logical broadcast domains regardless of physical switch topology. Prevents broadcast storms, enhances security, and organizes departments logically (e.g., Faculty VLAN, Student VLAN, Lab VLAN).
• Port-Based VLAN (Untagged)
Switch ports assigned static VLAN IDs. Traffic inside switch segregated by port group; frames on access links remain standard untagged Ethernet frames.
• IEEE 802.1Q Tagged Frame (4 Bytes Inserted after Source MAC)
1. **TPID (Tag Protocol Identifier - 16 bits)**: Set to `0x8100` (identifies frame as 802.1Q tagged). \n 2. **PCP (Priority Code Point - 3 bits)**: IEEE 802.1p Quality of Service priority (0 to 7). \n 3. **DEI (Drop Eligible Indicator - 1 bit)**: Set to 1 if frame can be dropped during congestion. \n 4. **VID (VLAN Identifier - 12 bits)**: Uniquely identifies VLAN number (1 to 4094; 0 and 4095 reserved).
• Access Port vs Trunk Port
**Access Port**: Connects end hosts; carries traffic for 1 untagged VLAN only. **Trunk Port**: Interconnects switches/routers; carries multiplexed tagged traffic for multiple VLANs simultaneously.
IEEE 802.1Q Tag
→ TPID: 0x8100 (16 bits)
→ PCP: 3 bits (QoS Priority)
→ DEI: 1 bit (Drop eligibility)
→ VID: 12 bits (4094 VLANs)
→ Trunking: Carries tagged frames
→ Access: Carries untagged frames
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 121
3.5V.2 Inter-VLAN Routing: Router-on-a-Stick vs Layer 3 Switch
M3.5V INTER-VLAN ROUTING
• Why Inter-VLAN Routing?
By design, hosts on different VLANs cannot communicate at Layer 2 even if plugged into the same physical switch. Inter-VLAN routing requires Layer 3 packet forwarding.
• Router-on-a-Stick (Legacy Approach)
A single physical Ethernet interface on an external router is connected to a switch Trunk port. The router interface is divided into logical **Sub-interfaces** (e.g., `eth0.10`, `eth0.20`), each configured with the default gateway IP and 802.1Q encapsulation for its respective VLAN.
• Layer 3 Switch (Modern Core Routing)
Switches with built-in hardware ASIC routing capabilities. Configured with **Switched Virtual Interfaces (SVIs)** (`interface vlan 10`, `interface vlan 20`) providing multi-gigabit wire-speed inter-VLAN routing without external router bottleneck.
Inter-VLAN Methods
→ Router-on-a-Stick: 1 Trunk link
→ Sub-interfaces: eth0.10, eth0.20
→ L3 Switch: Hardware SVI routing
→ Wire-speed routing in L3 switch
→ Isolates broadcast domains
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 122
🎯 Exam Booster & Review: Virtual LANs (VLANs)
M3.5V
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the benefits of VLANs and illustrate the 4-byte IEEE 802.1Q tag header format. (7 Marks)
Q: Differentiate between Access ports and Trunk ports on an Ethernet switch. (5 Marks)
Q: Explain Inter-VLAN routing using the Router-on-a-Stick architecture with a network diagram and configuration concepts. (7 Marks)
💡 Critical Conceptual Takeaways
✔ VLANs partition a single physical switch into multiple isolated broadcast domains.
✔ IEEE 802.1Q tag inserts 4 bytes (TPID 0x8100 + 12-bit VID for 4094 VLANs).
✔ Trunk links carry tagged multiplexed frames between switches and routers.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 123
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.6
Connecting Devices & Spanning Tree Protocol (STP)
Repeaters, Hubs (L1), Bridges & Layer 2 Switches (MAC Learning), Spanning Tree Protocol (IEEE 802.1D STP), Routers & Layer 3 Switches
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 124
3.6.1 Connecting Devices Taxonomy & Collision/Broadcast Domains
M3.6 CONNECTING DEVICES
Layer 1: Repeaters & Hubs
• Operating Layer: Physical Layer (L1)
• Function: Regenerates and amplifies electrical/optical signals; broadcasts incoming bits to all ports
• Collision Domains: Single shared collision domain across all ports
• Broadcast Domains: Single broadcast domain
• Intelligence: Zero intelligence / No buffering
Layer 2: Bridges & Switches
• Operating Layer: Data Link Layer (L2)
• Function: Inspects MAC addresses; filters and forwards frames selectively using hardware MAC Learning table
• Collision Domains: Microsegmentation: **Each individual port is an isolated collision domain**
• Broadcast Domains: Single broadcast domain (unless partitioned via VLANs)
• Buffering: Store-and-forward / Cut-through
Layer 3: Routers & L3 Switches
• Operating Layer: Network Layer (L3)
• Function: Routes packets across heterogeneous networks using IP addresses
• Collision Domains: Separate collision domain per port
• Broadcast Domains: **Separates broadcast domains** (does not forward L2 broadcasts)
• Routing Table: Maintains FIB routing table
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 125
3.6.2 Spanning Tree Protocol (IEEE 802.1D STP)
M3.6 SPANNING TREE PROTOCOL
• The Layer 2 Loop Problem
Redundant links between switches provide fault tolerance, but create disastrous **Broadcast Storms**, multiple frame copies, and MAC table instability.
• STP Goal
Logically disables redundant links by placing them in Blocking state, dynamically constructing a loop-free active tree topology while keeping backup paths on standby.
• BPDU (Bridge Protocol Data Units)
Switches exchange BPDUs containing: `Bridge ID = Priority (2B) + MAC Address (6B)` (Default priority = 32768).
• 4-Step STP Algorithm
1. **Root Bridge Election**: Switch with the lowest Bridge ID becomes the Root Bridge. \n 2. **Root Port (RP) Selection**: On each non-root switch, the port with the lowest path cost to the Root Bridge is selected as RP. \n 3. **Designated Port (DP) Selection**: On each LAN segment, the port with the lowest path cost to Root becomes DP. \n 4. **Blocking State**: All remaining ports are placed in Blocking/Discarding state to break loops.
STP Algorithm Steps
→ 1. Lowest Bridge ID -> Root Bridge
→ 2. Lowest Cost to Root -> Root Port (RP)
→ 3. Lowest Cost per Link -> Designated Port (DP)
→ 4. Remaining Ports -> Blocked / Alternate
→ Convergence time: ~30-50 seconds (RSTP: < 1s)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 126
🎯 Exam Booster & Review: Connecting Devices & STP
M3.6
📚 KTU High-Yield Questions (K3 Apply)
Q: Compare Repeaters, Hubs, Switches, and Routers with respect to operating layer, collision domains, and broadcast domains. (8 Marks)
Q: Explain the working of the Spanning Tree Protocol (IEEE 802.1D) with Bridge ID, Root Bridge election, Root Ports, and Blocking ports. (8 Marks)
💡 Critical Conceptual Takeaways
✔ Hubs extend collision domains; Switches isolate collision domains; Routers isolate broadcast domains.
✔ Transparent switches dynamically populate MAC tables by inspecting source MACs of arriving frames.
✔ STP prevents broadcast storms by breaking physical switching loops into a single logical tree.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 127
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.7
Wireless LANs: IEEE 802.11 (Wi-Fi) Architecture
BSS, AP, ESS, Distribution System, Hidden/Exposed Terminal Problems, CSMA/CA with RTS/CTS, SIFS/PIFS/DIFS, 802.11 Frame (4 Addresses)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 128
3.7.1 IEEE 802.11 Architecture & Terminal Problems
M3.7 WIRELESS ARCHITECTURE
• Basic Service Set (BSS)
The fundamental building block consisting of wireless stations and a central Access Point (AP) in Infrastructure mode (or peer-to-peer in Ad-hoc / IBSS mode).
• Extended Service Set (ESS)
Multiple BSSs interconnected via a wired Distribution System (DS) sharing a common SSID, enabling seamless roaming across campus.
• Hidden Terminal Problem
Nodes A and C cannot hear each other due to distance or physical obstacles, but both are in range of AP B. If A and C transmit simultaneously, their frames collide at B!
• Exposed Terminal Problem
Node B is transmitting to A. Node C wants to transmit to D (away from A). C senses B transmitting and unnecessarily defers, wasting channel capacity.
• Solution: CSMA/CA with RTS/CTS Handshake
Sender transmits short **RTS (Request to Send)** frame (20B). AP replies with **CTS (Clear to Send)** broadcast (14B) containing Network Allocation Vector (NAV) reservation time, silencing hidden terminals.
802.11 Topology
→ BSS: AP + Associated Stations
→ ESS: Multiple BSSs + Wired DS
→ Hidden Terminal: Collisions at AP
→ RTS/CTS: Virtual carrier sensing
→ NAV: Channel reservation timer
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 129
3.7.2 CSMA/CA Protocol Timing Intervals & 4-Address Frame
M3.7 CSMA/CA TIMING
• Inter-Frame Space (IFS) Hierarchy
1. **SIFS (Short IFS)**: Highest priority; used for immediate ACKs, CTS, and fragmented frames. \n 2. **PIFS (PCF IFS)**: Medium priority; used in polling mode. \n 3. **DIFS (DCF IFS)**: Standard priority; minimum wait time before station can contend for channel.
• Contention Window (CW) & Backoff
Station waits DIFS; if idle, selects random backoff slot in $[0, CW]$. Counts down while channel is idle; freezes counter during busy periods.
• IEEE 802.11 4-Address Frame Format
Frame Control (2B) | Duration/ID (2B) | Address 1 (6B: Receiver MAC) | Address 2 (6B: Transmitter MAC) | Address 3 (6B: Original Source or Final Dest MAC) | Sequence Control (2B) | Address 4 (6B: Used strictly when bridging across WDS wireless distribution links) | Payload (0-2312B) | FCS (4B).
Timing Hierarchy
→ SIFS < PIFS < DIFS < EIFS
→ SIFS: ACKs & CTS (Highest priority)
→ DIFS: Standard data contention
→ Addr 1: Immediate Receiver
→ Addr 2: Immediate Transmitter
→ Addr 3: Original Source / Dest
→ Addr 4: WDS Wireless Bridge
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 130
🎯 Exam Booster & Review: IEEE 802.11 Wireless LANs
M3.7
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the Hidden Terminal and Exposed Terminal problems in Wireless LANs. How does CSMA/CA with RTS/CTS resolve them? (8 Marks)
Q: Explain the timing relationships between SIFS, PIFS, and DIFS in IEEE 802.11 CSMA/CA with a neat timing diagram. (7 Marks)
Q: Explain the four MAC address fields in the IEEE 802.11 frame format. When is Address 4 used? (6 Marks)
💡 Critical Conceptual Takeaways
✔ Wireless radios cannot detect collisions while transmitting; hence Wi-Fi uses collision avoidance (CSMA/CA).
✔ RTS and CTS frames carry NAV reservation timers to silence hidden nodes.
✔ Address 4 is populated only when frames are bridged between two wireless APs in WDS mode.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 131
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.8
Mobile IP Architecture & Protocols
Mobile Node (MN), Home Agent (HA), Foreign Agent (FA), Home Address (HoA), Care-of Address (CoA), Tunneling & Triangle Routing
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 132
3.8.1 Mobile IP Architecture & Entities (RFC 5944)
M3.8 MOBILE IP BASICS
• The Mobility Challenge
Standard IP routing uses destination IP prefixes. If a mobile laptop moves to a new subnet, changing its IP address terminates all active TCP connections! Mobile IP allows a host to retain its permanent IP transparently.
• Mobile IP Entities
1. **Mobile Node (MN)**: The roaming host. \n 2. **Home Network & Home Agent (HA)**: The home subnet and the router acting on behalf of MN when away. \n 3. **Foreign Network & Foreign Agent (FA)**: The visited subnet router assisting MN. \n 4. **Correspondent Node (CN)**: The peer host communicating with MN.
• Dual-Address Mechanism
1. **Home Address (HoA)**: Permanent IP address assigned in home subnet (used for active TCP sessions). \n 2. **Care-of Address (CoA)**: Temporary IP address associated with visited foreign network.
Core Entities
→ MN: Mobile Node
→ HA: Home Agent router
→ FA: Foreign Agent router
→ HoA: Permanent IP address
→ CoA: Temporary visited IP
→ CN: Correspondent Node
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 133
3.8.2 Operational Phases: Registration, Tunneling & Triangle Routing
M3.8 MOBILE IP PHASES
• Phase 1: Agent Discovery
Foreign Agents broadcast periodic Agent Advertisements (ICMP extension); MN detects it has moved and obtains a CoA.
• Phase 2: Registration
MN sends Registration Request to FA -> FA forwards to Home Agent (HA) -> HA updates binding table (`HoA -> CoA`) and sends Registration Reply.
• Phase 3: Data Transfer (IP-in-IP Encapsulation Tunneling)
CN sends packet to `HoA` -> Routed to Home Network -> Home Agent intercepts packet via Proxy ARP -> HA encapsulates packet inside a new IP header (`Src IP = HA`, `Dst IP = CoA`) -> Transmits through IP tunnel to FA -> FA decapsulates and delivers to MN.
• Reverse Path & Triangle Routing Problem
MN sends directly to CN via standard IP routing. However, traffic from CN travels through HA -> FA -> MN (inefficient Triangle Routing). Solution: Route Optimization allows CN to cache MN's CoA and tunnel directly.
Tunneling Flow
→ CN -> Home Agent (HoA)
→ HA intercepts (Proxy ARP)
→ HA tunnels to FA (IP-in-IP)
→ FA decapsulates -> MN
→ MN replies directly to CN
→ Triangle Routing fixed via CoA cache
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 134
🎯 Exam Booster & Review: Mobile IP Architecture
M3.8
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the architecture and entities of Mobile IP (MN, HA, FA, HoA, CoA) with a neat diagram. (8 Marks)
Q: Explain the three operational phases of Mobile IP: Agent Discovery, Registration, and Encapsulation Tunneling. (8 Marks)
Q: What is the Triangle Routing problem in Mobile IP, and how does Route Optimization solve it? (6 Marks)
💡 Critical Conceptual Takeaways
✔ Mobile IP preserves TCP connection survivability during subnet roaming.
✔ Home Agent intercepts packets using Proxy ARP and encapsulates them via IP-in-IP tunneling to the Care-of Address.
✔ Triangle routing introduces latency by routing all forward traffic through the Home Agent.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 135
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 3 • M3.9
Linux Network Programming: Raw Sockets & PF_PACKET
Data Link Provider Interface (DLPI), BSD Packet Filter (BPF), Linux PF_PACKET / AF_PACKET (SOCK_RAW, ETH_P_ALL), Promiscuous Sniffer
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 136
3.9.1 Hands-On: Packet Sniffing with Linux `PF_PACKET`
M3.9 LINUX RAW SOCKETS
// Linux Socket & Protocol Implementation
#include <sys/socket.h> #include <netinet/ether.h> #include <net/if.h> #include <sys/ioctl.h> int main() { // 1. Create Raw Packet Socket to capture all Ethernet frames int raw_sock = socket(AF_PACKET, SOCK_RAW, htons(ETH_P_ALL)); // 2. Enable Promiscuous Mode on network interface eth0 struct ifreq ifr; strcpy(ifr.ifr_name, "eth0"); ioctl(raw_sock, SIOCGIFFLAGS, &ifr); ifr.ifr_flags |= IFF_PROMISC; ioctl(raw_sock, SIOCSIFFLAGS, &ifr); // 3. Capture and Dissect Raw Ethernet Frame unsigned char buffer[2048]; while (1) { int len = recvfrom(raw_sock, buffer, sizeof(buffer), 0, NULL, NULL); struct ether_header *eth = (struct ether_header *)buffer; printf("Src MAC: %s -> Dst MAC: %s | Protocol: 0x%04X\n", ether_ntoa((struct ether_addr *)eth->ether_shost), ether_ntoa((struct ether_addr *)eth->ether_dhost), ntohs(eth->ether_type)); } }
⚙️ System Call & Execution Workflow
• `AF_PACKET` / `PF_PACKET`: Linux-specific socket domain allowing direct interaction with Layer 2 device drivers, bypassing the standard kernel TCP/IP protocol stack entirely.
• `SOCK_RAW` vs `SOCK_DGRAM`: `SOCK_RAW` provides raw Ethernet frames including L2 header and trailer; `SOCK_DGRAM` provides frames with L2 header stripped.
• Protocol Filter `ETH_P_ALL`: Captures all incoming and outgoing frames (IPv4, ARP, IPv6, STP, VLAN).
• Promiscuous Mode (`IFF_PROMISC`): Instructs the NIC hardware to disable MAC address filtering and deliver all overheard frames on the physical wire to the OS.
💡 Hands-on Insight: Used by network diagnostic tools like Wireshark, tcpdump, and custom IDS packet analysis engines.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 137
🎯 Exam Booster & Review: Linux Raw Sockets
M3.9
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the difference between standard Berkeley sockets (`AF_INET`) and Linux packet sockets (`AF_PACKET`). (6 Marks)
Q: Write a C program using `PF_PACKET` and `SOCK_RAW` to capture Ethernet frames and extract Source and Destination MAC addresses. (8 Marks)
💡 Critical Conceptual Takeaways
✔ `AF_PACKET` gives direct access to Layer 2 raw Ethernet frames.
✔ Promiscuous mode captures all frames on the shared link regardless of destination MAC.
✔ `ETH_P_ALL` captures all Layer 3 protocol payloads.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 138
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 MASTER • MODULE 4 MASTER DECK
Network Management & Physical Layer Fundamentals
Complete Lecture Slides for KTU PCCST501 Computer Networks | Topics M4.1 through M4.6
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 139
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.1
Network Management Architecture & SNMP Protocol
Managing Entities (Managers), Managed Devices (Agents), MIB, SNMP Protocol Operations, SNMPv1 vs SNMPv2c vs SNMPv3 (USM & VACM)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 140
4.1.1 Network Management Framework & SNMP Operations
M4.1 SNMP FRAMEWORK
• Network Management Architecture
Consists of 4 pillars: 1. **Managing Entity (Manager / NMS)**: Centralized workstation running management software. 2. **Managed Devices**: Routers, switches, servers, hosts containing management data. 3. **Management Agent**: Software daemon running inside managed device. 4. **Management Information Base (MIB)**: Virtual database of manageable object variables.
• SNMP Protocol (Simple Network Management Protocol - RFC 3411)
Operates over UDP port 161 (Manager to Agent queries) and UDP port 162 (Agent to Manager asynchronous Traps).
• Core SNMP Protocol Operations
1. **GetRequest**: Manager fetches value of 1 or more MIB variables from Agent. \n 2. **GetNextRequest**: Manager fetches the lexicographically next MIB variable (used for MIB tree walking and table traversal). \n 3. **GetBulkRequest (v2c/v3)**: Fetches large blocks of table rows in a single packet. \n 4. **SetRequest**: Manager sets/modifies configuration value on Agent device. \n 5. **Response**: Agent returns requested data values or error status. \n 6. **Trap / InformRequest**: Unsolicited alert sent by Agent to Manager upon an event (e.g., link failure, reboot). `InformRequest` requires Manager ACK.
SNMP Ports & PDUs
→ UDP Port 161: Agent listener
→ UDP Port 162: Manager Trap listener
→ GetRequest: Read variable
→ SetRequest: Write configuration
→ GetNext: Sequential MIB walk
→ GetBulk: Fast table download
→ Trap: Asynchronous alert
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 141
4.1.2 SNMP Version Evolution: SNMPv1 vs SNMPv2c vs SNMPv3
M4.1 SNMP EVOLUTION
SNMPv1 & SNMPv2c
• Security Model: Plaintext Community Strings (`public` for read-only, `private` for read-write). Vulnerable to packet sniffing
• Operations (v1): Get, GetNext, Set, Response, Trap
• Enhancements (v2c): Adds `GetBulkRequest` for fast table fetching and 64-bit high-capacity counters (`Counter64`), but retains plaintext community security
• Suitability: Isolated, trusted internal LANs only
SNMPv3 (Cryptographically Secure)
• Security Model: User-Based Security Model (USM) + View-Based Access Control Model (VACM)
• Authentication: Message digest authentication via HMAC-MD5 or HMAC-SHA (verifies origin and prevents tampering)
• Confidentiality: Payload encryption via DES or AES-128 / AES-256 (prevents eavesdropping)
• Message Freshness: Timestamps and boot counters prevent Replay attacks
• Enterprise Standard: Mandatory standard for secure network management
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 142
🎯 Exam Booster & Review: Network Management & SNMP
M4.1
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the four components of the Network Management architecture (Manager, Agent, MIB, SNMP) with a neat diagram. (7 Marks)
Q: Describe the various SNMP protocol operations (GetRequest, GetNextRequest, GetBulkRequest, SetRequest, Trap, InformRequest). (8 Marks)
Q: Compare SNMPv1, SNMPv2c, and SNMPv3 with focus on the User-Based Security Model (USM) in SNMPv3. (7 Marks)
💡 Critical Conceptual Takeaways
✔ SNMP uses UDP port 161 for synchronous polling and port 162 for asynchronous event Traps.
✔ SNMPv2c introduced `GetBulk` and 64-bit counters; SNMPv3 added cryptographic authentication and AES encryption.
✔ `InformRequest` provides reliable delivery of trap notifications with manager acknowledgments.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 143
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.2
Structure of Management Information (SMI) & ASN.1
Abstract Syntax Notation One (ASN.1), SMIv2 Macro Definitions, MIB OID Tree Hierarchy (1.3.6.1.2.1), Standard MIB-II Groups, BER Encoding
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 144
4.2.1 SMIv2 & MIB Object Identifier (OID) Tree Hierarchy
M4.2 SMI & MIB HIERARCHY
• SMI (Structure of Management Information - RFC 2578)
The formal language defining the rules for naming, specifying data types, and structuring management objects in the MIB.
• ASN.1 (Abstract Syntax Notation One)
A formal notation for describing data structures independently of machine hardware architectures. Defines primitives (INTEGER, OCTET STRING, OBJECT IDENTIFIER, SEQUENCE).
• Globally Unique OID Tree Hierarchy
Every manageable variable is assigned a globally unique dot-delimited Object Identifier (OID) arranged in an inverted tree:
• Standard Internet MIB-2 Path
`iso(1)` -> `org(3)` -> `dod(6)` -> `internet(1)` -> `mgmt(2)` -> `mib-2(1)` = **`1.3.6.1.2.1`**.
• Standard MIB-II Functional Groups
1. `system (1.3.6.1.2.1.1)`: Device name, description, uptime, contact. \n 2. `interfaces (1.3.6.1.2.1.2)`: Subnet interfaces, MTU, speed, packet counters. \n 3. `ip (1.3.6.1.2.1.4)`: IP routing tables, forward state, TTL, packet discards. \n 4. `tcp (1.3.6.1.2.1.6)`: Active TCP connection table, current connections, timeouts. \n 5. `udp (1.3.6.1.2.1.7)`: UDP listener table and datagram counters.
• Basic Encoding Rules (BER)
Transfers data over wire using **TLV format**: `Tag (Type)` | `Length` | `Value`.
Standard MIB-2 Groups
→ 1.3.6.1.2.1.1: system
→ 1.3.6.1.2.1.2: interfaces
→ 1.3.6.1.2.1.4: ip
→ 1.3.6.1.2.1.6: tcp
→ 1.3.6.1.2.1.7: udp
→ 1.3.6.1.2.1.11: snmp
→ Encoding: BER TLV format
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 145
🎯 Exam Booster & Review: SMI & ASN.1
M4.2
📚 KTU High-Yield Questions (K2 Understand)
Q: Explain the role of SMI and ASN.1 in SNMP network management. (6 Marks)
Q: Illustrate the MIB Object Identifier (OID) tree hierarchy from Root to MIB-II (`1.3.6.1.2.1`) and describe the primary MIB-II groups (`system`, `interfaces`, `ip`, `tcp`). (8 Marks)
Q: Explain Basic Encoding Rules (BER) and the Tag-Length-Value (TLV) encoding format with an example. (6 Marks)
💡 Critical Conceptual Takeaways
✔ SMI defines how MIB data objects are formally defined using ASN.1 syntax.
✔ OID `1.3.6.1.2.1` is the root prefix for all standard Internet MIB-II management objects.
✔ BER encodes variables into machine-independent Tag-Length-Value (TLV) binary streams.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 146
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.3
Data and Signals: Theoretical Channel Capacity
Analog vs Digital Signals, Bandwidth, Transmission Impairments (Attenuation, Noise), Signal-to-Noise Ratio (SNR), Nyquist Rate vs Shannon Capacity
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 147
4.3.1 Signals, Bandwidth & Transmission Impairments
M4.3 DATA & SIGNALS
• Analog vs Digital Signals
Analog signals have infinitely many continuous values over time (e.g., sine wave $s(t) = A \sin(2\pi f t + \phi)$). Digital signals have discrete discrete levels (e.g., 0V and 5V pulses representing bits 0 and 1).
• Bandwidth ($B$)
The range of frequencies contained in a composite signal: $B = f_{max} - f_{min}$ Hertz (Hz).
• Transmission Impairments
1. **Attenuation**: Loss of signal energy over distance (measured in decibels $dB = 10 \log_{10} (P_2 / P_1)$). Corrected via amplifiers/repeaters. \n 2. **Distortion**: Different frequency components travel at different speeds, altering composite waveform shape. \n 3. **Noise**: Unwanted external energy added to signal (Thermal noise $N_0 = kTB$, Induced noise, Crosstalk, Impulse noise).
• Signal-to-Noise Ratio (SNR)
Ratio of signal power to noise power: $SNR = \frac{P_{signal}}{P_{noise}}$. In decibels: $SNR_{dB} = 10 \log_{10} (SNR)$ (e.g., $SNR = 1000 \implies SNR_{dB} = 30$ dB).
Key Formulas
→ Bandwidth: B = f_max - f_min (Hz)
→ Decibels: dB = 10 * log10(P2 / P1)
→ SNR = P_signal / P_noise
→ SNR_dB = 10 * log10(SNR)
→ SNR = 10^(SNR_dB / 10)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 148
4.3.2 Channel Capacity Limits: Nyquist vs Shannon
M4.3 NYQUIST VS SHANNON
Nyquist Bit Rate (Noiseless Channel)
• Formulated By: Harry Nyquist (1928)
• Channel Condition: Assumes theoretical **noiseless** channel with bandwidth $B$ Hz and $L$ discrete signaling levels
• Formula: $C = 2 \times B \times \log_2 (L)$ bps
• Implication: Data rate can be increased indefinitely by increasing the number of signal levels $L$, but is constrained by noise in practice
Shannon Capacity (Noisy Channel)
• Formulated By: Claude Shannon (1948)
• Channel Condition: Assumes real-world channel contaminated with Thermal White Noise (Gaussian Noise)
• Formula: $C = B \times \log_2 (1 + SNR)$ bps
• Implication: Defines the absolute physical upper bound on error-free channel capacity regardless of how many signal levels $L$ are used
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 149
4.3.3 Worked KTU Numerical: Nyquist & Shannon Capacity
M4.3 CAPACITY NUMERICAL
📌 KTU Numerical Problem Statement
A telephone line has bandwidth B = 3000 Hz and Signal-to-Noise ratio SNR_dB = 31.62 dB (SNR approx 1452). (a) Calculate the theoretical maximum Shannon channel capacity. (b) To achieve this capacity on a noiseless line with B = 3000 Hz, how many signal levels L are required by Nyquist formula?
📐 Governing Formulas & Principles:
• Shannon Capacity: C = B * log2(1 + SNR) bps
• Given SNR_dB = 31.62 dB -> SNR = 10^(31.62 / 10) = 10^3.162 = 1452.1
• Nyquist Bit Rate: C = 2 * B * log2(L) bps -> log2(L) = C / (2 * B) -> L = 2^(C / 2B).
📝 Step-by-Step Derivation & Solution
Step 1: 1 + SNR = 1 + 1452.1 = 1453.1
Step 2: log2(1453.1) = log10(1453.1) / log10(2) = 3.1623 / 0.30103 = 10.505 bits
Step 3: Shannon Capacity C = 3000 Hz * 10.505 = 31,515 bps (approx 31.5 kbps).
Step 4: Equating to Nyquist: 31,515 = 2 * 3000 * log2(L) = 6000 * log2(L)
Step 5: log2(L) = 31,515 / 6000 = 5.2525 -> L = 2^5.2525 = 38.12 -> L = 38 signal levels.
✅ FINAL ANSWER: Shannon Capacity C = 31.5 kbps | Required Nyquist signal levels L = 38
💡 Exam Tip: Shannon determines the upper capacity limit; Nyquist tells us how many signal levels L are required to realize it.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 150
🎯 Exam Booster & Review: Channel Capacity & Signals
M4.3
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain the three transmission impairments: Attenuation, Distortion, and Noise with diagrams and formulas. (7 Marks)
Q: State and derive the Nyquist Bit Rate formula for noiseless channels and Shannon Capacity theorem for noisy channels. (8 Marks)
Q: A channel has bandwidth B = 4 kHz. Calculate Shannon capacity if SNR_dB = 20 dB. (5 Marks)
💡 Critical Conceptual Takeaways
✔ Nyquist bit rate ($2B \log_2 L$) applies to ideal noiseless channels.
✔ Shannon capacity ($B \log_2(1+SNR)$) establishes the fundamental thermodynamic limit of noisy channels.
✔ Decibels convert logarithmic power ratios into simple additive terms.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 151
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.4
Digital Transmission & Line Coding Schemes
Line Coding Criteria (DC, Sync, Baseline Wander), Unipolar, Polar (NRZ, RZ, Manchester, Diff Manchester), Bipolar (AMI), Block Coding (4B/5B), PCM & DM
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 152
4.4.1 Line Coding Design Criteria & Characteristics
M4.4 LINE CODING CRITERIA
• Line Coding Definition
The process of converting a sequence of digital bits (1s and 0s) into a discrete electrical/optical signal waveform for baseband transmission.
• Key Line Coding Design Criteria
1. **Signal Level vs Data Level**: Number of voltage states ($L$) vs bit values. \n 2. **DC Component**: Frequencies around 0 Hz create heat, cannot pass through transformers/capacitors, and waste transmitter power. Desirable = Zero DC. \n 3. **Self-Synchronization**: Signal transitions (edges) must allow receiver clock to synchronize timing, especially during long strings of consecutive 0s or 1s. \n 4. **Baseline Wander**: Running average of signal voltage must remain constant to maintain accurate decision slicing threshold. \n 5. **Error Detection**: Built-in coding violations indicate physical link errors.
• Pulse Code Modulation (PCM)
Digitizes analog signals in 3 steps: 1. **Sampling** (Nyquist Rate $f_s \ge 2 f_{max}$), 2. **Quantization** (approximates sample amplitudes to discrete levels; introduces Quantization Error), 3. **Encoding** (maps quantized levels into $n$-bit binary codewords: Bit Rate $= n \times f_s$).
Line Coding Goals
→ Eliminate DC components
→ Provide self-synchronization
→ Prevent baseline wander
→ Minimize bandwidth needs
→ PCM: Sample -> Quantize -> Encode
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 153
4.4.2 Major Line Coding Schemes Comparison
M4.4 SCHEMES COMPARISON
Unipolar & Polar NRZ
• Unipolar NRZ: Bit 1 = Positive voltage $+V$, Bit 0 = Zero 0V. Severe DC component; no synchronization on long 0s/1s
• Polar NRZ-L (Level): Bit 1 = Negative $-V$, Bit 0 = Positive $+V$. Sensitive to polarity inversion
• Polar NRZ-I (Invert): Bit 1 = Transition at start of bit interval; Bit 0 = No transition. Immune to polarity inversion, but fails on consecutive 0s
Biphase: Manchester & Differential Manchester
• Manchester (IEEE 802.3): Mid-bit transition: Bit 1 = High-to-Low transition; Bit 0 = Low-to-High transition. Perfect clock synchronization and Zero DC component, but doubles bandwidth requirement ($2 \times$ baud rate)
• Differential Manchester (Token Ring): Always transitions in the middle for clocking. Bit 0 = Transition at start of bit interval; Bit 1 = No transition at start. Highly robust against wire twists
Bipolar AMI & Multilevel
• Bipolar AMI: Bit 0 = Zero 0V; Bit 1 = Alternating positive $+V$ and negative $-V$. Zero DC component, low bandwidth, but loses sync on long 0s (solved via B8ZS/HDB3 scrambling)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 154
🎯 Exam Booster & Review: Digital Transmission & Line Coding
M4.4
📚 KTU High-Yield Questions (K3 Apply)
Q: Draw the line coding waveforms for the bit stream `10110001` using: (a) Unipolar NRZ, (b) NRZ-L, (c) NRZ-I, (d) Manchester, (e) Differential Manchester, (f) Bipolar AMI. (9 Marks)
Q: Explain the working of Pulse Code Modulation (PCM) with Sampling Theorem ($f_s \ge 2f_{max}$), Quantization, and Encoding. (8 Marks)
Q: What is the DC component problem and baseline wander in digital transmission? (5 Marks)
💡 Critical Conceptual Takeaways
✔ Manchester coding guarantees a transition in every single bit cell for foolproof clock synchronization.
✔ Differential Manchester transitions at the start for bit 0, and has no start transition for bit 1.
✔ PCM digitizes voice signals at 8000 samples/sec $\times$ 8 bits/sample = 64 kbps (standard DS0 channel).
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 155
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.5
Analog Transmission & Bandwidth Utilization (Multiplexing)
Digital-to-Analog Modulation (ASK, FSK, PSK, QAM), Multiplexing Techniques (FDM, WDM, Synchronous vs Statistical TDM), Spread Spectrum (FHSS, DSSS)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 156
4.5.1 Digital Modulation Schemes: ASK vs FSK vs PSK vs QAM
M4.5 MODULATION SCHEMES
ASK, FSK & PSK
• ASK (Amplitude Shift Keying / BASK): Bit 1 = High amplitude carrier $A_1 \cos(2\pi f_c t)$; Bit 0 = Low amplitude $A_2$ (or 0 in OOK). Susceptible to noise
• FSK (Frequency Shift Keying / BFSK): Bit 1 = Frequency $f_1$; Bit 0 = Frequency $f_2$. Robust against amplitude noise; requires higher bandwidth
• PSK (Phase Shift Keying / BPSK & QPSK): BPSK: Bit 1 = $0^\circ$ phase, Bit 0 = $180^\circ$ phase. QPSK: 2 bits per baud ($00, 01, 10, 11$) using 4 orthogonal phases ($45^\circ, 135^\circ, 225^\circ, 315^\circ$)
QAM (Quadrature Amplitude Modulation)
• Concept: Combines Amplitude Modulation (ASK) and Phase Modulation (PSK) simultaneously to maximize spectral efficiency
• 16-QAM & 64-QAM: 16-QAM encodes 4 bits/symbol ($2^4 = 16$ constellation points); 64-QAM encodes 6 bits/symbol; 256-QAM encodes 8 bits/symbol
• Constellation Diagrams: Visualizes constellation constellation points in In-Phase ($I$) and Quadrature ($Q$) 2D plane
• Applications: Wi-Fi (802.11ac/ax), 4G/5G LTE, Cable modems (DOCSIS)
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 157
4.5.2 Multiplexing: FDM vs WDM vs Synchronous TDM vs Statistical TDM
M4.5 MULTIPLEXING TAXONOMY
Frequency & Optical Multiplexing
• FDM (Frequency-Division Multiplexing): Divides total analog bandwidth into distinct frequency channels separated by **Guard Bands** (e.g., FM radio, cable TV)
• WDM (Wavelength-Division Multiplexing): Optical analog of FDM. Combines multiple laser light beams of different wavelengths (e.g., 1550 nm, 1310 nm) onto a single optical fiber using diffraction prisms. DWDM handles 80+ channels
Time-Division Multiplexing (TDM)
• Synchronous TDM: Time divided into fixed recurring frames containing dedicated slots allocated round-robin to each input line. Slot wasted if an input line is idle
• Statistical TDM (Asynchronous): Dynamically allocates time slots **on demand** only to active lines transmitting data. Eliminates idle slot waste by adding channel address headers to each slot
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 158
🎯 Exam Booster & Review: Analog Transmission & Multiplexing
M4.5
📚 KTU High-Yield Questions (K3 Apply)
Q: Explain Quadrature Amplitude Modulation (QAM) and draw the constellation diagrams for 4-QAM and 16-QAM. (8 Marks)
Q: Compare Synchronous TDM and Statistical TDM with framing and slot allocation diagrams. (7 Marks)
Q: Explain Spread Spectrum techniques: Frequency Hopping Spread Spectrum (FHSS) vs Direct Sequence Spread Spectrum (DSSS). (7 Marks)
💡 Critical Conceptual Takeaways
✔ QAM modulates both amplitude and phase to pack multiple bits into a single baud symbol.
✔ FDM shares bandwidth in frequency; TDM shares bandwidth in time slots.
✔ Statistical TDM dynamically allocates slots on demand, achieving much higher link utilization than Synchronous TDM.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 159
PCCST501 Computer Networks | KTU 2024 Scheme • MODULE 4 • M4.6
Physical Transmission Media
Guided Media (Twisted Pair UTP/STP, Coaxial Cable, Fiber Optics SMF/MMF), Unguided Wireless (Radio Waves, Microwaves, Infrared)
Prepared by: Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Viswajyothi College of Engineering and Technology (VJCET), Vazhakulam • KTU S5 CSE
KTU B.Tech Curriculum
Official Classroom Slide Deck

## Slide 160
4.6.1 Guided Media: Twisted Pair vs Coaxial vs Optical Fiber
M4.6 GUIDED MEDIA
Twisted-Pair & Coaxial Cable
• Twisted-Pair (UTP / STP): Two insulated copper wires twisted together to cancel electromagnetic interference (crosstalk). Cat 5e (100 MHz, 1 Gbps), Cat 6 (250 MHz, 10 Gbps up to 55m), Cat 6a (500 MHz, 10 Gbps 100m). Terminated with RJ-45 connectors
• Coaxial Cable: Central copper core surrounded by dielectric insulator, metallic braided shield, and outer jacket. 10Base5 (Thicknet, 500m), 10Base2 (Thinnet, 185m), RG-59 (Cable TV). Terminated with BNC connectors
Optical Fiber (Total Internal Reflection)
• Physics Principle: Light pulses propagate via Total Internal Reflection inside glass core (refractive index $n_1$) surrounded by cladding ($n_2 < n_1$) when incident angle exceeds critical angle
• Multimode Step-Index: Multiple light rays reflect abruptly at core-cladding boundary; causes modal dispersion (short distances)
• Multimode Graded-Index: Core refractive index decreases gradually outward; light rays curve smoothly, reducing modal dispersion
• Single-Mode Fiber (SMF): Ultra-narrow core (8-10 $\mu$m); single light ray propagates straight; zero modal dispersion; enables 100+ km long-haul backbone links
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 161
4.6.2 Unguided Media: Wireless Electromagnetic Spectrum
M4.6 UNGUIDED WIRELESS
• Radio Waves (3 kHz to 1 GHz)
Omnidirectional radiation pattern (transmitting antenna broadcasts signals in all directions). Penetrates physical walls effortlessly. Subject to multi-path interference. Used in AM/FM radio and cordless phones.
• Microwaves (1 GHz to 300 GHz)
Unidirectional, Line-of-Sight propagation. Focused beam using parabolic dish or horn antennas. Cannot penetrate solid obstacles (walls, hills). Used in cellular networks, satellite communications, and GPS.
• Infrared Waves (300 GHz to 400 THz)
High-frequency, short-range line-of-sight communication. Completely blocked by walls and solid obstacles (ensures indoor security without room-to-room interference). Used in TV remote controls and IrDA devices.
Wireless Spectrum
→ Radio: Omnidirectional (Wall penetration)
→ Microwaves: Line-of-sight (Dish antenna)
→ Infrared: Short range (Blocked by walls)
→ Satellite: Geosynchronous (36,000 km)
→ Fiber: Total Internal Reflection
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET

## Slide 162
🎯 Exam Booster & Review: Transmission Media
M4.6
📚 KTU High-Yield Questions (K2 Understand)
Q: Compare Step-Index Multimode, Graded-Index Multimode, and Single-Mode optical fibers with refractive index profiles and light propagation paths. (8 Marks)
Q: Compare Twisted-Pair Cable, Coaxial Cable, and Optical Fiber across bandwidth, attenuation, EMI immunity, and cost. (7 Marks)
Q: Differentiate between Radio waves, Microwaves, and Infrared wireless media. (6 Marks)
💡 Critical Conceptual Takeaways
✔ Optical fibers provide immense bandwidth, zero EMI susceptibility, and ultra-low attenuation.
✔ Single-mode fiber eliminates modal dispersion for high-speed long-distance backbones.
✔ Microwaves require line-of-sight parabolic antennas; Infrared is safely contained by room walls.
PCCST501 Computer Networks | KTU 2024 Scheme | Prof. Anju Markose | Assistant Professor, Dept. of CSE | VJCET
Dept. of CSE, VJCET